Contact Information
- Stephan Heinemann
- SMS: +1 (250) 891-5446
- Email: stephan.heinemann@hotmail.com
- Bookings, Questions

---
Flight for Range and Endurance
- Review Straight and Level Flight
- Definition and Motivation
- Flight for Range
  - Diagrams, Maximum Range (Experimental)
- Flight for Endurance
  - Diagrams, Maximum Endurance (Experimental)
- Summary and Questions
- Pre-Flight Briefing
[Speaker Notes: - gear and carburetor heat are not applicable]

---
Review Straight and Level Flight
- Attitude plus power equals performance!
- Mentally perform a power reduction from the cruise power setting while maintaining straight and level flight.
- What effect does the power reduction have on the airspeed and the fuel consumption?
- What effect does the power reduction have on the estimated time of arrival?
[Speaker Notes: Until what point can the power be reduced while maintaining straight and level flight?]

---
Definition and Motivation
- Airspeed and fuel flow can be traded off
- Range – achievable distance per fuel unit (air versus ground range): destinations, alternates
- Endurance – achievable time per fuel unit: holding or orbiting procedures, cockpit management / decision making, economy
- Maximum range – best achievable distance
- Maximum endurance – best achievable time
[Speaker Notes: BSFC = FF / BHP = FF n / Pa]

---
        Cruise Performance
        POH Section 5
- Consider conditions
- Select pressure altitude
- Select temperature
- Select power setting
- Interpolate as required
- Determine airspeed and fuel flow
[Speaker Notes: The diagram shows % maximum cruise power (power available) at different pressure altitudes. Since power available decreases with altitude due to decreasing thrust available even at increasing TAS, the absolute power associated with the stated % power available decreases. The drag and thrust required at constant CAS remain constant with increasing altitude and increasing TAS. Power required increases with altitude due to the increasing TAS. To maintain the required thrust and constant CAS, higher RPM is required at higher density altitudes due to reduced propeller efficiency. Both engine (combustion) and propeller efficiency are reduced at higher density altitudes (for normally aspirated engines). Mixture is leaned with density altitude and results in a constant fuel flow at reduced absolute power. Consequently, the fuel consumption per unit of power (BSFC) decreases slightly with altitude. Derive power curve from table! 2550 - 118 2500 - 115 : 3 2400 - 110 : 5 (non-linear) 2300 - 104 : 6 (best range) 2100 - 97 : 7 (linear) 2000 - 90 : 7 Tested (approx. ISA 5500 ASL): 2300 → 109 KIAS, 8 GPH 2200 → 100 KIAS, 7 GPH 2100 → 90 KIAS, 6 GPH 2000 → 81 KIAS, 5 GPH 1900 → 75 KIAS, 4 GPH]

---
Flight for Endurance
Power Required
        D * V
(Drag * Velocity)
Min Power: Max Endurance
[Speaker Notes: - Experimental Method - POH - Mixture, Flaps, Altitude (Factors → Turbulence) - Reduced Control Response - SL for reciprocating engines (air density) - Total Drag = Thrust Required (Force) D = F - F = m * a [N = kg*m/s²] - P = W / t = F * s / t = F * V → P = D * V - [N * m / s = kg * m / s² * m / s = kg * m² / s³ = W] (Power = Total Drag * Velocity)]

---
        Endurance Profile
        POH Section 5
- Consider conditions
- Select pressure altitude
- Select power setting
- Determine endurance
- Endurance decreases slightly for given % of power available
- Specific fuel consumption (SFC) increases slightly with altitude for power-rated engines (piston-propeller)
[Speaker Notes: - put cruise power table next to it… To maintain level flight, CAS has to be maintained or AoA has to be increased. TAS increases to compensate decreasing air density. With constant thrust (drag) at constant CAS, the power required increases due to increasing TAS. The power available, however, decreases with decreasing thrust available being the dominant factor compared to TAS due to propeller efficiency, engine (combustion) efficiency and RPM limits. The graph shows % available cruise power. Since power available decreases with decreasing thrust available even at increasing TAS, the absolute power for % available cruise power decreases. If the graph shows decreasing absolute powers with altitude, then the product of thrust available and TAS decreases with altitude. Since TAS increases with altitude, thrust available decreases more in comparison. If CAS cannot be kept constant, then the AoA (lift coefficient) has to be increased to maintain level flight. The fuel flow for a % available cruise power remains approximately constant. The fuel consumption per unit of power (BSFC) therefore must approximately increase accordingly. - review carefully: %HP may not be constant - power available decreases with altitude (less thrust available) - power required increases with altitude (increased TAS) - SFC remains almost constant - same %HP reveals same fuel flow - FF = SFC * P → SFC constant - why does endurance decrease with altitude? - if power available decreases with altitude so does %HP as a value giving reduced set power - %HP of maximum cruise power (available) - power required increases]

---
Flight for Maximum Endurance (Experimental)
- Reduce power in 100 RPM steps maintaining level flight with stable airspeed steps and trim
- Unstable decreasing airspeed indicates slow flight range – more power required
- Accelerate to cruise airspeed and then decrease power to slightly higher than last stable setting to compensate for turbulence and possible required turns
- Lean mixture as recommended
- Notice reduced control responses due to reduced airflow
[Speaker Notes: www.eaa1000.av.org/technicl/perfspds/perfspds.htm - approximately 1700 RPM for max. endurance - T = F / FF, D = T * GS Familarization Demo ? - 1700 RPM → 3 GPH → 80 KIAS 30 USG → 10 H → 800 NM Different Environment: - 1800 RPM → 4 GPH, 65 KIAS 40 USG → 10 H → 650 NM 20 USG → 5 H →325 NM Leaning is key for this exercise!]

---
Leaning
- Slowly turn mixture knob out / anticlockwise until a drop in RPM can be observed
- Turn the mixture knob back in / clockwise until the RPM has increased again (2-3 turns)
- Check fuel flow and exhaust gas temperature (50°F below peak EGT)

---
Flight for Range
Power Required
Optimize both power and speed
        D * V
(Drag * Velocity)
Min Drag: Max Endurance
[Speaker Notes: - parasite drag: form, skin friction, interference - induced drag, wave drag (trans-/supersonic) - thrust curve: jet aircraft - power curve: propeller aircraft (reciprocating engine) - engine and propeller efficiency - Experimental Method - POH - Wind, Mixture, Altitude (Factors) - Power (W) = Force (N) * Distance (m) / Time (s) = Force (N) * Velocity (m/s) = Drag (N) * Velocity (m/s) - D = Cd * ½ r * S * v² - P = Cd * ½ r * S * v³]

---
        Range Profile
        POH Section 5
- Consider conditions
- Select pressure altitude
- Select power setting
- Determine range
- Range increases with increasing altitude
- True airspeed (TAS) increases with increasing altitude
[Speaker Notes: - Notice almost linear dependency between power setting and airspeed - Linear dependency will eventually change to a much lower airspeed for a lower power setting - Engine and propeller efficiency decrease with decreasing air density, power cannot be increased to maintain 75% above 10000ft (full throttle)]

---
Flight for Maximum Range
Min Drag
Max Range
D * V
- Increase power in 100 RPM steps until a non-linear increase in airspeed can be observed
- Maintain level flight, trim and lean mixture as recommended (rich of peak)
[Speaker Notes: - airspeed versus ground speed (air range versus ground range) - can be decreased in 100 RPM steps as well - approximately 2000 RPM for max. range Familarization Demo - 2000 RPM → 5 GPH → 100 KIAS 30 USG → 6 H → 600 NM - 2400 RPM → 10 GPH → 120 KIAS 30 USG → 3 H → 360 NM Different Environment (approx. ISA 5500 ASL) - 1900 RPM → 4 GPH, 75 KIAS 40 USG → 10 H → 750 NM 20 USG → 5 H → 375 NM - 2000 RPM → 5 GPH, 81 KIAS 40 USG → 8 H → 648 NM 20 USG → 4 H → 324 NM - 2100 RPM → 6 GPH, 90 KIAS 40 USG → 6.5 H → 585 NM]

---
Range and Endurance – Instruments
Performance
Control
Altitude
Attitude
Power
Airspeed
Throttle
Mixture
EGT / FF
- Control: Attitude, Power → Performance: Airspeed, Altitude
- Mixture → Exhaust Gas Temperature, Fuel Flow

---
Factors Affecting Range and Endurance
- Endurance: fuel available, power setting, flap setting (configuration), weight, center of gravity, air density (altitude, temperature, humidity), contamination, mixture, turbulence
- Range: fuel available, power setting, flap setting (configuration), weight, center of gravity, air density (altitude, temperature, humidity), contamination, mixture, wind (air versus ground range)

---
Summary / Quiz
- Define range, maximum range, endurance and maximum endurance.
- Give examples for when flight for range or endurance is preferable.
- What are the main factors that influence range and endurance and how do they affect them?
- Mentally configure the airplane for best range and endurance and state all required actions, respectively.

---
Pre-Flight Briefing
- Exercise
- Training Area
- Departure and Arrival Procedures
- Weather Briefing / NOTAMs
- Aircraft and Documents
- Time and Fuel Requirements
- Safety Considerations and Responsibilities
[Speaker Notes: - Safety: nose-high, poor forward visibility, engine cooling...]

---
Additional Materials
- Additional materials for Flight for Range and Endurance
- Flight Instructor Guide – Exercise 10, Lesson Plan 4

---
Specific Fuel Consumption
- Jet (thrust specific fuel consumption):
  - TSFC = Fuel Consumption / Unit of Thrust
  - Fuel Flow = TSFC * Thrust
- Propeller (brake specific fuel consumption):
  - BSFC = Fuel Consumption / Unit of Power
  - Fuel Flow = BSFC * Power

---
Maximum Endurance

---
Weight and Endurance

---
Configuration and Endurance

---
Altitude and Endurance

---
Specific Range
- Specific Air Range
  - Air Range = Air Distance / Unit of Fuel
  - SAR = TAS / Fuel Flow
  - Jet: SAR = TAS / TSFC * Thrust Required
  - Propeller: SAR = TAS / BSFC * Power Required
- Specific Ground Range
  - Ground Range = Ground Distance / Unit of Fuel
  - SGR = GS / Fuel Flow
  - Jet: SGR = GS / TSFC * Thrust Required
  - Propeller: SGR = GS / BSFC * Power Required
- Maximum Specific Range
  - Maximize TAS or GS while minimizing SFC

---
Maximum Air Range

---
Weight and Range

---
Configuration and Range

---
Altitude and Range