Contact Information
- Stephan Heinemann
- SMS: +1 (250) 891-5446
- Email: stephan.heinemann@hotmail.com
- Bookings, Questions

---
Stalls
- Definition and Motivation
- Power-Off and Power-On Stalls
- Stalls in Clean and Landing Configuration
- Acceleration, Turning and Departure Stalls (Approach Stalls – Power-On)

---
Review Slow Flight
- Attitude plus power equals performance!
- Mentally enter a slow flight in landing configuration from cruise flight and state all observations and required actions.
- What particular observation applies to the control inputs compared to normal cruise flight?
- Mentally recover from a slow flight in landing configuration and state all observations and required actions.

---
Definition and Motivation
- Lower limit of the slow flight range
- Any angle of attack beyond the critical angle of attack at which any further increase leads to less lift and more drag
- Incipient / Imminent – stall warning, bottom of arc, buffet
- Fully Developed – nose or wing drop
[Speaker Notes: - Stall can happen at any attitude and airspeed]

---
Safety Considerations
- High nose-up attitude maneuver
- Limited forward visibility
- HASEL, lookout ahead and below
- Maintain good lookout during maneuver
- Yaw is to be controlled precisely with rudder
- Remain coordinated at all times

---
Entering a Power-Off Stall
- Reduce power to idle
- Apply elevator back-pressure to increase nose-up attitude controlling yaw with rudder maintaining altitude
- Extend flaps in stages to desired degree in white arc

---
Recovering a Power-Off Stall
- Apply elevator forward pressure to lower the nose
- Apply full power controlling yaw with rudder to remain coordinated
- Retract flaps in stages to up in white arc
- Establish best rate of climb airspeed to regain altitude
- Establish cruise attitude and accelerate to cruise airspeed
- Reduce power to cruise power setting and finally trim
[Speaker Notes: - Break the stall first (lower nose), then apply power - Establish best rate of climb airspeed first during recovery]

---
Entering a Power-On Stall
- Reduce power to low power setting (1500 RPM)
- Apply elevator back-pressure to increase nose-up attitude controlling yaw with rudder maintaining altitude
- Extend flaps in stages to desired degree in white arc

---
Recovering a Power-On Stall
- Apply elevator forward pressure to lower the nose
- Apply full power controlling yaw with rudder to remain coordinated
- Retract flaps in stages to up in white arc
- Establish best rate of climb airspeed to regain altitude
- Establish cruise attitude and accelerate to cruise airspeed
- Reduce power to cruise power setting and finally trim
[Speaker Notes: - Lower stall speed due to power and slipstream - Higher nose-up attitude - More yaw to be controlled - Less effective ailerons - More sudden and abrupt nose (wing) drop]

---
Accelerated Stall
- Secondary Stall
- Higher load factor
- Apprupt elevator back-pressure, gusts

---
Approach Stall
- Power-off / descending turn
- Review angles of attack at inner and outer wing
- Inner wing drop

---
Departure Stall
- Power-on climbing turn
- Review angles of attack at inner and outer wing
- Outer wing drop

---
Incipient Stall

---
Fully Developed Stall

---
Summary / Quiz
- Define slow flight and give examples for when slow flight is applicable.
- Mentally enter a slow flight in landing configuration from cruise flight and state all observations and required actions.
- Mentally perform a turn to the right in slow flight and state all observations and required actions.
- Mentally recover from a slow flight in landing configuration and state all observations and required actions.

---
Pre-Flight Briefing
- Exercise
- Training Area
- Departure and Arrival Procedures
- Weather Briefing / NOTAMs
- Aircraft and Documents