Contact Information
- Stephan Heinemann
- SMS: +1 (250) 891-5446
- Email: stephan.heinemann@hotmail.com
- Bookings, Questions

---
Night Flying
- Review Instrument Flying
- Definition and Motivation
- Night Flying
- Summary and Questions
- Pre-Flight Briefing

---
Review Instrument Flying

---
Definition and Motivation

---
Aircraft and Equipment Requirements
- Interior Lighting – cabin, panel, instruments, screens
- Exterior lighting – beacon, position, landing, taxi, strobe
- Flashlight – reading and backup light, dimmable red

---
Airport Lighting
- Approach – different types depending on category
- Runway – threshold, edge, center, landing zone
- Taxiway – edge, center, protection, holding
- Obstructions – steady, flashing
- ARCAL, Reflectors – check CFS for airport lighting

---
Human Limitations
- Darkness adaptation may take up to 30 min
- Red light helps to preserve adaption
- Strobe, landing and apron lighting may interfere
- Sensory Illusions and vertigo may occur
- Corriolis, head-up, head-down, black hole, autokinetic ...
[Speaker Notes: - leans - graveyard spin/spiral - corriolis - inversion - head-up/down - linear perspective - black hole - autokinetic - fase visual references - vection - pattern]

---
Traffic and Evironment
- Peripheral scanning for effective traffic avoidance
- Strobe and position lights for recognition and orientation
- Inadvertant flight into clouds – maintain VMC at night

---
Taxiing at Night
- Taxi lights on during taxi and off when holding
- Strobe lights remain off before take-off and after landing
- Beacon and position lights remain on at all times
- Follow lighted signs and observe clearance limits
- Blue edge, green and yellow center, red holding lights
- Use light distance as reference for appropriate taxi speed

---
Take-Off at Night
- Sparse references and possible sensory illusions
- Head-up illusion may lead to wrong pitch attitude
- Trust attitude and airspeed indicator during initial climb
- Crosscheck visual references with instruments

---
Approach and Landing at Night
Request appropriate intensity

---
Circuit at Night

---
Cross Country at Night

---
Summary / Quiz

---
Pre-Flight Briefing
- Exercise
- Training Area
- Departure and Arrival Procedures
- Weather Briefing / NOTAMs
- Aircraft and Documents
- Time and Fuel Requirements

---
Night Flying (Ex. 25, LP. )
- Objective
- Review
- Motivation
- Howto
- Summary / Questions
- Preflight Briefing