Contact Information
- Stephan Heinemann
- SMS: +1 (250) 891-5446
- Email: stephan.heinemann@hotmail.com
- Bookings, Questions

---
Forced Landing
- Review Descent, Approach and Landing
- Definition and Motivation
- Forced Landing
- Summary and Questions
- Preflight Briefing

---
Review Descent, Approach and Landing
- Mentally perform a power-off descent and state all observations and required actions.
- What is the best glide airspeed and where do we find it?
- How do we visually determine our glide distance?
- What types of landing can we select?
- Mentally perform a soft-field landing and state all observations and required actions.

---
Definition and Motivation
- Unplanned landing due to failure or other emergency
- Aviate, Navigate, Communicate, Manage
- Continue to fly the airplane has highest priority
- Situations: engine failure (mechanical, oil supply, fuel supply – contamination, air supply – icing, blockage)

---
Engine Failure During Take-Off
Power Idle
Apply Brakes
Best Glide
Avoid Obstacles
- During Take-Off Run: power idle, apply brakes
- Immediately after Take-Off: best glide airspeed (68 KIAS), avoid obstacles
[Speaker Notes: - V1, TODA, ASDA? - if time permits: Fuel Valve Off, Mixture Off, Ignition Off, Master Off]

---
Engine Failure at Low Altitude
- Establish best glide (68 KIAS) and trim
- Select and head towards field
- Seats, Seatbelts
- Fuel Valve - Off, Mixture - Off, Ignition - Off
- Mayday, Squawk 7700, ELT On
- Flaps as required
- Master - Off, Doors – Unlatch
- MEMORIZE THIS PROCEDURE!

---
Engine Failure at Safe Altitude
- Establish best glide (68 KIAS) and trim
- Select and head towards field
- Cause check (Fuel Valve, Fuel Selector, Mixture, Throttle, Engine Instruments, Fuel Pump, Magnetos, Primer)
- Attempt restart
- If restart not successful, continue with low altitude procedures
- MEMORIZE THIS PROCEDURE!
[Speaker Notes: - Carburettor heat if equipped - Alternate air door automatically opens due to suction - Causes: Mechanical, Fuel, Oil, Icing - Safe Altitude: 2000' AGL?]

---
Engine Failure in Circuit
- Perform power-off landing if at circuit altitude
- Anticipate glide and altitude loss for each leg to final
- Inform ATC

---
Forced Landing Approach
- Organize legs according to altitude, rate of descent and wind – lost altitude cannot be regained
- Approach slightly high and attempt to land in first third of the selectd field
- Use flaps and slipping to control rate of descent

---
360° Forced Landing Pattern
- Proceed to key point at altitude – High Key
- Descend to lower altitude circling – Low Key
- Initiate final approach from low key point

---
Communication
- Current frequency or 121.5
- Mayday, Mayday, Mayday
- 3 x Callsign
- Position, Altitude
- Problem
- Intentions
- Callsign
- Squawk 7700, ELT On

---
Hills, Mountains, Forrest, Water
- Land uphill
- Assume top of trees as landing area
- Lookout for roads (traffic, obstructions)
- Ditching procedures (waves, wind)

---
Safety Considerations
Clear engine every 1000'

---
Landing Site Selection – COWLS
- Civilization
- Obstacles
- Wind
- Landing (Take-Off) Area / Length
- Surface
- Landing Type Selection: Normal, Short, Soft, Crosswind

---
High Pass
- Assess overall situation and environment – establish headings
- Number of passes, shape, altitude and airspeed depend on situation
- Overfly landing site on the upwind side for better visibility
- Example: alitude 2000' AGL, airspeed 60 KIAS, flaps 10°
- 60 KIAS → 60 NM/h → 1 NM / min → 100' / s, 10s → 1000' length
- Sufficient evidence to not support landing decision?
[Speaker Notes: - landing path and direction – reasons not to land - stable altitude and airspeed - altitudes, airspeeds and number of passes depend on situation and environment]

---
Low Pass
- Assess details such as obstacles and surface condition
- Number of passes, shape, altitude and airspeed depend on situation
- Trim properly for airspeed and altitude, maintain obstacle clearance
- Overfly landing site on the upwind side for better visibility
- Example: circuit altitude 1000' AGL, airspeed 60 KIAS, flaps 10°
- Sufficient evidence to support landing decision?
[Speaker Notes: - landing site details – reasons to land - surface color: green, brown, black...]

---
Low Approach
- Final assessment of landing site, landing type and approach path and configuration
- Number of approaches, shape, altitude and airspeed depend on situation
- Example: approach speed 60 KIAS, flaps 30°, go-around at 30' AGL
- Configuration according to selected landing type
- Final assessment for landing decision – in favor or against

---
Communication
Inform ATC
Briefings
Checklists
- Inform ATC – Flight Service Station, Flight Planning
- Passenger briefing
- Approach and landing briefing and checklists

---
Safety Considerations
- Maintain a safe airspeed
- Maintain a safe height (obstacle clearance)
- Maintain a good lookout
- Turn accurately and coordinated
- Anticipate turns and compensate drift on legs
- Do not overbank or skid

---
Summary / Quiz
- What situations may lead to a precautionary landing?
- Explain the acronym COWLS.
- Mentally perform a precautionary landing due to deteriorating weather on a grass field. State all observations and actions.
- What role plays proper communication when deciding for a precautionary landing?

---
Pre-Flight Briefing
- Exercise
- Training Area
- Departure and Arrival Procedures
- Weather Briefing / NOTAMs
- Aircraft and Documents

---
Precautionary Landing (Ex. 21, LP. 24)
- Objective
- Review
- Motivation
- Howto
- Summary / Questions
- Preflight Briefing