Contact Information
- Stephan Heinemann
- SMS: +1 (250) 891-5446
- Email: stephan.heinemann@hotmail.com
- Bookings, Questions

---
Flight for Range and Endurance
- Review Straight and Level Flight
- Definition and Motivation
- Flight for Range
  - Diagrams, Maximum Range (Experimental)
- Flight for Endurance
  - Diagrams, Maximum Endurance (Experimental)
- Summary and Questions
- Pre-Flight Briefing
[Speaker Notes: - gear and carbutettor heat are not applicable]

---
Review Straight and Level Flight
- Attitude plus power equals performance!
- Mentally perform a power reduction from the cruise power setting while maintaining straight and level flight.
- What effect does the power reduction have on the airspeed and the fuel consumption?
- What effect does the power reduction have on the estimated time of arrival?
[Speaker Notes: Until what point can the power be reduced while maintaining straight and level flight?]

---
Definition and Motivation
- Airspeed and fuel flow can be traded off
- Range – achievable distance per fuel unit (air versus ground range): destinations, alternates
- Endurance – achievable time per fuel unit: holding or orbiting procedures, cockpit management / decision making, economy
- Maximum range – best achievable distance
- Maximum endurance – best achievable time
[Speaker Notes: SFC = FF / BHP = FF n / Pa]

---
        Cruise Performance
        POH Section 5
- Consider conditions
- Select pressure altitude
- Select temperature
- Select power setting
- Interpolate as required
- Determine airspeed and fuel flow
[Speaker Notes: Derive power curve from table! 2550 - 118 2500 - 115 : 3 2400 - 110 : 5 (non-linear) 2300 - 104 : 6 (best range) 2100 - 97 : 7 (linear) 2000 - 90 : 7 Tested (approx. ISA 5500 ASL): 2300 → 109 KIAS, 8 GPH 2200 → 100 KIAS, 7 GPH 2100 → 90 KIAS, 6 GPH 2000 → 81 KIAS, 5 GPH 1900 → 75 KIAS, 4 GPH]

---
Flight for Endurance
Power Required
        D * V
(Drag * Velocity)
Min Power: Max Endurance
[Speaker Notes: - Experimental Method - POH - Mixture, Flaps, Altitude (Factors → Turbulence) - Reduced Control Response - SL for reciprocating engines (air density) - Total Drag = Thrust Required (Force) D = F - F = m * a [N = kg*m/s²] - P = W / t = F * s / t = F * V → P = D * V - [N * m / s = kg * m / s² * m / s = kg * m² / s³ = W] (Power = Total Drag * Velocity)]

---
        Endurance Profile
        POH Section 5
- Consider conditions
- Select pressure altitude
- Select power setting
- Determine endurance
- Endurance decreases slightly with altitude for power-rated engines
- Specific fuel consumption (SFC) increases slightly with altitude for power-rated engines (piston-propeller)
[Speaker Notes: - put cruise power table next to it… - review carefully: %HP may not be constant - power available changes with altitude - power required changes with altitude - SFC remains almost constant - same %HP reveals same fuel flow - FF = SFC * P → SFC constant - why does endurance decrease with altitude? - if power available decreases with altitude so does %HP as a value giving reduced set power - %HP of maximum cruise power (available) - power required increases]

---
Flight for Maximum Endurance (Experimental)
- Reduce power in 100 RPM steps maintaining level flight with stable airspeed steps and trim
- Unstable decreasing airspeed indicates slow flight range – more power required
- Accelerate to cruise airspeed and then decrease power to slightly higher than last stable setting to compensate for turbulence and possible required turns
- Lean mixture as recommended
- Notice reduced control responses due to reduced airflow
[Speaker Notes: www.eaa1000.av.org/technicl/perfspds/perfspds.htm - approximately 1700 RPM for max. endurance - T = F / FF, D = T * GS Familarization Demo ? - 1700 RPM → 3 GPH → 80 KIAS 30 USG → 10 H → 800 NM Different Environment: - 1800 RPM → 4 GPH, 65 KIAS 40 USG → 10 H → 650 NM 20 USG → 5 H →325 NM Leaning is key for this exercise!]

---
Leaning
- Slowly turn mixture knob out / anticlockwise until a drop in RPM can be observed
- Turn the mixture knob back in / clockwise until the RPM has increased again (2-3 turns)
- Check fuel flow and exhaust gas temperature (50°F below peak EGT)

---
Endurance - Instruments
Performance
Control
Altitude
Attitude
Power
Airspeed
Throttle
EGT / FF
Mixture
- Attitude, Power → Airspeed (approximately 60 KIAS), Altitude
- Mixture → Exhaust Gas Temperature, Fuel Flow
[Speaker Notes: www.eaa1000.av.org/technicl/perfspds/perfspds.htm]

---
Flight for Range
Power Required
Optimize both power and speed
        D * V
(Drag * Velocity)
Min Drag: Max Endurance
[Speaker Notes: - parasite drag: form, skin friction, interference - induced drag, wave drag (trans-/supersonic) - thrust curve: jet aircraft - power curve: propeller aircraft (reciprocating engine) - engine and propeller efficiency - Experimental Method - POH - Wind, Mixture, Altitude (Factors) - Power (W) = Force (N) * Distance (m) / Time (s) = Force (N) * Velocity (m/s) = Drag (N) * Velocity (m/s) - D = Cd * ½ r * S * v² - P = Cd * ½ r * S * v³]

---
        Range Profile
        POH Section 5
- Consider conditions
- Select pressure altitude
- Select power setting
- Determine range
- Range increases with increasing altitude
- True airspeed (TAS) increases with increasing altitude
[Speaker Notes: - Notice almost linear dependency between power setting and airspeed - Linear dependency will eventually change to a much lower airspeed for a lower power setting - Engine and propeller efficiency decrease with decreasing air density, power cannot be increased to maintain 75% above 10000ft (full throttle)]

---
Flight for Maximum Range
Min Drag
Max Range
D * V
- Increase power in 100 RPM steps until a non-linear increase in airspeed can be observed
- Maintain level flight, trim and lean mixture as recommended (rich of peak)
[Speaker Notes: - airspeed versus ground speed (air range versus ground range) - can be decreased in 100 RPM steps as well - approximately 2000 RPM for max. range Familarization Demo - 2000 RPM → 5 GPH → 100 KIAS 30 USG → 6 H → 600 NM - 2400 RPM → 10 GPH → 120 KIAS 30 USG → 3 H → 360 NM Different Environment (approx. ISA 5500 ASL) - 1900 RPM → 4 GPH, 75 KIAS 40 USG → 10 H → 750 NM 20 USG → 5 H → 375 NM - 2000 RPM → 5 GPH, 81 KIAS 40 USG → 8 H → 648 NM 20 USG → 4 H → 324 NM - 2100 RPM → 6 GPH, 90 KIAS 40 USG → 6.5 H → 585 NM]

---
Range – Instruments
Performance
Control
Altitude
Attitude
Power
Airspeed
Throttle
Mixture
EGT / FF
- Attitude, Power → Airspeed (approximately 80 KIAS), Altitude
- Mixture → Exhaust Gas Temperature, Fuel Flow

---
Factors Affecting Range and Endurance
- Endurance: fuel available, power setting, flap setting (configuration), weight, center of gravity, air density (altitude, temperature, humidity), contamination, mixture, turbulence
- Range: fuel available, power setting, flap setting (configuration), weight, center of gravity, air density (altitude, temperature, humidity), contamination, mixture, wind (air versus ground range)

---
Summary / Quiz
- Define range, maximum range, endurance and maximum endurance.
- Give examples for when flight for range or endurance is preferable.
- What are the main factors that influence range and endurance and how do they affect them?
- Mentally configure the airplane for best range and endurance and state all required actions, respectively.

---
Pre-Flight Briefing
- Exercise
- Training Area
- Departure and Arrival Procedures
- Weather Briefing / NOTAMs
- Aircraft and Documents
- Time and Fuel Requirements
- Safety Considerations and Responsibilities
[Speaker Notes: - Safety: nose-high, poor forward visibility, engine cooling...]

---
Additional Materials
- Additional materials for flight for range and endurance
- Flight Instructor Guide – Exercise 10, Lesson Plan 4

---
Specific Fuel Consumption
- Jet (thrust specific fuel consumption):
  - TSFC = Fuel Consumption / Unit of Thrust
  - Fuel Flow = TSFC * Thrust
- Propeller (brake specific fuel consumption):
  - BSFC = Fuel Consumption / Unit of Power
  - Fuel Flow = BSFC * Power

---
Maximum Endurance

---
Weight and Endurance

---
Configuration and Endurance

---
Altitude and Endurance

---
Specific Range
- Specific Air Range
  - Air Range = Air Distance / Unit of Fuel
  - SAR = TAS / Fuel Flow
  - Jet: SAR = TAS / TSFC * Thrust Required
  - Propeller: SAR = TAS / BSFC * Power Required
- Specific Ground Range
  - Ground Range = Ground Distance / Unit of Fuel
  - SGR = GS / Fuel Flow
  - Jet: SGR = GS / TSFC * Thrust Required
  - Propeller: SGR = GS / BSFC * Power Required
- Maximum Specific Range
  - Maximize TAS or GS while minimizing SFC

---
Maximum Air Range

---
Weight and Range

---
Configuration and Range

---
Altitude and Range