Contact Information
- Stephan Heinemann
- SMS: +1 (250) 891-5446
- Email: stephan.heinemann@hotmail.com
- Bookings, Questions

---
Flight for Range and Endurance
- Review Straight and Level Flight
- Definition and Motivation
- Flight for Range
  - Diagrams, Maximum Range (Experimental)
- Flight for Endurance
  - Diagrams, Maximum Endurance (Experimental)
- Summary and Questions
- Pre-Flight Briefing
[Speaker Notes: - gear and carbutettor heat are not applicable]

---
Review Straight and Level Flight
- Attitude plus power equals performance!
- Mentally perform a power reduction from the cruise power setting while maintaining straight and level flight.
- What effect does the power reduction have on the airspeed and the fuel consumption?
- What effect does the power reduction have on the estimated time of arrival?
[Speaker Notes: Until what point can the power be reduced while maintaining straight and level flight?]

---
Definition and Motivation
- Airspeed and fuel flow can be traded off
- Range – achievable distance per fuel unit (air/ground range): destinations, alternates
- Endurance – achievable time per fuel unit: holding procedures, cockpit management / decision making, economy
- Maximum range – best achievable distance
- Maximum endurance – best achievable time
[Speaker Notes: SFC = FF / BHP = FF n / Pa]

---
        Cruise Performance
        POH Section 5
- Consider conditions
- Select pressure altitude
- Select temperature
- Select power setting
- Interpolate as required
- Determine airspeed and fuel flow
[Speaker Notes: Derive power curve from table! 2550 - 118 2500 - 115 : 3 2400 - 110 : 5 (non-linear) 2300 - 104 : 6 (best range) 2100 - 97 : 7 (linear) 2000 - 90 : 7]

---
Flight for Endurance
Power Required
Min Power
Max Endurance
D * V
[Speaker Notes: - Experimental Method - POH - Mixture, Flaps, Altitude (Factors → Turbulence) - Reduced Control Response - SL for reciprocating engines (air density)]

---
        Endurance Profile
        POH Section 5
- Consider conditions
- Select pressure altitude
- Select power
- Determine endurance
[Speaker Notes: - put cruise power table next to it...]

---
Flight for Maximum Endurance (Experimental)
- Reduce power in 100 RPM steps maintaining level flight with stable airspeed and trim
- Unstable decreasing airspeed indicates slow flight range – more power required
- Reset cruise power and then decrease power to slightly higher stable setting to compensate for turbulence and required turns
- Lean mixture as recommended
- Notice reduced control responses
[Speaker Notes: www.eaa1000.av.org/technicl/perfspds/perfspds.htm - approximately 1700 RPM for max. endurance Familarization Demo ? - 1700 RPM → 3 GPH → 80 KIAS 30 USG → 10 H → 800 NM]

---
Leaning
- Slowly turn mixture knob out / anticlockwise until a drop in RPM can be observed
- Turn the mixture knob back in / clockwise until the RPM has increased again (2-3 turns)
- Check fuel flow and exhaust gas temperature

---
Endurance - Instruments
Performance
Control
Altitude
Attitude
Power
Airspeed
Throttle
EGT / FF
Mixture
- Attitude, Power → Airspeed (about 50-60 KIAS), Altitude
- Mixture → Exaust Gas Temperature, Fuel Flow
[Speaker Notes: www.eaa1000.av.org/technicl/perfspds/perfspds.htm]

---
Flight for Range
Power Required
Min Drag
Max Range
D * V
[Speaker Notes: - parasite drag: form, skin friction, interference - induced drag, wave drag (trans-/supersonic) - thrust curve: jet aircraft - power curve: propeller aircraft (reciprocating engine) - engine and propeller efficiency - Experimental Method - POH - Wind, Mixture, Altitude (Factors) - Power (W) = Force (N) * Distance (m) / Time (s) = Force (N) * Velocity (m/s) = Drag (N) * Velocity (m/s) - D = Cd * ½ r * S * v² - P = Cd * ½ r * S * v³]

---
        Range Profile
        POH Section 5
- Consider conditions
- Select pressure altitude
- Select power setting
- Determine range
[Speaker Notes: - Notice almost linear dependency between power setting and airspeed - Linear dependency will eventually change to a much lower airspeed for a lower power setting]

---
Flight for Maximum Range
Min Drag
Max Range
D * V
- Increase power in 100 RPM steps until a non-linear increase in airspeed can be observed
- Maintain level flight, trim and lean mixture as recommended (rich of peak)
[Speaker Notes: - can be decreased in 100 RPM steps as well - approximately 2000 RPM for max. range Familarization Demo - 2000 RPM → 5 GPH → 100 KIAS 30 USG → 6 H → 600 NM - 2400 RPM → 10 GPH → 120 KIAS 30 USG → 3 H → 360 NM]

---
Range – Instruments
Performance
Control
Altitude
Attitude
Power
Airspeed
Throttle
Mixture
EGT / FF
- Attitude, Power → Airspeed (about 70-80 KIAS), Altitude
- Mixture → Exhaust Gas Temperature, Fuel Flow

---
Factors Affecting Range and Endurance
- Endurance: power setting, fuel available, flap setting, angle of attack, airspeed, weight, centre of gravity, altitude, mixture, turbulence
- Range: power setting, fuel available, flap setting, angle of attack, airspeed, weight, centre of gravity, altitude, mixture, wind

---
Summary / Quiz
- Define range, maximum range, endurance and maximum endurance.
- Give examples for when flight for range or endurance is preferable.
- What are the main factors that influence range and endurance and how do they affect them?
- Mentally configure the airplane for best range and endurance and state all required actions, respectively.

---
Pre-Flight Briefing
- Exercise
- Training Area
- Departure and Arrival Procedures
- Weather Briefing / NOTAMs
- Aircraft and Documents
- Time and Fuel Requirements
- Safety Considerations and Responsibilities
[Speaker Notes: - Safety: nose-high, poor forward visibility, engine cooling...]

---
Flight for Endurance
Thrust Required
Power Required
Min Power
Vbe
Min Drag
Vbr
D * V
[Speaker Notes: - Experimental Method - POH - Mixture, Flaps, Altitude (Factors → Turbulence) - Reduced Control Response - SL for reciprocating engines (air density)]

---
Flight for Range
Thrust Required
Power Required
Min Power
Vbe
Min Drag
Vbr
D * V
[Speaker Notes: - parasite drag: form, skin friction, interference - induced drag, wave drag (trans-/supersonic) - thrust curve: jet aircraft - power curve: propeller aircraft (reciprocating engine) - engine and propeller efficiency - Experimental Method - POH - Wind, Mixture, Altitude (Factors) - Power (W) = Force (N) * Distance (m) / Time (s) = Force (N) * Velocity (m/s) = Drag (N) * Velocity (m/s) - D = Cd * ½ r * S * v² - P = Cd * ½ r * S * v³]

---
Flight for Maximum Range (Derived)
- Reduce power to establish best glide airspeed
- Maintain level flight and trim accordingly
- Lean mixture as recommended (rich of peak)
[Speaker Notes: Experimental: ground references during glide - propeller efficiency is a factor]

---
Flight for Maximum Endurance (Derived)
- Reduce power to lowest setting (above slow flight) to maintain altitude (about best glide / 1.3 = 52 KIAS)
- Maintain level flight and trim accordingly
- Lean mixture as recommended (rich of peak)