Aircraft Instruments
Aircraft Instruments
Sean Tyrrell

---
Aircraft Instruments
Material you will be tested on
  - Private
    - http://www.tc.gc.ca/civilaviation/general/Exams/guides/tp12880/section8.htm
  - Commercial
    - http://www.tc.gc.ca/civilaviation/general/Exams/guides/tp12881/Section6.htm

---
Flight Instruments
Flight Instruments
The “6 pack”

---
Pitot/Static System
Pitot/Static System
- What instruments are connected to the pitot/static system?
- What does the pitot/static system provide to us?

---
Pitot/Static System

---
Airspeed Indicator
Airspeed Indicator

---
Airspeed Indicator

---
Airspeed Indicator
Compares dynamic (pitot) and static pressure sources
  - Comparing this difference, the ASI can determine our speed though the air
  - Diaphragm or Aneroid capsule is attached to the pitot source, the sealed case to the static pressure
    - The expansion and contraction of the aneroid capsule translates into an indication on the ASI
    - Essentially, the greater pressure from the ram air entering the pitot increases with airspeed, expanding the aneroid capsule and showing a speed increase
Pitot tube
  - Measures dynamic and static pressure
Static port
  - Measures static pressure – in order to “equalize” the static pressure reading from the pitot tube, or in other words, “subtract” it from the pitot tube static reading
Measures our airspeed through the air, not over the ground (ground speed)

---
Airspeed Indicator
IAS (indicated)
  - Read directly off ASI
CAS (calibrated)
  - IAS corrected for instrument and position error – most obvious at slow airspeeds
    - Position error
TAS (true)
  - CAS corrected for altitude and temperature (air density)

---
Airspeed Indicator
Errors
  - Altitude
    - Higher altitudes, airspeed indicator will not correctly read TAS – slight error due to air density
  - Pitot tube
    - High angles of attack can affect ram air pressure, thus causing a slight airspeed indication error
    - Designers attempt to find a place where the flow of air into the pitot tube is least affected by aerodynamic effects of the aircraft
  - Instrument Error
    - Inherent errors present in the airspeed indicator itself
  - Position Error
    - Location of the static port
    - Never possible to find an area of the aircraft to minimize static pressure error
    - This can affect the airspeed indications at high angles of attack or if airflow is disrupted (look at the POH charts for flaps up/flaps down, aircraft is in a slip/skid)
  - Blockages – Pitot/Static
    - See above

---
Airspeed Indicator
V speeds
  - Vne
  - Vno
  - Vfe
  - Va
  - Vs
  - Vso

---
Vertical Speed Indicator
Vertical Speed Indicator

---
Vertical Speed Indicator
- Only uses static pressure source
- Shows the “trend” (climb or descending) and “rate” (FPM)
- Measures the rate of change of pressure to determine climb or descent
- Both the sealed case and the aneroid capsule are connected to static pressure
  - The difference between the pressure changes in the aneroid capsule and the calibrated leak of static air into the sealed case results in a measurable expansion or contraction of the aneroid capsule
  - This translates into showing a climb or descent
  - When the aircraft climbs
    - Pressure in the diaphragm decreases faster than that in the instrument case because the slow response of the calibrated leak – translates into a climb
  - When the aircraft descends
    - The pressure that enters the case through the calibrated leak is slow to respond – thus the diaphragm expands due to the increased ambient pressure from the static source and shows a descent

---
Vertical Speed Indicator

---
Vertical Speed Indicator
Lag – can be a delay of up to 6-9 seconds after a change in altitude before the VSI reads correctly
  - Ex. Will still show a climb even though now levelled off from a climb
  - Lag noticeable in particularly turbulent conditions
  - Not advisable to use to maintain altitude, especially when flying instruments due to this lag – can cause you to have difficultly holding altitude! Use ALT instead
  - Some aircraft have instantaneous VSI which eliminates this lag
- Reversal – abrupt changes in altitude may cause the VSI to show a change in the wrong direction
- Blocked Static?

---
VSI
VSI

---
Altimeter
Altimeter

---
Altimeter
- Only uses static pressure source
- Consists of a series of sealed aneroid capsules that contain at standard sea level pressure air
  - The sealed case of the altimeter is connected to our static source
  - The changing pressure difference between our static port air and the sealed aneroid capsules results in a measurable expansion/contraction of the aneroid capsules
  - Expansion/contraction of the aneroid capsules translates into the movement of our altimeter needle

---
Altimeter

---
Altimeter
Errors
  - Pressure changes
    - As we fly, the local pressure changes and we have to reset our altimeter to the local pressure in order to be accurate in our altitude
    - “low to high, clear blue sky”
      - Going from a low pressure area to a high pressure area, our true altitude will be higher than our indicated altitude
    - “high to low, look out below”
      - Going from a high pressure area to a low pressure area, our true altitude will be lower than our indicated altitude
  - Temperature
    - Altimeter is set for ICAO standard temperature
      - 15 C at sea level, decreases 1.98 C every 1000 ft
      - Ex. 5000 ft should be about 5.1 degrees in the standard atmosphere
    - Colder than standard temperature for our altitude
      - Our true altitude will be lower than indicated
      - Ex. 5000 ft – should be 5.1 degrees, but is actually is -10
    - Hotter than standard temperature for our altitude
      - Our true altitude will be higher than indicated
      - Ex. 5000 ft – should be 5.1 degrees, but is actually is 15

---
Altimeter

---
Altimeter
Errors (con’t)
  - Position error
    - Location of static port
    - Airflow over static port can change depending on the movement/position of the aircraft
  - Instrument error
    - Age of instrument
    - Hysterisis – lag in instrument caused by aneroid material flexing and stretching – reversal error
  - Static errors/blockages

---
Pitot/Static System
Blockages
  - Pitot
    - Assuming pitot tube and drain hole
      - Airspeed indicator now acts as altimeter
      - As aircraft climbs, reads higher than actual airspeed
      - As aircraft descends, reads lower than actual airspeed
      - *NOTE* - if pitot tube is blocked but NOT drain hole both blocked, airspeed will go to zero
    - What can you do?
      - Pitot heat on
  - Static
    - Altimeter will freeze at the altitude that the static port became blocked
    - VSI will be frozen at zero
    - Airspeed will indicate
      - As aircraft climbs, reads lower than actual airspeed
      - As aircraft descends, reads higher than actual airspeed
    - What can you do?
      - Activate alternate static source (172 only)

---
Pitot Blockage
Pitot Blockage

---
Pitot Blockage

---
Static Blockage
Static Blockage

---
Pitot/Static System
What can you do?
  - Fly based on attitude, power setting
    - Set cruise power, maintain cruise attitude
Simulator
  - http://www.luizmonteiro.com/Learning_Pitot_Sim.htm

---
Pitot/Static System
- TAS, CAS, IAS
- True Airspeed check
  - Flight test!

---
Encoding Altimeter
Encoding Altimeter
Encoding altimeter is found in your mode C transponder
  - Provides ATC with your altitude
  - Sends out altitude at standard pressure 29.92
    - Radar systems compensate by adjusting value given with current station altimeter setting to get your actual altitude

---
Radar Altimeter
Radar Altimeter

---
Radar Altimeter
- Provides height AGL
- Uses radar signal that bounces off the surface of the earth and back to the receiver on the aircraft to provide height AGL
- Outfitted on more advanced IFR aircraft
  - Not common on light twins
- Works in conjunction with GPWS to provide terrain warnings
- Important in IFR situations – gives flight crews an idea of how high they are above their TD point, also plays a role in the operation of autoland systems
- Limitations
  - Provides height AGL only immediately in front of the aircraft – does not provide altitude of approaching terrain

---
Magnetic Compass
Magnetic Compass

---
Magnetic Compass

---
Magnetic Compass
- Based on magnetic field of earth
- This points at magnetic north
  - On our charts, these show the true north pole
Magnetic variation
  - this is the difference between magnetic north we read off the compass, and true north on the chart
  - Approximately 17E near Victoria
    - Ex. Runway 27 is 268 degrees magnetic, but actually would be 285 degrees true

---
Magnetic Compass
Errors
  - Acceleration/Deceleration
    - Happens only on easterly/westerly headings
    - Acceleration – compass swings to the north
    - Deceleration – compass swings to the south
    - ANDS
      - Accelerate North, Decelerate South
  - Northerly turning error
    - Turns to or from the north, the compass lags behind the actual heading
    - Turns to or from the south, the compass leads ahead of the actual heading
    - NAGS and SEADS
      - North Lags, South Leads
  - Magnetic dip
    - Near the poles, lines converge and compass is inaccurate – this is why in northern Canada the magnetic compass is not used
  - Compass Card
    - This is in the aircraft to show you the errors to the compass caused by the metal and electrics in the aircraft that cause a slight deviation in the compass readings
NOTE! We only can rely on the magnetic compass for accurate readings when we are in straight and level flight at a constant airspeed

---
Compass Correction Card
Compass Correction Card

---
Magnetic Compass

---
Magnetic Compass

---
Compass Swing
Compass Swing
How often?
  - Every 12 months
  - Done at the compass rose located on taxiway K
  - Aircraft is running during the compass swing with all systems normally used in flight powered up – we want a realistic scenario of magnetic interference from the aircraft while swinging the compass
  - Adjusted via two screws that move compensating magnets

---
Gyroscope
Gyroscope

---
Gyroscopes
Gyroscopes

---
Gyroscope
- What 3 instruments do we have gyroscopes in?
- Works on the principles of “rigidity in space” and gyroscopic precession
  - “rigidity in space” or gyroscopic inertia
    - Defined as “the tendency of any rotating body, if undisturbed, to maintain its plane of rotation”
    - Basically, this means that the spinning mass of the gyro will have the tendency to hold the same plane, despite being moved
When the gyro is spinning, it resists the tendency to move
  - The aircraft moves around the gyro

---
Gyroscope
A high speed spinning mass is mounted on an axis in a mounting called a gimbal

---
Vacuum Pump
Vacuum Pump

---
Vacuum Pump
An engine driven pump to provide suction power
  - Drives the AI and HI in our aircraft
Not used in high altitude aircraft due to the fact that the performance decreases with altitude with the reduced air density
  - Usually electrically driven in that case

---
Heading Indicator
Heading Indicator

---
Heading Indicator

---
Heading Indicator
Steady and accurate – we set the HI to the magnetic compass
  - The HI does not know our magnetic heading, we must set the HI to our compass
  - We use the heading indicator as it does not have the same errors as the magnetic compass

---
Heading Indicator
The gyro is mounted vertically in a HI
  - The gyro will attempt to hold its vertical position despite the motion of the aircraft
  - Gyroscopic precession caused by the turning of the aircraft will tend to disturb this, and as a result, gives us an instrument indication that we are changing heading
The gyro in the HI rotates at around 20000 to 25000 RPM!
  - This is driven by either a…
    - Venturi
    - Vacuum pump
    - Electrically

---
Heading Indicator
Errors
  - Apparent precession
    - the rotation of the earth causes a drift in the HI setting
  - Precession
    - Friction in the instrument can cause the HI to lose its setting – about 3 degrees/15 minutes
    - This can be worse in an older instrument that is a bit worn out

---
HSI
HSI
Slaved compass
  - A flux gate sensor located often in the tail of the aircraft provides constant magnetic compass readings – this is slaved to the HSI, providing us a constant, accurate magnetic heading on our HSI
  - We do not need to reset the HI to the compass with this system
Horizontal Situation Indicator
  - Combines a slaved heading indicator, VOR and glideslope indicator
  - Found on the Seminole
  - Electrically powered

---
HSI

---
Attitude Indicator
Attitude Indicator

---
Attitude Indicator

---
Attitude Indicator
- Provides us with an “artificial horizon” for circumstances where we may not be able to see the actual horizon
- Uses gyroscopic principles of
  - Rigidity in space
  - Precession

---
Attitude Indicator
The gyro is mounted horizontally in the AI (vertically in HI)
  - driven by either a…
    - Venturi
    - Vacuum pump
    - Electrically
The gyro stays stationary, and the aircraft moves about the gyro
  - The instrument translates our movement into the display that we see when the aircraft rolls and pitches
  - The gyro will attempt to hold its horizontal position despite the motion of the aircraft
  - Gyroscopic precession caused by the turning of the aircraft will tend to disturb this, and as a result, gives us an instrument indication that we are pitching and/or banking the aircraft

---
Attitude Indicator
Errors
  - Mostly friction
  - Accelation/deceleration errors
    - Acceleration – shows a false pitch up indication
    - Deceleration – shows a false pitch down indication

---
Turn and Bank Indicator / Turn Coordinator
Turn and Bank Indicator / Turn Coordinator

---
Turn and Bank Indicator / Turn Coordinator
- Contains a gyro – how is this gyro powered in our aircraft?
- Gyro rotates at 30000 RPM
- Uses gyroscopic principles of
  - Rigidity in space
  - Precession

---
Turn and Bank Indicator / Turn Coordinator
Also uses a steel ball in a liquid contained in a curved glass tube – inclinometer
  - We use this to determine if the aircraft is slipping or skidding
- Gravitational forces effect movement on the steel ball
- To keep the aircraft coordinated (meaning we are eliminating the yawing of the aircraft) we “Step on the ball”
  - This means if the ball is deflected to the left, we apply left rudder sufficient enough to bring the ball within the center markers

---
Turn and Bank Indicator / Turn Coordinator
Turn Coordinator
  - Shows rate of turn, rate of roll and coordination
  - Gyro is mounted at a 30-35 degree angle in order to provide us provide us roll information
Turn and Bank
  - Shows rate of turn and coordination

---
Turn and Bank / Turn Coordinator
Turn and Bank / Turn Coordinator

---
Turn and Bank Indicator / Turn Coordinator

---
Turn and Bank Indicator / Turn Coordinator
Rate one turn
  - 360 degrees of heading change in 2 minutes
  - Turn and Bank and Turn Coordinator figure this out automatically
    - As long as you keep the needle or wing of the aircraft on the mark, you will turn 360 degrees in 2 minutes
  - Formula for figuring out bank angle required for rate one turn
    - 10% of your airspeed + 7 = angle of bank required