## Slide 1
vfc©
weather to fly
meteorology for the commercial pilot

## Slide 2: hello my name is
vfc©
Sean Tyrrell
seantyrrell@flyvfc.com
250-882-4483

## Slide 3: Class outline
vfc©
http://www.tc.gc.ca/Publications/en/TP12881/PDF/HR/TP12881E.pdf
friday: pre-test, met theory
saturday: met theory, advanced theory - air mass, front
sunday: advanced theory - jet stream, aviation weather products, sample exam and take-up

## Slide 4: day1
vfc©
pre-test, met theory

## Slide 5: atmosphere
vfc©

## Slide 6: Atmosphere properties
mobility
expansion
compression
vfc©

## Slide 7: Atmosphere composition
nitrogen
78%
oxygen
21%
water vapour, CO2, argon, others
1%
vfc©

## Slide 8: Atmosphere the key
water vapour is water in its gaseous, invisible form
it is the key to visible weather formation
visible weather determines the possibility of visual (VFR) flight!
vfc©

## Slide 9
troposphere
stratosphere
mesosphere
thermosphere
16
Atmosphere divisions
vfc©

## Slide 10: Atmosphere troposphere
28000’ deep over the poles, 54000’ deep over the equator
pressure, density and temperature all decrease as we ascend into the troposphere
most visible weather occurs in the troposphere
vfc©

## Slide 11: Atmosphere tropopause
a ‘pause’ is a boundary between atmopsheric divisions
the tropopause divides the troposphere and the stratosphere above
characterized by a lowest temperature of -56°C
vfc©

## Slide 12: Atmosphere stratosphere
50000’ to 150000’ above earth’s surface
pressure and density continue to decrease but temperature rises towards 0°C in the upper stratosphere
due to existence of the ozone layer
temperature then decreases again in the stratopause
vfc©

## Slide 13: Atmosphere mesosphere
150000’ to 250000’ above earth’s surface
pressure, density and temperature continue to decrease
temperature falls as low as -100°C in the mesopause
this is the coldest temperature found within the atmosphere and on earth
vfc©

## Slide 14: Atmosphere thermosphere
500000’ to 500km above earth’s surface
pressure, density decrease yet an extreme rise in temperature is noted with an increase in altitude
vfc©

## Slide 15: Atmosphere thermosphere
1500°C to 2500°C due to the kinetic theory of gases
absorbtion of intese solar radiation by few O2 molecules that remain create these high temperatures
above 160km in the thermosphere exists the anacoustic zone - no sound transmission
vfc©

## Slide 16: Atmosphere and beyond
the exososphere is the last layer of the atmophere
has an upper boundary of approximately 190000km
mainly hydrogen molecules
influence of solar radiation energy on hydrogen molecules exceeds that of earth’s gravitational pull
vfc©

## Slide 17: Atmosphere temperature
vfc©

## Slide 18: Atmosphere standard
for aeronautical engineering purposes, it is necessary to have a set of clearly defined standards to reference for aircraft design
pilots must be able to understand and apply this set of standards
integral in performance and altitude computations
vfc©

## Slide 19: Atmosphere ISA Properties
the air is a perfectly dry gas
a mean sea level pressure of 29.92” Hg
a mean sea level temperature of 15°C
the rate of decrease of temperature with altitude is 1.98°C per 1000’
vfc©

## Slide 20: Atmosphere ISA Properties
standard atmosphere only exists on paper
vfc©

## Slide 21: Atmosphere pressure
pressure is the atmosphere exerting a force on the surface of the earth
vfc©

## Slide 22: Atmosphere barometer
29.92” Hg
vfc©

## Slide 23: Atmosphere station pressure
1” Hg change correlates to a 1000’ change in altitude
station pressure is the atmospheric pressure at the elevation of the observing station
station pressure
vfc©

## Slide 24: Atmosphere station pressure
station pressure is simply the weight of the one square inch column of air “weighing down” on the station barometer
station pressure IS NOT the altimeter setting
vfc©

## Slide 25: Atmosphere density
density is the ratio of the mass of an object in relation to the volume it occupies
atmospheric density decreases with altitude, increased temperature and increased humidity
this positively or negatively affects aircraft performance
vfc©

## Slide 26: Atmosphere density
a parcel of air rises because it is of a lesser density than the air surrounding it
less dense
vfc©

## Slide 27: Atmosphere relationships
atmospheric pressure and density are directly correlated
lower pressure equals lower density
pressure and therefore density decreases with an increase in altitude
vfc©

## Slide 28: altimetry
vfc©

## Slide 29: Altimetry altimeter
modern day altimeters are referred to as sensitive altimeters
they are simply barometers, calibrated to display a change of 30’ with each milibar of pressure change
each needle is representitive of either hundreds, thousands or tens of thousands of feet
includes a subscale which is used to set the altimeter setting
vfc©

## Slide 30: Altimetry IALT
indicated altitude (IALT) is the altitude as indicated on the altimeter above MSL when it is set to the current altimeter setting
it is simply “what the needles say” when the subscale is set correctly
IALT does not take into account non-ISA temperature or humidity values, or instrumentation error
vfc©

## Slide 31: Altimetry altimeter setting
altimeter setting is either expressed as QNH or QFE
QNH is station pressure corrected to mean sea level (MSL) values - altimeter will read height in feet above sea level (ASL) in ISA conditions
QFE is station pressure corrected to a reference datum on the airfield - altimeter will read zero when at the datum in ISA conditions
QNH = “nautical height”, QFE = “field elevation”
vfc©

## Slide 32: Altimetry altimeter setting
worldwide altimeter setting is expressed in millibars (mb) or hectopascals (hPa) - 1 mb = 1 hPa
altimeter setting is set on a subscale on the altimeter
EXCEPT in Canada, the United States and Columbia altimeter setting is expressed to the hundredth of an “Hg
ISA altimeter setting = 29.92”Hg = 1013.2 mb/hPa
vfc©

## Slide 33: Altimetry altimeter setting
15 year average MSL values, June - August
15 year average MSL values, December - February
vfc©

## Slide 34: Altimetry changing pressure
when flying between areas of differing sea level pressure, the altimeter setting will change
if this change is ignored it can be extremely dangerous
this is because the altimeter is simply a barometer - the reading of the needles will change with changes in pressure
having the correct altimeter setting set appropriate for the area you are flying in ensures this reading is accurate
vfc©

## Slide 35: Altimetry high to low
when flying from high to low pressure, the altimeter will over-read
the pilot’s reaction is to descend
this causes the pilot and aircraft to be lower than they think they are
“from high to low, lookout below”
vfc©

## Slide 36: Altimetry high to low
vfc©
30.92”Hg
28.92”Hg

## Slide 37: Altimetry high to low
vfc©
30.92”Hg
28.92”Hg

## Slide 38: Altimetry low to high
when flying from low to high pressure, the altimeter will under-read
the pilot’s reaction is to climb
this causes the pilot and aircraft to be higher than they think they are
“from low to high, look to the sky”
vfc©

## Slide 39: Altimetry low to high
vfc©
30.92”Hg
28.92”Hg

## Slide 40: Altimetry low to high
vfc©
30.92”Hg
28.92”Hg

## Slide 41: Altimetry PALT
pressure altitude (PALT) is the altitude as indicated on the altimeter above MSL when it is set to ISA pressure
PALT is the atmospheric pressure conditions the aircraft “thinks” it’s performing under
any non-standard (other than 29.92” Hg) altimeter settings will give non-standard performance
vfc©

## Slide 42: Altimetry cold air
cold air will cause an altimeter to over read due to the steeper pressure gradient, when compared to warm air
vfc©

## Slide 43: Altimetry PALT
PALT corrects for non-ISA sea level pressure settings only
aircraft performance charts (ie. takeoff, cruise, landing) are based on the aircraft’s pressure altitude
setting 29.92” Hg in flight will read PALT
vfc©

## Slide 44: Altimetry PALT
PALT is the standard for performance chart usage
vfc©

## Slide 45: Altimetry PALT formula
PALT is calculated using the formula below:
PALT = station elevation +
        [(29.92” Hg - altimeter setting) x1000]
1” Hg = 1000’
vfc©

## Slide 46: Altimetry DALT
density altitude (DALT) is pressure altitude corrected for non-standard ISA atmospheric temperature conditions
it is the altitude at which the aircraft will perform as if it’s at given pressure, humidity and temperature variances from ISA
vfc©

## Slide 47: Altimetry DALT
DALT is the most important value in terms of determining how an aircraft will perform
it is especially important under detrimental ISA conditions
hot, high, and humid
vfc©

## Slide 48: Altimetry DALT
DALT may be calculated in the air, using an E6B flight computer, the outside air temperature and the PALT
it may also be calculated on the ground using a formula
vfc©

## Slide 49: Altimetry DALT formula
DALT is calculated using the formula below:
DALT = PALT +
        [100(OAT - ISA temperature)]
1” Hg = 1000’
vfc©

## Slide 50: Altimetry formulae
DALT and PALT formulas, as any formulae, are truly remembered when they are understood
anticipate calculations by relating pressure and temperature values to standard
ie. lower than standard altimeter setting will give a higher pressure altitude than indicated - if not check your calculation
vfc©

## Slide 51: temperature
vfc©

## Slide 52: Temperature imbalance
vfc©
it is due to global temperature differences that we see the creation of weather
these variances are due to a variety of factors, such as location, season, surface type etc.
creates large and small scale weather patterns versus one global weather pattern

## Slide 53: Temperature radiation
vfc©
solar radiation is the energy transfer from the sun to the surface of the earth
terrestrial radiation is the energy transfer from the surface of the earth to the troposphere

## Slide 54: Temperature radiation
vfc©
only half of the incoming solar radiation is absorbed at the surface

## Slide 55: Temperature variation
vfc©
the earth spinning on a tilted axis causes seasonal variation

## Slide 56: Temperature variation
vfc©
latitudinal variation accounts for global wind circulation patterns

## Slide 57: Temperature variation
vfc©
diurnal variation occurs when solar radiation ceases at sunset

## Slide 58: Temperature variation
vfc©
surface variation determines how readily terrestrial radiation will occur due to absorption

## Slide 59: Temperature heating
vfc©
tropospheric heating is due to heating from the ground up
conduction plays a very small role
there are many other processes involved which distribute heat throughout the troposphere

## Slide 60: Temperature convective heating
vfc©
convective heating is due to the vertical cycle created by rising warm and descending cold air

## Slide 61: Temperature advective heating
vfc©
advective heating occurs as cold air is warmed from below as it moves over a warmer surface

## Slide 62: Temperature turbulent heating
vfc©
turbulence at the surface creates instability and causes heat to be forced aloft

## Slide 63: Temperature compression
vfc©
descending air is compressed, increasing pressure and temperature, also known as subsidence

## Slide 64: Temperature adiabatic heating
vfc©
the term adiabatic means that it is the act of compression itself that is heating the parcel of air
there is no external heating force affecting the air

## Slide 65: Temperature cooling
vfc©
as with heating, numerous processes are involved besides radiation that cool the troposphere
radiation cooling itself only affects the surface based levels of the troposphere

## Slide 66: Temperature radiation cooling
vfc©
cooling due to terrestrial radiation at night depends on the existence of cloud

## Slide 67: Temperature advective cooling
vfc©
advective cooling occurs as warm air is cooled from below as it moves over a colder surface

## Slide 68: Temperature adiabatic cooling
vfc©
the term adiabatic means that it is the act of expansion itself that is cooling the parcel of air
there is no external cooling force affecting the air

## Slide 69: Temperature isothermal
vfc©
an isothermal layer means there is no change in temperature with a change in altitude
it can occur if the predominant weather pattern is very stable
if a light mixing action is set up due to wind bringing together warm and cold air, an isothermal layer may be created

## Slide 70: Temperature inversion
vfc©
an inversion means an increase in temperature with an increase in altitude
like an isothermal condition, it can occur if the predominant weather pattern is very stable
inversions are in fact so stable that they can give poor VFR flight conditions

## Slide 71: Temperature inversion
vfc©
inversions can commonly form in valleys at sunset
the setting sun warms the air in the upper valley after it has set on the cooling lower air below

## Slide 72: Temperature inversion
vfc©

## Slide 73: Temperature inversion
vfc©
inversions may also form on cold, calm nights when terrestrial radiation ceases, cooling only the lowest levels of the troposphere
they may also occur with the passage of a cold front
inversions favour poor visibility in the cold air and are inherently stable so may persist for long periods of time

## Slide 74: wind
vfc©

## Slide 75: Wind pressure
wind is simply the horizontal movement of air
solely due to pressure gradients
pressure gradients are “slopes” created by relative areas of high and low pressure
vfc©

## Slide 76: Wind pressure gradient
isobars join points of equal sea level pressure to create a top down pressure “map”
isobars are without exception drawn at 4 mb intervals
knowing this you can determine the sea level pressure along each isobar
vfc©
4 mb
4 mb
4 mb

## Slide 77: Wind speed
the closer the isobars, the steeper the pressure gradient, and the faster the wind speed
the further apart the isobars, the shallower the pressure gradient, and the slower the wind speed
vfc©

## Slide 78: Wind pressure gradients
cross sectional view of isobars, steep and shallow gradients
vfc©
4 mb
4 mb

## Slide 79: Wind pressure map
vfc©

## Slide 80: Wind high
an area of high pressure is also known as an anti-cyclone
it is an area of relatively high sea level pressure
wind moves clockwise around a high in the Northern hemisphere
a high is marked by descending and compressing air
vfc©

## Slide 81: Wind low
an area of low pressure is also known as a cyclone
it is an area of relatively low sea level pressure
wind moves counter-clockwise around a low in the Northern hemishphere
a low is marked by ascending and expanding air
vfc©

## Slide 82: Wind low
vfc©

## Slide 83: Wind pressure systems
vfc©
✗

## Slide 84: Wind pressure systems
vfc©
✓

## Slide 85: Wind movement
wind does not move directly from areas of high to low pressure
it moves in relation to the isobars, following their curvature
how closely the wind follows the isobars is dependent on altitude
vfc©

## Slide 86: Wind movement
wind moves off of and away from centers of high pressure, in a clockwise direction
wind moves down into and towards centers of low pressure, in a counter-clockwise direction
there are two forces besides the pressure gradient that determine wind movement
vfc©

## Slide 87: Wind coriolis
the coriolis force is an apparent deflection of a moving body as viewed from a rotating reference frame
it is a major factor in explaining why wind moves the way it does
coriolis causes an apparent deflection of a moving body to the right in the Northern hemisphere
vfc©

## Slide 88: Wind coriolis
vfc©

## Slide 89: Wind coriolis
coriolis affects the apperent motion of all moving bodies
however it is only influential on objects moving on northerly or southerly tracks
it has a negligible effect upon objects moving east and west, as well as objects moving closer to the poles
vfc©

## Slide 90: Wind centrifugal
centrifugal force draws a rotating body away from its center of rotation
equal and opposite to centripetal force
remember wind moving in pressure systems is a rotating body
vfc©

## Slide 91: Wind centrifugal
centrifugal force works with the pressure gradient force when acting on wind blowing out from a high
centrifugal force works against the pressure gradient force when acting on wind blowing into a low
the net result is an increased wind speed blowing out of a high and a decreased wind speed blowing into a low
vfc©

## Slide 92: Wind buys ballots law
Buys Ballot’s law states that in the Northern hemisphere standing with your back to the wind, the area of low pressure will be to your left
vfc©
✈
✈
✈

## Slide 93: Wind notation
wind direction is indicated as a bearing, either in degrees true or magnetic depending on the type of information
wind is reported or forecast as coming from a specific bearing, rounded to the nearest ten degrees
wind speed is always observed or forecast in nautical miles per hour (KTS)
vfc©

## Slide 94: Wind veer
a wind that changes direction clockwise is termed a veering wind
ie. a wind of 180° changes to a wind of 230°
vfc©

## Slide 95: Wind back
a wind that changes direction counter-clockwise is termed a backing wind
ie. a wind of 230° changes to a wind of 180°
vfc©

## Slide 96: Wind surface
surface wind is generally termed as winds below 3000’ AGL
surface wind is influenced by surface friction, which slows its speed
a reduce wind speed means a lesser apparent deflection due to the coriolis force, causing movement across isobars
vfc©

## Slide 97: Wind surface
vfc©

## Slide 98: Wind surface
a reduction in coriolis leads to greater influence on the wind by the pressure gradient force
the result is less of an apparent deflection to the right
this is a backing wind
vfc©

## Slide 99: Wind aloft
aloft wind is generally termed as winds above 3000’ AGL
aloft wind is not influenced by surface friction, which increases its speed
an increased wind speed means a greater apparent deflection due to the coriolis force, causing movement parallel to the isobars
vfc©

## Slide 100: Wind aloft
vfc©

## Slide 101: Wind aloft
an increase in coriolis leads to lesser influence on the wind by the pressure gradient force
the result is more of an apparent deflection to the right
this is a veering wind
vfc©

## Slide 102: Wind surface and aloft
vfc©
surface
aloft

## Slide 103: Wind surface and aloft
during a descent from aloft to the surface, the wind is seen to decrease in intensity and back
during a climb from the surface to aloft, the wind is seen to increase in intensity and veer
vfc©

## Slide 104: Wind circulation
vfc©
global temperature differences create global atmospheric circulation
large scale prevailing winds, such as the northeastern trade winds in the tropics
pressure gradient force, coriolis force, centrifugal force all need to be considered

## Slide 105: wind circulation
www.nullschool.net

## Slide 106: Wind circulation
vfc©

## Slide 107: Wind sea breeze
vfc©
the wind blows on shore during the day due to the convective circulation cycle started as warm air rises over the warmer land surface

## Slide 108: Wind land breeze
vfc©
the wind blows off shore during the night due to the convective circulation cycle started as warm air rises over the warmer water surface

## Slide 109: Wind katabatic
vfc©
the wind blows down mountain slopes into valleys at night as the surface of the slopes are cooled

## Slide 110: Wind anabatic
vfc©
the wind rises up mountain slopes out of valleys during the day as the surface of the slopes are heated

## Slide 111: Wind glacial
vfc©
the wind blows down glacial slopes much like a katabatic wind due to the cold dense air cooled by the glacier

## Slide 112: Wind shift
vfc©
a gust is a rapid and irregular fluctuation in the movement of air caused commonly by mechanical turbulence and convection
a squall is a sudden increase in wind strength of a greater intensity than a gust, usually caused by thunderstorm passage

## Slide 113: Wind shear
vfc©
wind shear is the tearing effect that can be experienced along the border of two zones which have different wind speeds and intensities
shear may severely impact aircraft performance, especially critical during take-off and landing

## Slide 114: Wind shear
vfc©
increased performance wind shear is encountered with an increase in headwind or decrease in tailwind component
on approach, increased performance shear requires a net increase in power to maintain the ideal approach path

## Slide 115: Wind shear
vfc©

## Slide 116: Wind shear
vfc©
decreased performance wind shear is encountered with an decrease in headwind or increase in tailwind component
on approach, decreased performance shear requires a net decrease in power to maintain the ideal approach path

## Slide 117: Wind shear
vfc©

## Slide 118: day2
vfc©
met theory continuation, air masses, fronts

## Slide 119
vfc©
USING ALL AVAILABLE INFORMATION, WHAT IS THE DENSITY ALTITUDE (DALT) AT CALGARY INTERNATIONAL AIRPORT THIS MORNING, AT 1500Z?

## Slide 120: stability
vfc©

## Slide 121: Stability vertical displacement
vfc©
stability is used to to describe how resistant air is to vertical displacement
stable air resists vertical displacement
unstable air continues movement in the direction of displacement

## Slide 122: Stability vertical displacement
vfc©
stable
unstable

## Slide 123: Stability temperature
vfc©
stable
unstable

## Slide 124: Stability lapse rate
vfc©
lapse rate is a vertically descriptive rate of temperature change with altitude
a steep lapse rate implies a large temperature change within a given vertical distance
a shallow lapse rate implies a small temperature chage within a given vertical distance

## Slide 125: Stability lapse rate
vfc©
lapse rate is a key indicator of air stability
a steep lapse rate indicates unstable air
a shallow lapse rate indicates stable air

## Slide 126: Stability temperature
vfc©
shallow and stable
steep and unstable

## Slide 127: Stability air
vfc©
stability is a key determinant of weather and its severity
knowledge of stability allows pilots to predict weather conditions that will affect their flight

## Slide 128: Stability stable air
vfc©
little or no turbulence
steady winds
layer cloud
continuous precipitation
poor visibility, especially in the lower levels

## Slide 129: Stability unstable air
vfc©
turbulent
gusting winds
vertically developed cloud
intermittent precipitation
generally good visibility

## Slide 130: turbulence
vfc©

## Slide 131: Turbulence defined
vfc©
turbulence is a random spinning motion of air, or when it develops an abrupt updraft or downdraft
aircraft reaction to turbulence is dependant on a variety of factors
aircraft design, size, speed, wing loading and altitude will all determine this reaction

## Slide 132: Turbulence frequency
vfc©
a factor in the determination of turbulent effect is its frequency

## Slide 133: Turbulence classification
vfc©
turbulence is classified based on what causes it
mechanical
convective
shear
wake
clear air (jet stream)

## Slide 134: Turbulence intensity
vfc©
turbulence intensity is forecast and reported as follows:
LIGHT: small, erratic changes in altitude and attitude
LIGHT CHOP: light turbulence with a rapid, rhythmic component
MODERATE: greater intensity than light, often with variations in indicated airspeed, aircraft still in positive control

## Slide 135: Turbulence intensity
vfc©
MODERATE CHOP: greater intensity than light chop, without appreciable changes to attitude and/or altitude
SEVERE: large, abrupt changes in aircraft attitude and altitude, usually accompanied by large variations in indicated airspeed - aircraft may be temporarily out of control
EXTREME: aircraft out of control, structural damage possible

## Slide 136: lift
vfc©

## Slide 137: Lift lifting agents
vfc©
convection
orographic
fronts
turbulence
convergence

## Slide 138: Lift convection
vfc©
convective heating creates lift and with it a high degree of instability

## Slide 139: Lift orographic
vfc©
orographic implies large-scale geographic features
air will continue its unstable movement downwind of a mountain range

## Slide 140: Lift frontal
vfc©
frontal lift is an immensely powerful lifting force
fronts = active weather
C
W

## Slide 141: Lift turbulence
vfc©
turbulent eddies may be carried aloft if the air is inherently unstable and winds are strong

## Slide 142: Lift convergence
vfc©
air falling down the pressure gradient converges at the bottom of a low
forces air aloft creating large-scale lift
L

## Slide 143: saturation
vfc©

## Slide 144: Saturation atmospheric moisture
water vapour is the key to visible weather fromation
water vapour exists in the atmosphere due to transpiration from vegetation, and evaporation from bodies of water
water vapour is the invisible form of atmospheric moisture
liquid or crystalline are visible forms of moisture
vfc©

## Slide 145: Saturation state of change
water vapour’s change of state creates visible moisture
water vapour may condense into a liquid or sublimate directly to a solid
attention must be paid to the energy transfer during these reactions in order to understand visible weather formation
vfc©

## Slide 146: Saturation state of change
vfc©

## Slide 147: Saturation state of change
energy released during the process of condensation is know as the latent heat of vaporization
energy released during the process of freezing is known as the latent heat of fusion
this energy release into the atmosphere creates our most powerful weather phenomena
vfc©

## Slide 148: Saturation saturated
the maximum pressure due to water vapour a volume of air may hold is governed by its temperature
saturation implies this volume of air holds the maximum pressure of water vapour it can, at its given temperature
vfc©

## Slide 149: Saturation relative humidity
relative humidity is defined as the ratio between the partial pressure of water vapour and the saturated vapour pressure of water
partial pressure implies water vapour is only one component of the total gaseous pressure of a volume of air
the saturated vapour pressure of water is simply the pressure at which a volume of air must reach in order for gaseous water to change state (condense or deposit)
vfc©

## Slide 150: Saturation temperature
temperature governs the pressure of the volume of air
lower temperature raises air pressure, of which water vapour pressure is a part of, decreasing the difference between it and the saturated vapour pressure of water
this decreasing difference is represented by an increase in relative humidity
vfc©

## Slide 151: Saturation increasing pressure
a volume of air may have its vapour pressure increased towards saturation in two ways
by cooling...
or by increasing its water content
vfc©

## Slide 152: Saturation increasing moisture
vfc©
100% relative humidity
50% relative humidity
100% relative humidity

## Slide 153: Saturation dew point
dew point is the temperature a volume of air must be cooled to in order for water vapour to condense into water
dew point is a saturation temperature
dew point and relative humidity are related
vfc©

## Slide 154: Saturation cooling
vfc©
100% relative humidity
50% relative humidity

## Slide 155: Lapse rate
vfc©

## Slide 156: Lapse rate defined
vfc©
lapse rate is a measurement of how quickly air cools when ascending a given vertical distance
in non-inversion conditions, this is said to be a positive rate
in an inversion, this rate is negative

## Slide 157: Lapse rate values
vfc©
there are four adiabatic lapse rates that need to be understood:
standard adiabatic lapse rate (STALR): 1.98°C/1000’
dry adiabatic lapse rate (DALR): 3°C/1000’
saturated adiabatic lapse rate (SALR): 1.5°C/1000’
environmental adiabatic lapse rate (EALR): 2.5°C/1000’

## Slide 158: Lapse rate calculations
vfc©
using the appropriate rate and knowing the temperature and dew point of a reporting station, two values may be calculated
the expected base of convective cloud
the height of the freezing level in convective cloud

## Slide 159: cloud
vfc©

## Slide 160: Cloud formation
cloud formation is simply water in its visible state
due to condensation or deposition (reverse sublimation)
condensation nuclei are required as a basis for the condensation or deposition of water vapour
vfc©

## Slide 161: Cloud classification
clouds are classified in two different ways
by formation/appearance
by height based on the altitude of their bases
vfc©

## Slide 162: Cloud by formation
clouds may be formed horizontally, known as stratoform cloud (-stratus)
often appear as many stacked layers
multiple layers may create an extensive summative depth
vfc©

## Slide 163: Cloud by formation
clouds may also be formed vertically, known as cumuloform cloud (-cumulus)
appear to have extensive vertical development
one vertical cloud may extend to the upper reaches of the tropopause
vfc©

## Slide 164: Cloud by height
clouds are also classified based on the height of their bases in feet above ground level:
high clouds - bases above 20000’ AGL
middle clouds - bases from 6500’ AGL to 20000’ AGL
low clouds - bases from above surface the 6500’ AGL
clouds of vertical development - bases generally at the levels of low clouds
vfc©

## Slide 165: Cloud high clouds
high clouds are composed entirely of ice crystals
they are denoted using the prefix cirr-
vfc©

## Slide 166
vfc©
cirrus ci

## Slide 167
vfc©
cirrocumulus cc

## Slide 168
vfc©
cirrostratus cs

## Slide 169: Cloud middle clouds
middle clouds are composed of ice crystals or water droplets
they are denoted using the prefix alto-
vfc©

## Slide 170
vfc©
altostratus as

## Slide 171
vfc©
altocumulus ac

## Slide 172
vfc©
altocumulus castellanus acc

## Slide 173: Cloud low clouds
low clouds are composed of ice crystals or water droplets
they do not use one specific prefix
vfc©

## Slide 174
vfc©
stratus st

## Slide 175
vfc©
stratus fractus sf

## Slide 176
vfc©
stratocumulus sc

## Slide 177
vfc©
nimbostratus ns

## Slide 178: Cloud vertically developed clouds
vertically developed clouds are often composed of water in all of its states
due to extensive vertical height and thus differing temperature regions within the cloud
vfc©

## Slide 179
vfc©
cumulus cu

## Slide 180
vfc©
towering cumulus tcu

## Slide 181
vfc©
cumulonimbus cb

## Slide 182
vfc©
cumulonimbus cb

## Slide 183
vfc©
cumulonimbus cb

## Slide 184: precipitation
vfc©

## Slide 185: Precipitation formation
precipitation formation is due to two main factors
both of these factors involve moisture in cloud becoming too massive to support aloft
vfc©

## Slide 186: Precipitation coalescence
water droplets collide with each other in cloud, becoming more massive, termed coalescence
eventually they fall when the uplifting force in cloud is outweighed by their mass, and the droplets falling to the ground
coalescence is more prevalent in areas of cloud where the temperature is above freezing
vfc©

## Slide 187: Precipitation types
there are numerous forms of precipitation, once it has formed due to coalescence or sublimation
stratoform clouds yield continuous and light/moderate intensity precipitation
cumuloform clouds yield intermittent and intense precipitation
vfc©

## Slide 188: Precipitation rain
rain is formed of large droplets
freezing rain is composed of super cooled water droplets which instantaneously freeze upon impact
vfc©

## Slide 189: Precipitation super cooling
water may exist as a liquid at temperatures as low as -42°C
due to a lack of nuclei around which a crystal may form
supercooled demonstration
vfc©

## Slide 190: Precipitation drizzle
drizzle are small droplets that appear suspended
freezing drizzle occurs when drizzle freezes on impact with cold objects
vfc©

## Slide 191: Precipitation hail
hail forms in cumulonimbus clouds as ice crystals collide with supercooled water droplets
the large mass of hail stones requires an immense uplifting force in cloud for their creation, only present in well developed cumuloform cloud
vfc©

## Slide 192: Precipitation hail
vfc©

## Slide 193: Precipitation snow
snow is created through sublimation in cloud
its state at the surface is dependant on the ambient air temperature
vfc©

## Slide 194: Precipitation snow pellets
hail that does not acquire a hard outer coating of ice is termed a snow pellet, or soft hail
this occurs when the water region of the cloud is of limited depth
vfc©

## Slide 195: Precipitation ice pellets
ice pellets are formed by rain drops freezing
they are hard and transparent, and rebound upon striking a surface
vfc©

## Slide 196: fog
vfc©

## Slide 197: Fog formation
fog is simply visible moisture in contact with the surface
fog formation is identical to cloud formation, however the atmospheric moisture generating the fog is localized and the fog low lying
moisture laden air saturates forming fog in different ways
vfc©

## Slide 198: Fog formation
ideal fog formation conditions, besides high humidity in the presence of condensation nuclei, include light surface winds or instability
if there is no lifting or mixing action in low lying air, dew or frost may form
moisture laden air saturates forming fog in many different ways
vfc©

## Slide 199: Fog radiation
radiation fog forms on cold, clear nights in low areas such as valleys
vfc©
Notes: Radiation fog begins to form over land usually under clear skies and light winds typically after midnight and peaks early in the morning. As the land surface loses heat and radiates it into space, the air above the land is cooled and loses its ability to hold moisture. If an abundance of condensation nuclei is present in the atmosphere, radiation fog may develop before the temperature-dewpoint spread reaches zero. After sunrise, the fog begins to burn off from the edges over land but any fog that has drifted over water will take longer to burn off.

## Slide 200: Fog advection
advection fog forms in coastal areas as warm, moist air laden with salt (nuclei) is advectively cooled
vfc©
Notes: Fog that forms when warm moist air moves across a snow, ice or cold water surface.

## Slide 201: Fog upslope
air adiabatically cools and saturates as it is forced up a slope
vfc©

## Slide 202: Fog steam
warm water evaporates into the colder air lying just above it, saturating the air
vfc©
Notes: Steam fog forms when very cold arctic air moves over relatively warmer water. In this case moisture evaporates from the water surface and saturates the air. The extremely cold air cannot hold all the evaporated moisture, so the excess condenses into fog. The result looks like steam or smoke rising from the water, and is usually no more than 50 to 100 feet thick. Steam fog, also called arctic sea smoke, can produce significant icing conditions.

## Slide 203: Fog precipitation
precipitation evaporates into air it is falling through, saturating it to its dewpoint
vfc©
Notes: Precipitation fog, or frontal fog, forms ahead of warm fronts when precipitation falls through a cooler layer of air near the ground. The precipitation saturates the air at the surface and fog forms. Breaks in the precipitation usually results in the fog becoming thicker.

## Slide 204: Fog ice
the droplets in extremely cold saturated air freeze in suspension
vfc©
Notes: Ice fog occurs when water vapour sublimates directly into ice crystals. In conditions of light winds and temperatures colder than -30°C or so, water vapour from manmade sources or cracks in ice-covered rivers can form widespread and persistent ice fog. The fog produced by local heating systems, and even aircraft engines, can reduce the local visibility to near zero, closing an airport for hours or even days.

## Slide 205: Fog ice
hot exhaust gases saturate cold air extremely quickly, producing ice fog, in this case known as contrails
vfc©

## Slide 206: Fog ice
the ellusive twin engined stork
vfc©

## Slide 207: icing
vfc©

## Slide 208: Icing super cooled
supercooled water droplet impact by an aircraft wing at temperatures below freezing will cause icing
the quantity of supercooled droplets is dependent on the liquid water content of the cloud
clouds formed to due convection, lee wave turbulence, and orographic lift contain the largest size of water droplets due to their powerful lift
vfc©

## Slide 209: Icing rime
rime ice is milky-white, opaque, and is formed by almost instantaneous freezing of small water droplets at temperatures well below freezing
it tends to form only on the leading edges of airfoils, and builds forward into the airstream
because it is not very adhesive, it is relatively easy to remove with de-icing equipment
vfc©

## Slide 210: Icing clear
clear ice may vary from a transparent appearance to a very rough, opaque texture created from by a slow freezing process of large water droplets
the free droplet that didn’t freeze on initial impact moves aft and continues to freeze at temperatures not far below freezing
it may spread from the leading edges of the aircraft to cover it entirely in severe cases
vfc©

## Slide 211: Icing clear
because of its irregular freezing process it may create unique shapes the protrude from the aircraft
it is tougher to remove with de-icing equipment than rime
clear icing is a greater hazard than rime icing
vfc©

## Slide 212: Icing mixed
mixed icing is a combination of rime and clear
frequently the cloud temperature and range of droplet sizes are such that conditions are conducive to mixed ice formation
vfc©

## Slide 213: Icing types
vfc©

## Slide 214: Icing temperature
warm air will present a greater quantity of water droplets than cold air
larger droplets begin to spontaneously freeze to crystals around -10°C
colder temperatures are required to freeze smaller droplets
vfc©

## Slide 215: Icing temperature
the rate of freezing markedly increases at temperatures just below -15°C
larger droplets begin to spontaneously freeze to crystals around -10°C
by -40°C virtually all droplets will have frozen, therefore the chances of aircraft icing below -40°C are lower
vfc©

## Slide 216: Icing intensity
trace icing accumulates at a rate only slightly greater than it sublimates
not hazardous, even without anti/de-ice equipment, unless encountered for over an hour
vfc©

## Slide 217: Icing intensity
light icing may pose a problem if encountered for more than an hour
does not pose a problem if anti/de-ice equipment is installed and used
vfc©

## Slide 218: Icing intensity
moderate icing creates potentially hazardous situations, even if encountered for a short period of time
use of anti-de-ice equipment, or a diversion, is necessary
vfc©

## Slide 219: Icing intensity
severe icing accumulates at a rate such that anti/de-ice equipment does not decrease the hazard
an immediate diversion is the one and only option
vfc©

## Slide 220: Icing intensity
these terms of intensity are subjective to each individual aircraft
whether the icing intensity is light for one aircraft and medium for another depends on the qualitative effect on flight characteristics, and should be determined on a case by case basis
vfc©

## Slide 221: Icing freezing process
when a super cooled droplet freezes, latent heat of fusion is released which warms the remaining droplet to 0°C
droplet continues to freeze, but more slowly
fraction of droplet that initially freezes greater with colder temperatures
after initial impact, rate of freezing depends on temperature of aircraft skin and air temperature
vfc©

## Slide 222: Icing freezing process
vfc©

## Slide 223: Icing in clear air
icing in clear air is possible, meaning you DO NOT have to be in cloud to accumulate ice
ice accumulation in clear air is known as hoar frost
vfc©

## Slide 224: Icing hoar frost
hoar frost is a crystalline, feathery-white frost that may cover an entire aircraft
similar to the frost that forms on a car roof on cold, clear nights
forms due to deposition as warm, moist air comes in contact with a sufficiently cold surface
vfc©

## Slide 225: Icing hoar frost
parked aircraft are susceptible to hoar frost formation, especially on their upper surfaces as they radiately cool
hoar frost may also form on aircraft in flight that have been cold-soaked by flying at temperatures below freezing and then descend into warm, moist air
frequently the frost forms in the vicinity of integral fuel tanks as the cold fuel warms slower than the rest of the aircraft
vfc©

## Slide 226: Icing collection efficiency
collection efficiency is the fraction of liquid water which collects as ice on an aircraft
this efficiency varies directly with droplet size, aircraft speed and inversely with the geometric size of the collecting surface
a thin, fast wing travelling through an area containing large supercooled water droplets will be most efficient in ice collection
vfc©

## Slide 227: Icing collection efficiency
vfc©

## Slide 228: Icing law
it is against the law to take-off with any ice accumulation on an aircraft’s critical surfaces
CAR 602.11 (2): no person shall conduct or attempt to conduct a take-off in an aircraft that has frost, ice or snow adhering to any of its critical surfaces
critical surfaces means the wings, control surfaces, rotors, propellers, horizontal stabilizers, vertical stabilizers or any other stabilizing surface of the aircraft
vfc©

## Slide 229: Icing effect
it must be understood that every effect of aircraft icing has the potential to be extremely hazardous to flight
the cumulative effect of aircraft icing is an increased stalling speed
this is the greatest danger of aircraft icing
vfc©

## Slide 230: Icing effect
vfc©

## Slide 231: mountainwave
vfc©

## Slide 232: Mountain wave disturbances
vfc©
air moves in relation to a mountain or mountain ridge which in may create a series of disturbances
air is initially forced up, followed by a sharp drop downwind of the peak
further downwind the air movement may continue as a series of wave-like oscillations termed a mountain wave

## Slide 233: Mountain wave disturbances
vfc©
the intensity of the possible oscillations is dependant on the height of the mountain, and how sharply the terrain drops off on the leeward side
the greater the height and the sharper the drop-off, the greater the oscillation
the wave length downwind averages 6 miles, with an amplitude up to 3000’

## Slide 234: Mountain wave dimensions
vfc©

## Slide 235: Mountain wave clouds
vfc©
if conditions are favourable, tell-tale clouds will form in certain parts of the wave
these should be used as warning signs of the inherent dangers of mountain waves

## Slide 236: Mountain wave cap cloud
vfc©

## Slide 237: Mountain wave cap cloud
vfc©

## Slide 238: Mountain wave roll cloud
vfc©

## Slide 239: Mountain wave lenticular cloud
vfc©

## Slide 240: Mountain wave lenticular cloud
vfc©

## Slide 241: Mountain wave dangers
vfc©
windshear
turbulence
convective currents
altimeter error
icing

## Slide 242: Mountain wave dangers
vfc©

## Slide 243: thunderstorm
vfc©

## Slide 244: Thunderstorm formation
thunderstorm formation depends on air characteristics
warm air with a high moisture content, instability, a steep lapse rate and a convective lifting agent will promote thunderstorm formation
the latent heat of vaporization in the lower region of the cloud, and of fusion in the upper region of the cloud accelerate the initial updraft and grow the cumulonimbus
vfc©

## Slide 245: Thunderstorm stages
thunderstorm stages are identified by the shape of the cloud, the direction of air movement within the cloud, and the occurrence of precipitation
there are three main stages of the thunderstorm
vfc©

## Slide 246: Thunderstorm cumulus
vfc©
the first stage is the cumulus stage, when numerous small convective clouds merge and rapidly grow into a very large cell
only updrafts exist in the cumulus stage, are greatest in the upper levels and may reach 3000’ per minute
ice crystals and then rain form as cell builds past the freezing level, with drops eventually falling in cloud as they grow more massive
cumulus stage lasts about 20 minutes

## Slide 247: Thunderstorm cumulus
vfc©

## Slide 248: Thunderstorm mature
the mature stage is marked by precipitation at earth’s surface
the cloud continues to grow, with updrafts reaching 6000’ per minute
strong winds in the tropopause carry the cloud ahead of the storm, creating a characteristic anvil shape
vfc©

## Slide 249: Thunderstorm anvil
vfc©

## Slide 250: Thunderstorm mature
precipitation drags air in the cloud down with it, and evaporation cools the air strengthening the downdraft mid-cloud
a gust front is created when this air pours out of the cloud and reaches the surface, spreading out
the gust front is marked by gusty surface winds, a sharp drop in temperature and abrupt rise in pressure
vfc©

## Slide 251: Thunderstorm mature
ahead of the gust front, air rises up and over the incoming cold down-flowing air, flowing into the storm
as the gust front passes wind veers violently, sometimes up to 180°
the downdraft may originate short-lived but extremely violent winds known as microbursts
vfc©

## Slide 252: Thunderstorm mature
vfc©

## Slide 253: Thunderstorm mature
hail is most likely during the mature stage
Super cooled droplets begin to freeze, and other drops coalesce on them as they are cycled through the cloud, growing is size
small hail may be carried up and ejected laterally from the cloud
vfc©

## Slide 254: Thunderstorm mature
lightning is a discharge from negative to positive within cloud, from cloud to ground or rarely from ground to cloud
thunder is the resultant noise as lightning heats the air so that it expands more rapidly than the speed of sound
the distance in miles to the lightning strike is estimated by counting seconds between lightning and thunder and dividing the number by five
vfc©

## Slide 255: Thunderstorm mature
mature stage is the most violent stage
precipitation is most intense near the end of this stage
lasts for about 20-30 minutes
its end is marked by the updraft weakening and downdraft encompassing the entire cell
vfc©

## Slide 256: Thunderstorm mature
vfc©

## Slide 257: Thunderstorm dissipating
entire cell is a downdraft
mechanisms which generate precipitation, lightning, turbulence do not exist
longest yet least hazardous stage
vfc©

## Slide 258: Thunderstorm mature
vfc©

## Slide 259: Thunderstorm cells
a thunderstorm usually consists of two or more cells in different stages of their life cycles
vfc©

## Slide 260: Thunderstorm classification
thunderstorms are classified based on the lifting action that triggers instability
vfc©

## Slide 261: Thunderstorm warm front
vfc©

## Slide 262: Thunderstorm cold front
vfc©

## Slide 263: Thunderstorm convective
vfc©

## Slide 264: Thunderstorm orographic
vfc©

## Slide 265: Thunderstorm hazards
vfc©

## Slide 266: airmass
vfc©

## Slide 267: Air mass defined
an air mass is a large body of air, 1000 or more miles across
across the horizontal, an air mass has acquired fairly uniform properties of temperature and moisture
topped by the tropopause
vfc©

## Slide 268: Air mass characteristics
the air mass characterizes the type of weather seen within it
they are classified based on their two defining properties
vfc©

## Slide 269: Air mass classification
there are three relatively dry air masses:
continental arctic - cA
continental polar - cP
continental tropic - cT
vfc©

## Slide 270: Air mass classification
there are three relatively moist air masses:
maritime arctic - mA
maritime polar - mP
maritime tropic - mT
vfc©

## Slide 271: Air mass classification
continental arctic is the coldest driest air mass, has a very low tropopause and is very stable
maritime tropic is very warm and moist, has a high tropopause, and is very unstable
continental tropic has the highest tropopause, is very unstable and its source region is very small in North America
vfc©

## Slide 272: Air mass structure
vfc©
the warmer the air mass, the higher and colder its tropopause

## Slide 273: Air mass source regions
if an air mass remains over a particular region for an extended period of time it will acquire the properties of that region
these regions are termed source regions
vfc©

## Slide 274: Air mass modification
if an air mass moves out of its source region, it may modify to become a new air mass
the degree of modification depends on the speed at which the mass is moving, and the moisture content and temperature difference between the mass and the new source region
vfc©

## Slide 275: Air mass warming from below
an air mass warmed from below will develop convection and instability in its lower levels, which may be carried aloft
vfc©

## Slide 276: Air mass cooling from below
an air mass cooled from below will develop stability in its lower levels, and modification is confined to the first few thousand feet
vfc©

## Slide 277: Air mass source regions
vfc©

## Slide 278: fronts
vfc©

## Slide 279: Fronts defined
cold, dense air does not readily mix with warm, less dense air
along the border of two air masses, there is a relatively short transition zone of temperature change within 50-100 miles
this is a front, or frontal system
vfc©

## Slide 280: Fronts nomenclature
fronts are named based on the colder air mass involved
this means it is the relative movement of cold air with relation to the warm air that describes a front
vfc©

## Slide 281: Fronts frontal systems
vfc©

## Slide 282: Fronts cold
the advancing edge of a cold air mass is termed a cold front
the cold air advances towards, and eventually will catch up with, the warm air
vfc©

## Slide 283: Fronts warm
the retreating edge of a cold air mass is termed a warm front
the warm front is eventually caught up to by the cold front
or, the cold front eventually will catch up with itself
vfc©

## Slide 284: Fronts quasi-stationary
a quasi-stationary front shows little relative movement of the cold air
with reference to the ground, it is moving at less than 5 kts
vfc©

## Slide 285: Fronts upper
cold and warm fronts may also be referred to as upper fronts, meaning their frontal surface does not come in contact with the ground
there is an underlying mass of air with fairly uniform temperature causing the discontinuity of the frontal surface
vfc©

## Slide 286: Fronts frontogenesis
the creation of a front is termed frontogenesis
this occurs when wind increases the temperature contrast within one air mass, creating two areas of differing temperature
vfc©

## Slide 287: Fronts frontolysis
the dissipation of a front is termed frontolysis
this occurs when wind decreases the temperature contrast between two air masses to a point where there is no need for the front to exist
modification of two air masses that remain over the same source region may also cause frontolysis
vfc©

## Slide 288: Fronts structure
remember that a front is in fact a mixing zone of air 50-100 miles across
vfc©

## Slide 289: Fronts structure
it is important to see fronts from all perspectives to fully understand them
vfc©

## Slide 290: Fronts inversion
an inversion is encountered during ascent from the surface through a cold front
vfc©

## Slide 291: Fronts North America
vfc©

## Slide 292: Fronts motion
vfc©
frontal motion is dependent on the movement of the cold air perpendicular to it
the motion of the warm air does not affect frontal movement
this is true at both the cold front and the warm front

## Slide 293: Fronts motion
vfc©

## Slide 294: Fronts slope
vfc©
the slope a frontal surface makes with earth’s surface is extremely shallow, and in all cases it is in the realm of one degree
the shape of the frontal surface however varies significantly between the various fronts

## Slide 295: Fronts slope
vfc©

## Slide 296: Fronts going up
vfc©
two terms are used to describe the upwards movement that the warm air experiences at the cold and the warm front
at the warm front, the warm air overruns the retreating cold air, and it is lifted aloft
at the cold front, the advancing cold air aggressively lifts the warm air as it undercuts, creating frontal lift

## Slide 297: Fronts frontal lift
vfc©

## Slide 298: Fronts over running
vfc©

## Slide 299: Fronts passage
vfc©
it is important to note the changes with respect to wind, temperature and pressure with both cold and warm front passage
these changes may appear in advance of a front passing, or be evident only during or after its passage

## Slide 300: Fronts cold front passage
vfc©
weather | before passage | with passage | after passage
temperature | warm | suddenly cooling | steady cooling
pressure | decreasing | decreasing to lowest point, then sudden increase | steady increase
winds | backing | variable, gusting | veering
visibility | fair to poor | poor but improving | good, except during showers

## Slide 301: Fronts warm front passage
vfc©
weather | before passage | with passage | after passage
temperature | cool | sudden warming | warming, then sustaining
pressure | decreasing | sustaining | slight rise then decrease
winds | backing | variable | veering
visibility | poor | improving | fair

## Slide 302: Fronts waves
vfc©
wave-like disturbances may form on quasi-stationary fronts that can produce extensive areas of cloud and precipitation
these waves may be stable or unstable

## Slide 303: Fronts stable wave
vfc©

## Slide 304: Fronts unstable wave
vfc©

## Slide 305: Fronts trowal
vfc©
the trough of warm air that is lifted aloft during an unstable wave is termed a trowal

## Slide 306: Fronts occlusion
vfc©
the advancing cold front catching up to the warm front is termed an occlusion
it is a like a doing up a zipper with the resultant being a wedge of warm air pushed aloft
remember that in essence this is the cold front catching up to its own tail

## Slide 307: Fronts occlusion
vfc©

## Slide 308: Fronts cold front occlusion
cold air advances on and lifts its retreating cool tail, which in turn lifts warm air aloft
vfc©

## Slide 309: Fronts warm front occlusion
cool air advances on and overruns its retreating cold tail, which lifts warm air aloft
vfc©

## Slide 310: Fronts weather
vfc©
each type of front creates a specific type of weather
this can range from little cloud formation with no precipitation, to aggressive thunderstorms with intense precipitation
the weather seen at the front depends on the characteristics of the warm air mass

## Slide 311: Fronts cold front weather
vfc©

## Slide 312: Fronts warm front weather
vfc©

## Slide 313: Fronts winter warm front
rain falling from cloud in the cold air sector at a warm front has the potential to cause freezing rain and dangerous icing conditions
vfc©

## Slide 314: Fronts winter warm front
vfc©

## Slide 315: Fronts trowal weather
vfc©

## Slide 316: Day 3
vfc©
met advanced theory continued, jet stream, aviation weather products, sample exam and take-up

## Slide 317: jetstream
vfc©

## Slide 318: Jetstream defined
vfc©
jet streams are fast moving, narrow corridors of air within the main airflow
they may be thousands of miles long, hundreds of miles wide and a few thousand feet thick
the wind speed must be a minimum of 60 kts to qualify as a jet stream, and speeds in excess of 200 kts may occur

## Slide 319: Jetstream frontal
vfc©
jet streams may be associated with frontal systems
they flow parallel to the surface position of the front, crossing at the point of occlusion and circling northwards around the low
the jet takes the name of the front causing it - arctic, polar or maritime

## Slide 320: Jetstream frontal
vfc©

## Slide 321: Jetstream frontal
vfc©
jet streams flow easterly, below the warm air tropopause of a front, and at approximately the same level of the cold air tropopause
looking down the jet stream, air rotates counter-clockwise, rising to the south and descending to the north
if the ascending air is moist, cirrus clouds may form, with fibrous edges denoting the strong vertical shear

## Slide 322: Jetstream structure
vfc©

## Slide 323: Jetstream structure
vfc©

## Slide 324: Jetstream variation
vfc©
the jet stream position varies with the movement of the front it is associated with
the fronts themselves migrate depending on the season
the tropopause is higher in summer, and lower in winter
jet streams also meander in height along their length

## Slide 325: Jetstream variation
vfc©
during winter in the mid-latitudes in the northern hemisphere, there is a greater temperature contrast over land areas than in summer
fronts move further to the south in winter with lower tropopause heights
associated frontal jet streams are therefore lower and stronger in intensity (due to the greater temperature contrast) in winter than in summer

## Slide 326: navcanada
vfc©

## Slide 327: Nav Canada provider
Nav Canada is Canada’s civil air navigation service provider of...
air traffic control
flight information
weather briefings
vfc©

## Slide 328: Nav Canada provider
aeronautical information services
airport advisory services
electronic aids to navigation
the aviation weather website - AWWS
vfc©

## Slide 329: Nav Canada weather briefings
one way aviation weather may be obtained is through a pilot interpretative weather briefing provided by a NavCanada flight information center (FIC)
FICs may be contacted via toll free telephone from anywhere in Canada
1-866-WXBRIEF (1-866-992-7433)
vfc©

## Slide 330: Nav Canada FIC
vfc©

## Slide 331: Nav Canada weather briefings
when calling for a weather briefing, be prepared to give the following information:
aircraft registration and type
operation type - VFR
route
estimated zulu time of departure
planned altitude
estimated time en route
vfc©

## Slide 332: Nav Canada inflight weather
there are numerous ways to obtain weather information during flight
air traffic control
FICs via “Pacific Radio”
ATIS
voice generator module
vfc©

## Slide 333: Nav Canada inflight weather
there are numerous ways to obtain weather information during flight
air traffic control
FICs via “Pacific Radio”
ATIS
voice generator module
vfc©

## Slide 334: information
metar
taf
notam
pirep
fd
bkn
few
sct
ovc
SLP987
A2976
tempo
fm
prob30
becmg
ra
sc3
10018G25KT
speci
awos
rmk
cig
br
+snsh
fu
-dz
pressrr
fldurd
hj
1803Z
VV002
skc
cb
tcu
sf4
blsa
fc
ws
RVRRWY331200V2600
fg
3/4SM
cyyj
fzdz
auto
vis
M01/M05
fcst
ua
rime
nil
blo040
cu2st4acc1
10/03
lwis
FL080
mdt
vfc©

## Slide 335: Information sources and references
vfc©

## Slide 336: Information classification
vfc©

## Slide 337: Information METAR
a METAR is an aviation routine weather report
it observes actual weather conditions, as observed from the ground, within a 5 NM radius of the reporting station
the report is composed of several coded groups, always in the same relative position
vfc©

## Slide 338: Information METAR
vfc©
METAR CYYJ 250000Z CCA 13015G25KT 3/4SM R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=

## Slide 339: Metar report type
vfc©
CYYJ 250000Z CCA 13015G25KT 3/4SM R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
METAR
signifies a METAR report
always issued on the top of the zulu hour
issued 24 hours per day at all international airports in Canada

## Slide 340: Metar station
4 letter ICAO identifier of the reporting station
all Canadian stations commence with “C”
vfc©
METAR 250000Z CCA 13015G25KT 3/4SM R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
CYYJ

## Slide 341: Metar date and time
the day of the month is followed by the zulu time of the report issuance
zulu time is exclusively used in aviation weather
vfc©
METAR CYYJ CCA 13015G25KT 3/4SM R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
250000Z

## Slide 342: Metar correction
this code is used to correct a previous report due to observer or instrumentation error
the first correction uses the designator “A”, the second correction “B” etc.
vfc©
METAR CYYJ 250000Z 13015G25KT 3/4SM R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
CCA

## Slide 343: Metar wind
wind is reported as a two minute mean direction and speed, including gusts if observed
gusts are included if in the ten minutes prior to the report, the gust exceeds mean wind by 5 kts or more, and the gust itself is 15 kts or stronger
wind direction in metar is always reported as true
vfc©
METAR CYYJ 250000Z CCA 3/4SM R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
13015G25KT

## Slide 344: Metar visibility
the minimum prevailing ground visibility is reported in statute miles (SM)
an observer can only see point to point, along a statute mile
nautical miles are never used to report visibility
vfc©
METAR CYYJ 250000Z CCA 13015G25KT R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
3/4SM

## Slide 345: Metar runway visual range
runway visual range (RVR) reports ground visibility in feet if below 1 NM for a particular runway
trend is indicated if the visibility changes 300’ or more in the five minutes preceeding observation
/U = upwards trend
/D = downwards trend
/N = no distinct trend
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
    -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
R27/4000FT/D

## Slide 346: Metar present weather
this code describes one or more forms of precipitation, obscuration or other phenomenon
placed before the code are descriptors of intensity, proximity to the station, or other
present weather is coded by the World Meteorological Organization Code, table 4678
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
    R27/4000FT/D BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
-DZ BR

## Slide 347: Metar present weather
vfc©

## Slide 348: Metar sky condition
cloud bases are reported in hundreds of feet AGL
placed before these altitudes are summative terms that describe, in oktas (eighths), coverage of the sky
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
    R27/4000FT/D -DZ BR 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
    BKN002 OVC005

## Slide 349: Metar sky condition
vfc©
FEW (few)
<0/8 - 2/8
SCT (scattered)
<2/8 - 4/8
BKN (broken)
<4/8 - >8/8
OVC
(overcast) 8/8

## Slide 350
2/8
1/8
3/8
2/8
+
FEW
SCT
+
BKN
+
OVC
10 NM

## Slide 351: Metar sky condition
the height of the first reported layer of broken (BKN), overcast (OVC) or vertical visbility (VV) is termed a ceiling
a VFR pilot may not fly above the altitude of a summative cloud ceiling
this is true even if there is clear air below and the ground is visible
vfc©

## Slide 352
1/8
FEW
2/8
SCT
3/8
BKN
2/8
OVC
10 NM

## Slide 353: Metar temperature and dew point
temperature and dewpoint are rounded to the nearest Celsius degree
the spread between them is an expression of relative humidity
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
    R27/4000FT/D -DZ BR BKN002 OVC005 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
    08/08

## Slide 354: Metar altimeter setting
the altimeter setting is reported to the nearest hundredth of “ Hg
insert the decimal before the 2nd to last number of the group
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
    R27/4000FT/D -DZ BR BKN002 OVC005 08/08 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
    A3026

## Slide 355: Metar recent weather
recent weather of operational significance is reported here
this includes precipitation, blowing snow, storms or volcanic ash
recent implies the weather was seen following the previous report, but not at the issuing time of the current report
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
    RERA

## Slide 356: Metar wind shear
windshear, if known, is reported when occurring within 1600‘ AGL along an approach or departure path of a specific runway
this knowledge should be combined with the mean wind observance to identify the specific type of performance shear
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA RMK SF5SF3 VIS 3/8 TO NW SLP247=
    WS RWY27

## Slide 357: Metar remarks
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 VIS 3/8 TO NW SLP247=
        RMK SF5SF3
the first group of the remarks section indicates the cloud type of each layer, as well as the individual opacity (coverage) of each cloud layer, that was reported by sky condition
sky condition and this section of the remarks should to be used together to gain a complete picture of the observed cloud

## Slide 358: Metar remarks
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR 08/08 A3026 RERA WS RWY27 RMK VIS 3/8 TO NW SLP247=
        SF5
        SF3
        BKN002
        OVC005
10 NM

## Slide 359: Metar remarks
sector visibility is reported if half or less of the prevailing visibility is observed in a particular sector
the sector visibility, in SM, is followed by which sector is reporting it, as a compass direction referenced from the station
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 SLP247=
        VIS 3/8 TO NW

## Slide 360: Metar remarks
sea level pressure is the last part of the remarks code
it is abbreviated, and expressed in millibars
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW
        SLP247 =

## Slide 361: Metar remarks
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW
        SLP247 =
9/
mb
247
.
10

## Slide 362: Speci off hour
between METAR issuances, weather conditions may change
if conditions change such that a new report is warranted, an off-hour report of similar format to a METAR will be issued
this observance is termed a SPECI
vfc©

## Slide 363: Speci off hour
a SPECI may describe the commencement, cessation or change in sky condition, visibility, wind, precipitation, temperature or severe weather phenomena
a SPECI does not report observed changes in dew point, altimeter setting, or sea level pressure
vfc©

## Slide 364: Speci off hour
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247 =
      SPECI CYYJ 250023Z 18022G37KT 3/8SM R27/1200FT/D FZRA BKN001 OVC003 M01/ RMK SF6ST3=

## Slide 365: Awos automated
at some weather stations it is not feasible to have a human observer
at these stations, automated weather observation system (AWOS) sensors may be installed
vfc©

## Slide 366: Awos automated
AWOS sensors are capable of measuring wind, layer height, sky cover, visibility, temperature, dew point, altimeter setting, precipitation, icing and sea level pressure
to indicate AWOS sensors are being used, the term AUTO is used after the date/time group in a METAR or SPECI code
vfc©

## Slide 367: Awos automated
vfc©
METAR CYHE 072100Z AUTO 14008KT 9SM CLR M04/M19 A3021 RMK SLP233=

## Slide 368: metar/speci accessing
vfc©

## Slide 369: Taf terminal areadrome forecast
vfc©
the terminal areadrome forecast (TAF) is to a local forecast what the METAR is to a local observation
the TAF forecasts within a 5 NM radius of the forecasting station
the TAF is always coded in groups in the same relative position to one another

## Slide 370: Taf terminal areadrome forecast
vfc©
at international airports in Canada the TAF is valid for a minimum of 24 hours up to a maximum of 30 under the ICAO format
other stations may issue TAFs for shorter validity periods, depending on operational requirements
TAFs are issued at least every six hours

## Slide 371: Taf stations
vfc©

## Slide 372: Taf example
vfc©

## Slide 373: Taf example
vfc©
TAF CYDN 291145Z 2912/3012 24010G25KT WS01127050KT 3SM -SN BKN010 OVC040 TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z

## Slide 374: Taf station identifier
vfc©
291145Z 2912/3012 24010G25KT WS01127050KT 3SM -SN BKN010 OVC040 TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
TAF CYDN
station identifier, ICAO format
TAF is the international format for an aerodrome forecast, if corrected will be indicated by AMD (amended)

## Slide 375: Taf issuance
TAF CYDN 2912/3012 24010G25KT WS01127050KT 3SM -SN BKN010 OVC040 TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
vfc©
the TAF issuing date and time are consistent with the METAR format
291145Z

## Slide 376: Taf validity
vfc©
validity time is coded as a time bracket, from a specific day and zulu hour, until a specific zulu hour
this start and end bracket is separated by a forward slash
TAF CYDN 291145Z 24010G25KT WS01127050KT 3SM -SN BKN010 OVC040 TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
2912/3012

## Slide 377: Taf wind
vfc©
wind is forecast in degrees true and in knots
if it’s written, it’s true
the same gust criteria as METAR applies
TAF CYDN 291145Z 2912/3012 WS01127050KT 3SM -SN BKN010 OVC040 TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
24010G25KT

## Slide 378: Taf wind shear
vfc©
wind shear is forecast if the forecaster has strong evidence to believe that significant, non-convective wind shear will occur within 1500‘AGL of the station
often this evidence is based on pilot report
  TAF CYDN 291145Z 2912/3012 24010G25KT
  3SM -SN BKN010 OVC040 TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
WS01127050KT

## Slide 379: Taf visibility and sig weather
vfc©
prevailing visibility is forecast up to 3 SM in miles or fractions thereof, and then in whole SM up to 6 SM
visibilities forecast to be greater than 6 SM are coded as P6SM
significant weather codes are consistent with METAR
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT BKN010 OVC040 TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
  3SM -SN

## Slide 380: Taf sky condition
vfc©
cloud layers are consistent with METAR
forecast layers are summative in feet AGL
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT 3SM -SN TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
  BKN010 OVC040

## Slide 381: Taf tempo
vfc©
the TEMPO is a temporary change group of certain weather elements
weather groups following the abbreviation TEMPO will differ from those groups before it
TEMPO is in time bracket format
TEMPO states the changing elements will occur for no more than one hour, and if forecast to reoccur, will occur for a sum total of no more than 50% of the time bracket
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT 3SM -SN BKN010 OVC040
  1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
  TEMPO 2918/3001

## Slide 382: Taf tempo
vfc©
the changing elements are consistently coded
if a weather group is not indicated by TEMPO, it remains unchanged, as previously forecast
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT 3SM -SN BKN010 OVC040
  TEMPO 2918/3001 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
  1 1/2SM -SN BLSN BKN008

## Slide 383: Taf prob
vfc©
PROB describes the forecast probability of a change
it is included if there is the probability of thunderstorms, freezing precipitation or ceilings/visibility which may approach operational minima
PROB only indicates either a 30% or 40% chance of the forecast weather occurring
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT 3SM -SN BKN010 OVC040
        TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008
        PROB30 2920/2922
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
        1/2SM SN VV005

## Slide 384: Taf fm
vfc©
FM is used to forecast a rapid and permanent change
there is no time bracket associated with FM
it is a new, complete forecast within a TAF
even if elements are forecast to remain unchanged, they will be repeated within the FM change code
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT 3SM -SN BKN010 OVC040
        TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008
        PROB30 2920/2922 1/2SM SN VV005
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
FM300130 28010KT 5SM -SN BKN020

## Slide 385: Taf becmg
vfc©
BECMG is a gradual, permanent change
it is used when up to two elements are forecast to gradually change
the time bracket format is used
if a permanent change is expected in more than two elements, FM will be used
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT 3SM -SN BKN010 OVC040
        TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008
        PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
BECMG 3006/3008 00000KT SKC

## Slide 386: Taf becmg
vfc©
the remarks code will indicate if the forecast is based on AWOS
it will also indicate the time at which the next TAF will be issued by
TAF issuance commonly precedes its validity period by more than twenty minutes
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT 3SM -SN BKN010 OVC040
        TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008
        PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z

## Slide 387: Taf accessing
vfc©

## Slide 388: Fd upper wind and temp
vfc©
the upper level wind and temperature forecast is know as FD
to generate this forecast, data is collected twice daily (00Z, 12Z) from 32 sites across Canada

## Slide 389: Fd upper wind and temp
vfc©
wind direction (rounded to the nearest 10° true) and speed are forecast for all levels in 3000‘ increments ASL
temperature is forecast for all but the 3000‘ level, due to low level temperature variation

## Slide 390: Fd upper wind and temp
vfc©

## Slide 391: Fd accessing
vfc©

## Slide 392: Pirep pilot report
vfc©
PIREP is a report of weather conditions encountered in flight by other pilots
PIREP is invaluable, and pilots are encouraged to file them, especially when significant weather phenomena are observed
PIREP reported as UACN10 are regular
PIREP reported as UACN01 are urgent

## Slide 393: Pirep example
vfc©
UACN01 CYEG 270202 EG UUA /OV YYC 340010 /TM 0200 /FLUNKN /TP UNKN /RM PILOT ON GROUND REPORTS TORNADO MOVING WEST TO EAST
UACN01 CYKA 301613 VR UUA /OV CYVR 145030 /TM 1609 /FLDURD /TP DH8D /IC SEV MXD 090-120 /RM 20-30 NM ON GRIZZ.3 ARR IN CYVR. ACFT HAD NO CHOICE BUT TO DSND

## Slide 394: Pirep accessing
vfc©

## Slide 395: Information classification
vfc©

## Slide 396: Graphical weather visual
vfc©
graphical weather uses a combination of symbology and alphanumeric code overlaid on a geographic map to create a weather analysis or forecast
the graphical area forecast (GFA) is one such product

## Slide 397: Gfa background
vfc©
graphical weather uses a combination of symbology and alphanumeric code overlaid on a geographic map to create a weather analysis or forecast
the graphical area forecast (GFA) is one such product

## Slide 398: Gfa coverage
vfc©
seven GFA domains provide complete domestic coverage of Canada
it consists of a series of weather charts that provide a 24 hour depiction of the most probable weather conditions forecast to occur over a specific area at a specific time, from the surface to 24000’ ASL

## Slide 399: Gfa defined
vfc©
each GFA is in fact a series of weather charts, which are grouped into three sets
each set contains a chart that forecasts clouds and weather, and another chart that forecasts icing, turbulence, and the height of the freezing level

## Slide 400: Gfa 24 hour coverage
vfc©
the first GFA set is valid at the beginning of the forecast period, for six hours
the second set is valid six hours into the forecast period, for six hours
the third GFA set is valid twelve hours into the forecast period, for twelve hours
this creates a comprehensive 24 hour forecast

## Slide 401: Gfa issuance and validity
vfc©
GFA is issued every six hours, with four issuances a day
the issuance, as with any forecast, precedes validity time
GFA is issued before the top of the 0000, 0600, 1200 and 1800 zulu hours, the respective hours when each GFA becomes valid
every time GFA is issued the previous GFA is superseded

## Slide 402: Gfa issuance and validity
vfc©
GFA is issued every six hours, with four issuances a day
the issuance, as with any forecast, precedes validity time
GFA is issued before the top of the 0000, 0600, 1200 and 1800 zulu hours, the respective hours when each GFA becomes valid
every time GFA is issued the previous GFA is superseded

## Slide 403: Gfa issuance
vfc©
0000Z
0600Z
1200Z
1800Z
1st set
2nd set
3rd set

## Slide 404: Gfa IFR outlook
vfc©
the third clouds and weather chart contains an additional IFR outlook
this will forecast IFR conditions based on the following criteria, for the 12 hour period the 3rd clouds and weather chart represents

## Slide 405
vfc©
Gfa example

## Slide 406: Gfa set 1
vfc©

## Slide 407: Gfa set 2
vfc©

## Slide 408: Gfa set 3
vfc©

## Slide 409: Gfa accessing
vfc©

## Slide 410: Gfa amendments
vfc©
one way GFA is amended by SIGMET
SIGMET is a short-term weather advisory to warn pilots of certain potentially hazardous weather phenomena
SIGMET is broadcast on appropriate IFR and VFR ATS frequencies upon receipt

## Slide 411: Gfa amendments
vfc©
GFA is also amended by AIRMET
AIRMET is a short-term weather advisory to warn pilots of certain potentially hazardous weather phenomena, not warranting the issuance of SIGMET
SIGMET or AIRMET will be issued for weather occurrence without forecast, or non-occurrence with forecast

## Slide 412: Sigmet example
vfc©
SIGMET
SIGMETS GFACN31
WSCN31 CWEG 131750 SIGMET M4 VALID 131750/132150 CWEG- WTN 25 NM OF LN /4936N12722W/65 S PORT HARDY - /5112N12812W/45 NW PORT HARDY - /5158N12814W/25 SE MCINNES ISLAND. PTCHY SEV MECH/LLWS TURB FCST BLO 040. SOLANDER ISLAND REPD SE60G72KT AT 1700Z. AREA QS. LTL CHG EXPD. END/GFA31/RGH/CMAC-W
WSCN31 CWEG 131633 SIGMET N1 VALID 131635/132035 CWEG- WTN 45 NM OF LN /5206N12448W/25 W PUNTZI MOUNTAIN - /4916N12028W/30 E HOPE. PTCHY SEV LEE WV/MECH TURB FCST BLO 100 DUE STG SWLY WNDS ALF. AREA QS. LTL CHG EXPD. END/1/GFA31/RGH/CMAC-W

## Slide 413: airmet/sigmet accessing
vfc©

## Slide 414: Sigwx mid level
vfc©
the significant weather mid-level prognostic chart covers all of Canada
it represents the 700mb to 400mb levels (FL100 to FL240)
they forecast icing, cloud layers of significance, marked mountain waves, FZLVL at 5000’ intervals, surface position and direction of movement of highs, lows, troughs etc.
issued four times per day, 12 hours before validity

## Slide 415: Sigwx high level
vfc©
the significant weather high-level prognostic chart is produced by the world area forecast center (WAFC)
it represents from FL250 to FL630
it shows occurring or forecast weather conditions of concern to high level aircraft operations (ie. the jet stream, tropopause height, frontal positions etc.)
issued four times per day, 12 hours before validity

## Slide 416: Sig weather
vfc©

## Slide 417: Sig weather accessing
vfc©

## Slide 418: Analysis charts anal
vfc©
certain weather parameters in the upper atmosphere are measured on constant pressure level charts
four pressure levels in Canada are recorded: 850mb (5000’), 700mb (10,000’), 500mb (18,000’) and 250mb (34,000’)
they are not forecast charts - they indicate past conditions
issued twice daily at 0000Z and 1200Z

## Slide 419: Analysis charts anal
vfc©

## Slide 420: Analysis charts anal
vfc©
analysis charts represent a common pressure level, not a constant altitude
highs and lows marked on the charts indicate the highest and lowest altitudes of the pressure level in that area
constant pressure level charts are useful as an aircraft flying a constant indicated altitude is flying a constant pressure level
therefore variations in aircraft altitude can be determined based on the contour lines indicated on ANAL charts

## Slide 421: analysis
vfc©

## Slide 422: Analysis accessing
vfc©

## Slide 423: Notam notice to airmen
vfc©
NOTAM are coded messages that describe a change to an aeronautical facility, surface, procedure or hazard
they must be checked before each flight
NOTAM code is standardized in the Canadian Notam Procedures Manual
http://www.navcanada.ca/ContentDefinitionFiles/Publications/NOTAM/NOTAM_Manual_en.pdf

## Slide 424: Notam example
vfc©
110098 CYXX HOPE
CYHE FIRST 1000 FT RWY 07 CLSD, USABLE RWY LEN REMAINING 2960 FT
TIL APRX 1103211900

## Slide 425: Notam accessing
vfc©

## Slide 426: Live RVR current wind
vfc©
LIVE RVR is a relatively new product created by NAVCANADA which displays current magnetic wind direction and speed at certain airports
this is overlaid on top of an airport diagram so is very intuitive and gives a clear relationship between runway orientation and wind direction
it is updated every 30 seconds

## Slide 427: Live RVR accessing
vfc©

## Slide 428: AWWS exploring
vfc©
the aviation weather website contains much more information than is required to be known for the CPL written test
however it should be explored as much as possible
make sure you are completely versed on the dissemination of any weather product you intend to use for flight planning purposes