## Slide 1
vfc©
weather to fly
meteorology for the commercial pilot

## Slide 2: hellomynameis
vfc©
tyler bishop
tylerbishop46@gmail.com

## Slide 3: classoutline
vfc©
http://www.tc.gc.ca/Publications/en/TP12881/PDF/HR/TP12881E.pdf
friday: pre-test, met theory
saturday: met theory, advanced theory - air mass, front
sunday: advanced theory - jet stream, aviation weather products, sample exam and take-up

## Slide 4: day1
vfc©
pre-test, met theory

## Slide 5: atmosphere
vfc©

## Slide 6: atmosphereproperties
mobility
expansion
compression
vfc©

## Slide 7: atmospherecomposition
nitrogen
78%
oxygen
21%
water vapour, CO2, argon, others
1%
vfc©

## Slide 8: atmospherethekey
water vapour is water in its gaseous, invisible form
it is the key to visible weather formation
visible weather determines the possibility of visual (VFR) flight!
vfc©

## Slide 9
troposphere
stratosphere
mesosphere
thermosphere
16
atmospheredivisions
vfc©

## Slide 10: atmospheretroposphere
28000’ deep over the poles, 54000’ deep over the equator
pressure, density and temperature all decrease as we ascend into the troposphere
most visible weather occurs in the troposphere
vfc©

## Slide 11: atmospheretropopause
a ‘pause’ is a boundary between atmopsheric divisions
the tropopause divides the troposphere and the stratosphere above
characterized by a lowest temperature of -56°C
vfc©

## Slide 12: atmospherestratosphere
50000’ to 150000’ above earth’s surface
pressure and density continue to decrease but temperature rises towards 0°C in the upper stratosphere
due to existence of the ozone layer
temperature then decreases again in the stratopause
vfc©

## Slide 13: atmospheremesosphere
150000’ to 250000’ above earth’s surface
pressure, density and temperature continue to decrease
temperature falls as low as -100°C in the mesopause
this is the coldest temperature found within the atmosphere and on earth
vfc©

## Slide 14: atmospherethermosphere
500000’ to 500km above earth’s surface
pressure, density decrease yet an extreme rise in temperature is noted with an increase in altitude
vfc©

## Slide 15: atmospherethermosphere
1500°C to 2500°C due to the kinetic theory of gases
absorbtion of intese solar radiation by few O2 molecules that remain create these high temperatures
above 160km in the thermosphere exists the anacoustic zone - no sound transmission
vfc©

## Slide 16: atmosphereandbeyond
the exososphere is the last layer of the atmophere
has an upper boundary of approximately 190000km
mainly hydrogen molecules
influence of solar radiation energy on hydrogen molecules exceeds that of earth’s gravitational pull
vfc©

## Slide 17: atmospheretemperature
vfc©

## Slide 18: atmospherestandard
for aeronautical engineering purposes, it is necessary to have a set of clearly defined standards to reference for aircraft design
pilots must be able to understand and apply this set of standards
integral in performance and altitude computations
vfc©

## Slide 19: atmosphereISAstandards
the air is a perfectly dry gas
a mean sea level pressure of 29.92” Hg
a mean sea level temperature of 15°C
the rate of decrease of temperature with altitude is 1.98°C per 1000’
vfc©

## Slide 20: atmosphereISAstandards
standard atmosphere only exists on paper
vfc©

## Slide 21: atmospherepressure
pressure is the atmosphere exerting a force on the surface of the earth
vfc©

## Slide 22: atmospherebarometer
29.92” Hg
vfc©

## Slide 23: atmospherestationpressure
1” Hg change correlates to a 1000’ change in altitude
station pressure is the atmospheric pressure at the elevation of the observing station
station pressure
vfc©

## Slide 24: atmospherestationpressure
station pressure is simply the weight of the one square inch column of air “weighing down” on the station barometer
station pressure IS NOT the altimeter setting
vfc©

## Slide 25: atmospheredensity
density is the ratio of the mass of an object in relation to the volume it occupies
atmospheric density decreases with altitude, increased temperature and increased humidity
this positively or negatively affects aircraft performance
vfc©

## Slide 26: atmospheredensity
a parcel of air rises because it is of a lesser density than the air surrounding it
less dense
vfc©

## Slide 27: atmosphererelationships
atmospheric pressure and density are directly correlated
lower pressure equals lower density
pressure and therefore density decreases with an increase in altitude
vfc©

## Slide 28: altimetry
vfc©

## Slide 29: altimetryaltimeter
modern day altimeters are referred to as sensitive altimeters
they are simply barometers, calibrated to display a change of 30’ with each milibar of pressure change
each needle is representitive of either hundreds, thousands or tens of thousands of feet
includes a subscale which is used to set the altimeter setting
vfc©

## Slide 30: altimetryIALT
indicated altitude (IALT) is the altitude as indicated on the altimeter above MSL when it is set to the current altimeter setting
it is simply “what the needles say” when the subscale is set correctly
IALT does not take into account non-ISA temperature or humidity values, or instrumentation error
vfc©

## Slide 31: altimetryaltimetersetting
altimeter setting is either expressed as QNH or QFE
QNH is station pressure corrected to mean sea level (MSL) values - altimeter will read height in feet above sea level (ASL) in ISA conditions
QFE is station pressure corrected to a reference datum on the airfield - altimeter will read zero when at the datum in ISA conditions
QNH = “nautical height”, QFE = “field elevation”
vfc©

## Slide 32: altimetryaltimetersetting
worldwide altimeter setting is expressed in millibars (mb) or hectopascals (hPa) - 1 mb = 1 hPa
altimeter setting is set on a subscale on the altimeter
EXCEPT in Canada, the United States and Columbia altimeter setting is expressed to the hundredth of an “Hg
ISA altimeter setting = 29.92”Hg = 1013.2 mb/hPa
vfc©

## Slide 33: altimetryaltimetersetting
15 year average MSL values, June - August
15 year average MSL values, December - February
vfc©

## Slide 34: altimetrychangingpressure
when flying between areas of differing sea level pressure, the altimeter setting will change
if this change is ignored it can be extremely dangerous
this is because the altimeter is simply a barometer - the reading of the needles will change with changes in pressure
having the correct altimeter setting set appropriate for the area you are flying in ensures this reading is accurate
vfc©

## Slide 35: altimetryhightolow
when flying from high to low pressure, the altimeter will over-read
the pilot’s reaction is to descend
this causes the pilot and aircraft to be lower than they think they are
“from high to low, lookout below”
vfc©

## Slide 36: altimetryhightolow
vfc©
30.92”Hg
28.92”Hg

## Slide 37: altimetryhightolow
vfc©
30.92”Hg
28.92”Hg

## Slide 38: altimetrylowtohigh
when flying from low to high pressure, the altimeter will under-read
the pilot’s reaction is to climb
this causes the pilot and aircraft to be higher than they think they are
“from low to high, look to the sky”
vfc©

## Slide 39: altimetrylowtohigh
vfc©
30.92”Hg
28.92”Hg

## Slide 40: altimetrylowtohigh
vfc©
30.92”Hg
28.92”Hg

## Slide 41: altimetryPALT
pressure altitude (PALT) is the altitude as indicated on the altimeter above MSL when it is set to ISA pressure
PALT is the atmospheric pressure conditions the aircraft “thinks” it’s performing under
any non-standard (other than 29.92” Hg) altimeter settings will give non-standard performance
vfc©

## Slide 42: altimetrycoldair
cold air will cause an altimeter to over read due to the steeper pressure gradient, when compared to warm air
vfc©

## Slide 43: altimetryPALT
PALT corrects for non-ISA sea level pressure settings only
aircraft performance charts (ie. takeoff, cruise, landing) are based on the aircraft’s pressure altitude
setting 29.92” Hg in flight will read PALT
vfc©

## Slide 44: altimetryPALT
PALT is the standard for performance chart usage
vfc©

## Slide 45: altimetryPALTformula
PALT is calculated using the formula below:
PALT = station elevation +
        [(29.92” Hg - altimeter setting) x1000]
1” Hg = 1000’
vfc©

## Slide 46: altimetryDALT
density altitude (DALT) is pressure altitude corrected for non-standard ISA atmospheric temperature conditions
it is the altitude at which the aircraft will perform as if it’s at given pressure, humidity and temperature variances from ISA
vfc©

## Slide 47: altimetryDALT
DALT is the most important value in terms of determining how an aircraft will perform
it is especially important under detrimental ISA conditions
hot, high, and humid
vfc©

## Slide 48: altimetryDALT
DALT may be calculated in the air, using an E6B flight computer, the outside air temperature and the PALT
it may also be calculated on the ground using a formula
vfc©

## Slide 49: altimetryDALTformula
DALT is calculated using the formula below:
DALT = PALT +
        [100(OAT - ISA temperature)]
1” Hg = 1000’
vfc©

## Slide 50: altimetryformulae
DALT and PALT formulas, as any formulae, are truly remembered when they are understood
anticipate calculations by relating pressure and temperature values to standard
ie. lower than standard altimeter setting will give a higher pressure altitude than indicated - if not check your calculation
vfc©

## Slide 51: temperature
vfc©

## Slide 52: temperatureimbalance
vfc©
it is due to global temperature differences that we see the creation of weather
these variances are due to a variety of factors, such as location, season, surface type etc.
creates large and small scale weather patterns versus one global weather pattern

## Slide 53: temperatureradiation
vfc©
solar radiation is the energy transfer from the sun to the surface of the earth
terrestrial radiation is the energy transfer from the surface of the earth to the troposphere

## Slide 54: temperatureradiation
vfc©
only half of the incoming solar radiation is absorbed at the surface

## Slide 55: temperaturevariation
vfc©
the earth spinning on a tilted axis causes seasonal variation

## Slide 56: temperaturevariation
vfc©
latitudinal variation accounts for global wind circulation patterns

## Slide 57: temperaturevariation
vfc©
diurnal variation occurs when solar radiation ceases at sunset

## Slide 58: temperaturevariation
vfc©
surface variation determines how readily terrestrial radiation will occur due to absorption

## Slide 59: temperatureheating
vfc©
tropospheric heating is due to heating from the ground up
conduction plays a very small role
there are many other processes involved which distribute heat throughout the troposphere

## Slide 60: temperatureconvectiveheating
vfc©
convective heating is due to the vertical cycle created by rising warm and descending cold air

## Slide 61: temperatureadvectiveheating
vfc©
advective heating occurs as cold air is warmed from below as it moves over a warmer surface

## Slide 62: temperatureturbulentheating
vfc©
turbulence at the surface creates instability and causes heat to be forced aloft

## Slide 63: temperaturecompression
vfc©
descending air is compressed, increasing pressure and temperature, also known as subsidence

## Slide 64: temperatureadiabaticheating
vfc©
the term adiabatic implies that it is the act of compression itself that is heating the parcel of air
there is no external heating force affecting the air

## Slide 65: temperaturecooling
vfc©
as with heating, numerous processes are involved besides radiation that cool the troposphere
radiation cooling itself only affects the surface based levels of the troposphere

## Slide 66: temperatureradiationcooling
vfc©
cooling due to terrestrial radiation at night depends on the existence of cloud

## Slide 67: temperatureadvectivecooling
vfc©
advective cooling occurs as warm air is cooled from below as it moves over a colder surface

## Slide 68: temperatureadiabaticcooling
vfc©
the term adiabatic implies that it is the act of expansion itself that is cooling the parcel of air
there is no external cooling force affecting the air

## Slide 69: temperatureisothermal
vfc©
an isothermal layer implies there is no change in temperature with a change in altitude
it can occur if the predominant weather pattern is very stable
if a light mixing action is set up due to wind bringing together warm and cold air, an isothermal layer may be created

## Slide 70: temperatureinversion
vfc©
an inversion implies an increase in temperature with an increase in altitude
like an isothermal condition, it can occur if the predominant weather pattern is very stable
inversions are in fact so stable that they can give poor VFR flight conditions

## Slide 71: temperatureinversion
vfc©
inversions can commonly form in valleys at sunset
the setting sun warms the air in the upper valley after it has set on the cooling lower air below

## Slide 72: temperatureinversion
vfc©

## Slide 73: temperatureinversion
vfc©
inversions may also form on cold, calm nights when terrestrial radiation ceases, cooling only the lowest levels of the troposphere
they may also occur with the passage of a cold front
inversions favour poor visibility in the cold air and are inherently stable so may persist for long periods of time

## Slide 74: wind
vfc©

## Slide 75: windpressure
wind is simply the horizontal movement of air
solely due to pressure gradients
pressure gradients are “slopes” created by relative areas of high and low pressure
vfc©

## Slide 76: windpressuregradient
isobars join points of equal sea level pressure to create a top down pressure “map”
isobars are without exception drawn at 4 mb intervals
knowing this you can determine the sea level pressure along each isobar
vfc©
4 mb
4 mb
4 mb

## Slide 77: windspeed
the closer the isobars, the steeper the pressure gradient, and the faster the wind speed
the further apart the isobars, the shallower the pressure gradient, and the slower the wind speed
vfc©

## Slide 78: windpressuregradients
cross sectional view of isobars, steep and shallow gradients
vfc©
4 mb
4 mb

## Slide 79: windpressuremap
vfc©

## Slide 80: windhigh
an area of high pressure is also known as an anti-cyclone
it is an area of relatively high sea level pressure
wind moves clockwise around a high in the Northern hemisphere
a high is marked by descending and compressing air
vfc©

## Slide 81: windlow
an area of low pressure is also known as a cyclone
it is an area of relatively low sea level pressure
wind moves counter-clockwise around a low in the Northern hemishphere
a low is marked by ascending and expanding air
vfc©

## Slide 82: windlow
vfc©

## Slide 83: windpressuresystems
vfc©
✗

## Slide 84: windpressuresystems
vfc©
✓

## Slide 85: windmovement
wind does not move directly from areas of high to low pressure
it moves in relation to the isobars, following their curvature
how closely the wind follows the isobars is dependent on altitude
vfc©

## Slide 86: windmovement
wind moves off of and away from centers of high pressure, in a clockwise direction
wind moves down into and towards centers of low pressure, in a counter-clockwise direction
there are two forces besides the pressure gradient that determine wind movement
vfc©

## Slide 87: windcoriolis
the coriolis force is an apparent deflection of a moving body as viewed from a rotating reference frame
it is a major factor in explaining why wind moves the way it does
coriolis causes an apparent deflection of a moving body to the right in the Northern hemisphere
vfc©

## Slide 88: windcoriolis
vfc©

## Slide 89: windcoriolis
coriolis affects the apperent motion of all moving bodies
however it is only influential on objects moving on northerly or southerly tracks
it has a negligible effect upon objects moving east and west, as well as objects moving closer to the poles
vfc©

## Slide 90: windcentrifugal
centrifugal force draws a rotating body away from its center of rotation
equal and opposite to centripetal force
remember wind moving in pressure systems is a rotating body
vfc©

## Slide 91: windcentrifugal
centrifugal force works with the pressure gradient force when acting on wind blowing out from a high
centrifugal force works against the pressure gradient force when acting on wind blowing into a low
the net result is an increased wind speed blowing out of a high and a decreased wind speed blowing into a low
vfc©

## Slide 92: windbuysballotslaw
Buys Ballot’s law states that in the Northern hemisphere standing with your back to the wind, the area of low pressure will be to your left
vfc©
✈
✈
✈

## Slide 93: windnotation
wind direction is indicated as a bearing, either in degrees true or magnetic depending on the type of information
wind is reported or forecast as coming from a specific bearing, rounded to the nearest ten degrees
wind speed is always observed or forecast in nautical miles per hour (KTS)
vfc©

## Slide 94: windveer
a wind that changes direction clockwise is termed a veering wind
ie. a wind of 180° changes to a wind of 230°
vfc©

## Slide 95: windback
a wind that changes direction counter-clockwise is termed a backing wind
ie. a wind of 230° changes to a wind of 180°
vfc©

## Slide 96: windsurface
surface wind is generally termed as winds below 3000’ AGL
surface wind is influenced by surface friction, which slows its speed
a reduce wind speed means a lesser apparent deflection due to the coriolis force, causing movement across isobars
vfc©

## Slide 97: windsurface
vfc©

## Slide 98: windsurface
a reduction in coriolis leads to greater influence on the wind by the pressure gradient force
the result is less of an apparent deflection to the right
this is a backing wind
vfc©

## Slide 99: windaloft
aloft wind is generally termed as winds above 3000’ AGL
aloft wind is not influenced by surface friction, which increases its speed
an increased wind speed means a greater apparent deflection due to the coriolis force, causing movement parallel to the isobars
vfc©

## Slide 100: windaloft
vfc©

## Slide 101: windaloft
an increase in coriolis leads to lesser influence on the wind by the pressure gradient force
the result is more of an apparent deflection to the right
this is a veering wind
vfc©

## Slide 102: windsurfaceandaloft
vfc©
surface
aloft

## Slide 103: windsurfaceandaloft
during a descent from aloft to the surface, the wind is seen to decrease in intensity and back
during a climb from the surface to aloft, the wind is seen to increase in intensity and veer
vfc©

## Slide 104: windcirculation
vfc©
global temperature differences create global atmospheric circulation
large scale prevailing winds, such as the northeastern trade winds in the tropics
pressure gradient force, coriolis force, centrifugal force all need to be considered

## Slide 105: windcirculation
vfc©

## Slide 106: windseabreeze
vfc©
the wind blows on shore during the day due to the convective circulation cycle started as warm air rises over the warmer land surface

## Slide 107: windlandbreeze
vfc©
the wind blows off shore during the night due to the convective circulation cycle started as warm air rises over the warmer water surface

## Slide 108: windkatabatic
vfc©
the wind blows down mountain slopes into valleys at night as the surface of the slopes are cooled

## Slide 109: windanabatic
vfc©
the wind rises up mountain slopes out of valleys during the day as the surface of the slopes are heated

## Slide 110: windglacial
vfc©
the wind blows down glacial slopes much like a katabatic wind due to the cold dense air cooled by the glacier

## Slide 111: windshift
vfc©
a gust is a rapid and irregular fluctuation in the movement of air caused commonly by mechanical turbulence and convection
a squall is a sudden increase in wind strength of a greater intensity than a gust, usually caused by thunderstorm passage

## Slide 112: day2
vfc©
met theory continuation, air masses, fronts

## Slide 113
vfc©
USING ALL AVAILABLE INFORMATION, WHAT IS THE DENSITY ALTITUDE (DALT) AT CALGARY INTERNATIONAL AIRPORT THIS MORNING, AT 1500Z?

## Slide 114: windshear
vfc©
wind shear is the tearing effect that can be experienced along the border of two zones which have different wind speeds and intensities
shear may severely impact aircraft performance, especially critical during take-off and landing

## Slide 115: windshear
vfc©
increased performance wind shear is encountered with an increase in headwind or decrease in tailwind component
on approach, increased performance shear requires a net increase in power to maintain the ideal approach path

## Slide 116: windshear
vfc©

## Slide 117: windshear
vfc©
decreased performance wind shear is encountered with an decrease in headwind or increase in tailwind component
on approach, decreased performance shear requires a net decrease in power to maintain the ideal approach path

## Slide 118: windshear
vfc©

## Slide 119: stability
vfc©

## Slide 120: stabilityveticaldisplacement
vfc©
stability is used to to describe how resistant air is to vertical displacement
stable air resists vertical displacement
unstable air continues movement in the direction of displacement

## Slide 121: stabilityverticaldisplacement
vfc©
stable
unstable

## Slide 122: stabilitytemperature
vfc©
stable
unstable

## Slide 123: stabilitylapserate
vfc©
lapse rate is a vertically descriptive rate of temperature change with altitude
a steep lapse rate implies a large temperature change within a given vertical distance
a shallow lapse rate implies a small temperature chage within a given vertical distance

## Slide 124: stabilitylapserate
vfc©
lapse rate is a key indicator of air stability
a steep lapse rate indicates unstable air
a shallow lapse rate indicates stable air

## Slide 125: stabilitytemperature
vfc©
shallow and stable
steep and unstable

## Slide 126: stabilityflight
vfc©
stability is a key determinant of weather and its severity
knowledge of stability allows pilots to predict weather conditions that will affect their flight

## Slide 127: stabilitystableflight
vfc©
little or no turbulence
steady winds
layer cloud
continuous precipitation
poor visibility, especially in the lower levels

## Slide 128: stabilityunstableflight
vfc©
turbulent
gusting winds
vertically developed cloud
intermittent precipitation
generally good visibility

## Slide 129: turbulence
vfc©

## Slide 130: turbulencedefined
vfc©
turbulence is a random spinning motion of air, or when it develops an abrupt updraft or downdraft
aircraft reaction to turbulence is dependant on a variety of factors
aircraft design, size, speed, wing loading and altitude will all determine this reaction

## Slide 131: turbulencefrequency
vfc©
a factor in the determination of turbulent effect is its frequency

## Slide 132: turbulenceclassification
vfc©
turbulence is classified based on what causes it
mechanical
convective
shear
wake
clear air (jet stream)

## Slide 133: turbulenceintensity
vfc©
turbulence intensity is forecast and reported as follows:
LIGHT: small, erratic changes in altitude and attitude
LIGHT CHOP: light turbulence with a rapid, rhythmic component
MODERATE: greater intensity than light, often with variations in indicated airspeed, aircraft still in positive control

## Slide 134: turbulenceintensity
vfc©
MODERATE CHOP: greater intensity than light chop, without appreciable changes to attitude and/or altitude
SEVERE: large, abrupt changes in aircraft attitude and altitude, usually accompanied by large variations in indicated airspeed - aircraft may be temporarily out of control
EXTREME: aircraft out of control, structural damage possible

## Slide 135: lift
vfc©

## Slide 136: liftliftingagents
vfc©
convection
orographic
fronts
turbulence
convergence

## Slide 137: liftconvection
vfc©
convective heating creates lift and with it a high degree of instability

## Slide 138: liftorographic
vfc©
orographic implies large-scale geographic features
air will continue its unstable movement downwind of a mountain range

## Slide 139: liftfrontal
vfc©
frontal lift is an immensely powerful lifting force
fronts = active weather
C
W

## Slide 140: liftturbulence
vfc©
turbulent eddies may be carried aloft if the air is inherently unstable and winds are strong

## Slide 141: liftconvergence
vfc©
air falling down the pressure gradient converges at the bottom of a low
forces air aloft creating large-scale lift
L

## Slide 142: saturation
vfc©

## Slide 143: saturationatmosphericmoisture
water vapour is the key to visible weather fromation
water vapour exists in the atmosphere due to transpiration from vegetation, and evaporation from bodies of water
water vapour is the invisible form of atmospheric moisture
liquid or crystalline are visible forms of moisture
vfc©

## Slide 144: saturationstateofchange
water vapour’s change of state creates visible moisture
water vapour may condense into a liquid or sublimate directly to a solid
attention must be paid to the energy transfer during these reactions in order to understand visible weather formation
vfc©

## Slide 145: saturationstateofchange
vfc©

## Slide 146: saturationstateofchange
energy released during the process of condensation is know as the latent heat of vaporization
energy released during the process of freezing is known as the latent heat of fusion
this energy release into the atmosphere creates our most powerful weather phenomena
vfc©

## Slide 147: saturationsaturated
the maximum pressure due to water vapour a volume of air may hold is governed by its temperature
saturation implies this volume of air holds the maximum pressure of water vapour it can, at its given temperature
vfc©

## Slide 148: saturationrelativehumidity
relative humidity is defined as the ratio between the partial pressure of water vapour and the saturated vapour pressure of water
partial pressure implies water vapour is only one component of the total gaseous pressure of a volume of air
the saturated vapour pressure of water is simply the pressure at which a volume of air must reach in order for gaseous water to change state (condense or deposit)
vfc©

## Slide 149: saturationtemperature
temperature governs the pressure of the volume of air
lower temperature raises air pressure, of which water vapour pressure is a part of, decreasing the difference between it and the saturated vapour pressure of water
this decreasing difference is represented by an increase in relative humidity
vfc©

## Slide 150: saturationincreasingpressure
a volume of air may have its vapour pressure increased towards saturation in two ways
by cooling...
or by increasing its water content
vfc©

## Slide 151: saturationincreasingmoisture
vfc©
100% relative humidity
50% relative humidity
100% relative humidity

## Slide 152: saturationdewpoint
dew point is the temperature a volume of air must be cooled to in order for water vapour to condense into water
dew point is a saturation temperature
dew point and relative humidity are related
vfc©

## Slide 153: saturationcooling
vfc©
100% relative humidity
50% relative humidity

## Slide 154: lapserate
vfc©

## Slide 155: lapseratedefined
vfc©
lapse rate is a measurement of how quickly air cools when ascending a given vertical distance
in non-inversion conditions, this is said to be a positive rate
in an inversion, this rate is negative

## Slide 156: lapseratevalues
vfc©
there are four adiabatic lapse rates that need to be understood:
standard adiabatic lapse rate (STALR): 1.98°C/1000’
dry adiabatic lapse rate (DALR): 3°C/1000’
saturated adiabatic lapse rate (SALR): 1.5°C/1000’
environmental adiabatic lapse rate (EALR): 2.5°C/1000’

## Slide 157: lapseratecalculations
vfc©
using the appropriate rate and knowing the temperature and dew point of a reporting station, two values may be calculated
the expected base of convective cloud
the height of the freezing level in convective cloud

## Slide 158: cloud
vfc©

## Slide 159: cloudformation
cloud formation is simply water in its visible state
due to condensation or deposition (reverse sublimation)
condensation nuclei are required as a basis for the condensation or deposition of water vapour
vfc©

## Slide 160: cloudclassification
clouds are classified in two different ways
by formation/appearance
by height based on the altitude of their bases
vfc©

## Slide 161: cloudbyformation
clouds may be formed horizontally, known as stratoform cloud (-stratus)
often appear as many stacked layers
multiple layers may create an extensive summative depth
vfc©

## Slide 162: cloudbyformation
clouds may also be formed vertically, known as cumuloform cloud (-cumulus)
appear to have extensive vertical development
one vertical cloud may extend to the upper reaches of the tropopause
vfc©

## Slide 163: cloudbyheight
clouds are also classified based on the height of their bases in feet above ground level:
high clouds - bases above 20000’ AGL
middle clouds - bases from 6500’ AGL to 20000’ AGL
low clouds - bases from surface above the 6500’ AGL
clouds of vertical development - bases generally at the levels of low clouds
vfc©

## Slide 164: cloudhighclouds
high clouds are composed entirely of ice crystals
they are denoted using the prefix cirr-
vfc©

## Slide 165
vfc©
cirrus ci

## Slide 166
vfc©
cirrocumulus cc

## Slide 167
vfc©
cirrostratus cs

## Slide 168: cloudmiddleclouds
middle clouds are composed of ice crystals or water droplets
they are denoted using the prefix alto-
vfc©

## Slide 169
vfc©
altostratus as

## Slide 170
vfc©
altocumulus ac

## Slide 171
vfc©
altocumulus castellanus acc

## Slide 172: cloudlowclouds
low clouds are composed of ice crystals or water droplets
they do not use one specific prefix
vfc©

## Slide 173
vfc©
stratus st

## Slide 174
vfc©
stratus fractus sf

## Slide 175
vfc©
stratocumulus sc

## Slide 176
vfc©
nimbostratus ns

## Slide 177: cloudverticallydevelopedclouds
vertically developed clouds are often composed of water in all of its states
due to extensive vertical height and thus differing temperature regions within the cloud
vfc©

## Slide 178
vfc©
cumulus cu

## Slide 179
vfc©
towering cumulus tcu

## Slide 180
vfc©
cumulonimbus cb

## Slide 181
vfc©
cumulonimbus cb

## Slide 182
vfc©
cumulonimbus cb

## Slide 183: precipitation
vfc©

## Slide 184: precipitationformation
precipitation formation is due to two main factors
both of these factors involve moisture in cloud becoming too massive to support aloft
vfc©

## Slide 185: precipitationcoalescence
water droplets collide with each other in cloud, becoming more massive, termed coalescence
eventually they fall when the uplifting force in cloud is outweighed by their mass, and the droplets falling to the ground
coalescence is more prevalent in areas of cloud where the temperature is above freezing
vfc©

## Slide 186: precipitationtypes
there are numerous forms of precipitation, once it has formed due to coalescence or sublimation
stratoform clouds yield continuous and light/moderate intensity precipitation
cumuloform clouds yield intermittent and intense precipitation
vfc©

## Slide 187: precipitationrain
rain is formed of large droplets
freezing rain is composed of supercooled water droplets which instantanteously change freeze upon impact
vfc©

## Slide 188: precipitationsupercooling
water may exist as a liquid at temperatures as low as -42°C
due to a lack of nuclei around which a crystal may form
supercooled demonstration
vfc©

## Slide 189: precipitationdrizzle
drizzle are small droplets that appear suspended
freezing drizzle occurs when drizzle freezes on impact with cold objects
vfc©

## Slide 190: precipitationhail
hail forms in cumulonimbus clouds as ice crystals collide with supercooled water droplets
the large mass of hail stones requires an immense uplifting force in cloud for their creation, only present in well developed cumuloform cloud
vfc©

## Slide 191: precipitationhail
vfc©

## Slide 192: precipitationsnow
snow is created through sublimation in cloud
its state at the surface is dependant on the ambient air temperature
vfc©

## Slide 193: precipitationsnowpellets
hail that does not acquire a hard outer coating of ice is termed a snow pellet, or soft hail
this occurs when the water region of the cloud is of limited depth
vfc©

## Slide 194: precipitationicepellets
ice pellets are formed by rain drops freezing
they are hard and transparent, and rebound upon striking a surface
vfc©

## Slide 195: fog
vfc©

## Slide 196: fogformation
fog is simply visible moisture in contact with the surface
fog formation is identical to cloud formation, however the atmospheric moisture generating the fog is localized and the fog low lying
moisture laden air saturates forming fog in different ways
vfc©

## Slide 197: fogformation
ideal fog formation conditions, besides high humidity in the presence of condensation nuclei, include light surface winds or instability
if there is no lifting or mixing action in low lying air, dew or frost may form
moisture laden air saturates forming fog in many different ways
vfc©

## Slide 198: fogradiation
radiation fog forms on cold, clear nights in low areas such as valleys
vfc©

## Slide 199: fogadvection
advection fog forms in coastal areas as warm, moist air laden with salt (nuclei) is advectively cooled
vfc©

## Slide 200: fogupslope
air adiabatically cools and saturates as it is forced up a slope
vfc©

## Slide 201: fogsteam
warm water evaporates into the colder air lying just above it, saturating the air
vfc©

## Slide 202: fogprecipitation
precipitation evaporates into air it is falling through, saturating it to its dewpoint
vfc©

## Slide 203: fogice
the droplets in extremely cold saturated air freeze in suspension
vfc©

## Slide 204: fogice
hot exhaust gases saturate cold air extremely quickly, producing ice fog, in this case known as contrails
vfc©

## Slide 205: fogice
the ellusive twin engined stork
vfc©

## Slide 206: icing
vfc©

## Slide 207: icingsupercooled
supercooled water droplet impact by an aircraft wing at temperatures below freezing will cause icing
the quantity of supercooled droplets is dependent on the liquid water content of the cloud
clouds formed to due convection, lee wave turbulence, and orographic lift contain the largest size of water droplets due to their powerful lift
vfc©

## Slide 208: icingrime
rime ice is milky-white, opaque, and is formed by almost instantaneous freezing of small water droplets at temperatures well below freezing
it tends to form only on the leading edges of airfoils, and builds forward into the airstream
because it is not very adhesive, it is relatively easy to remove with de-icing equipment
vfc©

## Slide 209: icingclear
clear ice may vary from a transparent appearance to a very rough, opaque texture created from by a slow freezing process of large water droplets
the free droplet that didn’t freeze on initial impact moves aft and continues to freeze at temperatures not far below freezing
it may spread from the leading edges of the aircraft to cover it entirely in severe cases
vfc©

## Slide 210: icingclear
because of its irregular freezing process it may create unique shapes the protrude from the aircraft
it is tougher to remove with de-icing equipment than rime
clear icing is a greater hazard than rime icing
vfc©

## Slide 211: icingmixed
mixed icing is a combination of rime and clear
frequently the cloud temperature and range of droplet sizes are such that conditions are conducive to mixed ice formation
vfc©

## Slide 212: icingtypes
vfc©

## Slide 213: icingtemperature
warm air will present a greater quantity of water droplets than cold air
larger droplets begin to spontaneously freeze to crystals around -10°C
colder temperatures are required to freeze smaller droplets
vfc©

## Slide 214: icingtemperature
the rate of freezing markedly increases at temperatures just below -15°C
larger droplets begin to spontaneously freeze to crystals around -10°C
by -40°C virtually all droplets will have frozen, therefore the chances of aircraft icing below -40°C are lower
vfc©

## Slide 215: icingintensity
trace icing accumulates at a rate only slightly greater than it sublimates
not hazardous, even without anti/de-ice equipment, unless encountered for over an hour
vfc©

## Slide 216: icingintensity
light icing may pose a problem if encountered for more than an hour
does not pose a problem if anti/de-ice equipment is installed and used
vfc©

## Slide 217: icingintensity
moderate icing creates potentially hazardous situations, even if encountered for a short period of time
use of anti-de-ice equipment, or a diversion, is necessary
vfc©

## Slide 218: icingintensity
severe icing accumulates at a rate such that anti/de-ice equipment does not decrease the hazard
an immediate diversion is the one and only option
vfc©

## Slide 219: icingintensity
these terms of intensity are subjective to each individual aircraft
whether the icing intensity is light for one aircraft and medium for another depends on the qualitative effect on flight characteristics, and should be determined on a case by case basis
vfc©

## Slide 220: icingfreezingprocess
when a supercooled droplet freezes, latent heat of fusion is released which warms the remaining droplet to 0°C
droplet continues to freeze, but more slowly
fraction of droplet that initially freezes greater with colder temperatures
after initial impact, rate of freezing depends on temperature of aircraft skin and air temperature
vfc©

## Slide 221: icingfreezingprocess
vfc©

## Slide 222: icinginclearair
icing in clear air is possible, meaning you DO NOT have to be in cloud to accumulate ice
ice accumulation in clear air is known as hoar frost
vfc©

## Slide 223: icinghoarfrost
hoar frost is a crystalline, feathery-white frost that may cover an entire aircraft
similar to the frost that forms on a car roof on cold, clear nights
forms due to sublimation as warm, moist air comes in contact with a sufficiently cold surface
vfc©

## Slide 224: icinghoarfrost
parked aircraft are susceptible to hoar frost formation, especially on their upper surfaces as they radiately cool
hoar frost may also form on aircraft in flight that have been cold-soaked by flying at temperatures below freezing and then descend into warm, moist air
frequently the frost forms in the vicinity of integral fuel tanks as the cold fuel warms slower than the rest of the aircraft
vfc©

## Slide 225: icingcollectionefficiency
collection efficiency is the fraction of liquid water which collects as ice on an aircraft
this efficiency varies directly with droplet size, aircraft speed and inversely with the geometric size of the collecting surface
a thin, fast wing travelling through an area containing large supercooled water droplets will be most efficient in ice collection
vfc©

## Slide 226: icingcollectionefficiency
vfc©

## Slide 227: icinglaw
it is against the law to take-off with any ice accumulation on an aircraft’s critical surfaces
CAR 602.11 (2): no person shall conduct or attempt to conduct a take-off in an aircraft that has frost, ice or snow adhering to any of its critical surfaces
critical surfaces means the wings, control surfaces, rotors, propellers, horizontal stabilizers, vertical stabilizers or any other stabilizing surface of the aircraft
vfc©

## Slide 228: icingeffect
it must be understood that every effect of aircraft icing has the potential to be extremely hazardous to flight
the cumulative effect of aircraft icing is an increased stalling speed
this is the greatest danger of aircraft icing
vfc©

## Slide 229: icingeffect
vfc©

## Slide 230: mountainwave
vfc©

## Slide 231: mountainwavedisturbances
vfc©
air moves in relation to a mountain or mountain ridge which in may create a series of disturbances
air is initially forced up, followed by a sharp drop downwind of the peak
further downwind the air movement may continue as a series of wave-like oscillations termed a mountain wave

## Slide 232: mountainwavedisturbances
vfc©
the intensity of the possible oscillations is dependant on the height of the mountain, and how sharply the terrain drops off on the leeward side
the greater the height and the sharper the drop-off, the greater the oscillation
the wave length downwind averages 6 miles, with an amplitude up to 3000’

## Slide 233: mountainwavedimensions
vfc©

## Slide 234: mountainwaveclouds
vfc©
if conditions are favourable, tell-tale clouds will form in certain parts of the wave
these should be used as warning signs of the inherent dangers of mountain waves

## Slide 235: mountainwavecapcloud
vfc©

## Slide 236: mountainwavecapcloud
vfc©

## Slide 237: mountainwaverollcloud
vfc©

## Slide 238: mountainwavelenticularcloud
vfc©

## Slide 239: mountainwavelenticularcloud
vfc©

## Slide 240: mountainwavedangers
vfc©
windshear
turbulence
convective currents
altimeter error
icing

## Slide 241: mountainwavedangers
vfc©

## Slide 242: thunderstorm
vfc©

## Slide 243: thunderstormformation
thunderstorm formation depends on air characteristics
warm air with a high moisture content, potential instability, a steep lapse rate and a convective lifting agent will promote thunderstorm formation
the latent heat of vaporization in the lower region of the cloud, and of fusion in the upper region of the cloud accelerate the initial updraft and grow the cumulonimbus
vfc©

## Slide 244: thunderstormstages
thunderstorm stages are identified by the shape of the cloud, the direction of air movement within the cloud, and the occurrence of precipitation
there are three main stages of the thunderstorm
vfc©

## Slide 245: thunderstormcumulus
vfc©
the first stage is the cumulus stage, when numerous small convective clouds merge and rapidly grow into a very large cell
only updrafts exist in the cumulus stage, are greatest in the upper levels and may reach 3000’ per minute
ice crystals and then rain form as cell builds past the freezing level, with drops eventually falling in cloud as they grow more massive
cumulus stage lasts about 20 minutes

## Slide 246: thunderstormcumulus
vfc©

## Slide 247: thunderstormmature
the mature stage is marked by precipitation at earth’s surface
the cloud continues to grow, with updrafts reaching 6000’ per minute
strong winds in the tropopause carry the cloud ahead of the storm, creating a characteristic anvil shape
vfc©

## Slide 248: thunderstormanvil
vfc©

## Slide 249: thunderstormmature
precipitation drags air in the cloud down with it, and evaporation cools the air strengthening the downdraft mid-cloud
a gust front is created when this air pours out of the cloud and reaches the surface, spreading out
the gust front is marked by gusty surface winds, a sharp drop in temperature and abrupt rise in pressure
vfc©

## Slide 250: thunderstormmature
ahead of the gust front, air rises up and over the incoming cold down-flowing air, flowing into the storm
as the gust front passes wind veers violently, sometimes up to 180°
the downdraft may originate short-lived but extremely violent winds known as microbursts
vfc©

## Slide 251: thunderstormmature
vfc©

## Slide 252: thunderstormmature
hail is most likely during the mature stage
supercooled droplets begin to freeze, and other drops coalesce on them as they are cycled through the cloud, growing is size
small hail may be carried up and ejected laterally from the cloud
vfc©

## Slide 253: thunderstormmature
lightning is a discharge from negative to positive within cloud, from cloud to ground or rarely from ground to cloud
thunder is the resultant noise as lightning heats the air so that it expands more rapidly than the speed of sound
the distance in miles to the lightning strike is estimated by counting seconds between lightning and thunder and dividing the number by five
vfc©

## Slide 254: thunderstormmature
mature stage is the most violent stage
precipitation is most intense near the end of this stage
lasts for about 20-30 minutes
its end is marked by the updraft weakening and downdraft encompassing the entire cell
vfc©

## Slide 255: thunderstormmature
vfc©

## Slide 256: thunderstormdissipating
entire cell is a downdraft
mechanisms which generate precipitation, lightning, turbulence do not exist
longest yet least hazardous stage
vfc©

## Slide 257: thunderstormmature
vfc©

## Slide 258: thunderstormcells
a thunderstorm usually consists of two or more cells in different stages of their life cycles
vfc©

## Slide 259: thunderstormclassification
thunderstorms are classified based on the lifting action that triggers instability
vfc©

## Slide 260: thunderstormwarmfront
vfc©

## Slide 261: thunderstormcoldfront
vfc©

## Slide 262: thunderstormconvective
vfc©

## Slide 263: thunderstormorographic
vfc©

## Slide 264: thunderstormhazards
vfc©

## Slide 265: airmass
vfc©

## Slide 266: airmassdefined
an air mass is a large body of air, 1000 or more miles across
across the horizontal, an air mass has acquired fairly uniform properties of temperature and moisture
topped by the tropopause
vfc©

## Slide 267: airmasscharacteristics
the airmass characterizes the type of weather seen within it
they are classified based on their two defining properties
vfc©

## Slide 268: airmassclassification
there are three relatively dry air masses:
continental arctic - cA
continental polar - cP
continental tropic - cT
vfc©

## Slide 269: airmassclassification
there are three relatively moist air masses:
maritime arctic - mA
maritime polar - mP
maritime tropic - mT
vfc©

## Slide 270: airmassclassification
continental arctic is the coldest driest air mass, has a very low tropopause and is very stable
maritime tropic is very warm and moist, has a high tropopause, and is very unstable
continental tropic has the highest tropopause, is very unstable and its source region is very small in North America
vfc©

## Slide 271: airmassstructure
vfc©
the warmer the air mass, the higher and colder its tropopause

## Slide 272: airmasssourceregions
if an air mass remains over a particular region for an extended period of time it will acquire the properties of that region
these regions are termed source regions
vfc©

## Slide 273: airmassmodification
if an air mass moves out of its source region, it may modify to become a new air mass
the degree of modification depends on the speed at which the mass is moving, and the moisture content and temperature difference between the mass and the new source region
vfc©

## Slide 274: airmasswarmingfrombelow
an air mass warmed from below will develop convection and instability in its lower levels, which may be carried aloft
vfc©

## Slide 275: airmasscoolingfrombelow
an airmass cooled from below will develop stability in its lower levels, and modification is confined to the first few thousand feet
vfc©

## Slide 276: airmasssourceregions
vfc©

## Slide 277: fronts
vfc©

## Slide 278: frontsdefined
cold, dense air does not readily mix with warm, less dense air
along the border of two air masses, there is a relatively short transition zone of temperature change within 50-100 miles
this is a front, or frontal system
vfc©

## Slide 279: frontsnomenclature
fronts are named based on the colder air mass involved
this means it is the relative movement of cold air with relation to the warm air that describes a front
vfc©

## Slide 280: frontsfrontalsystems
vfc©

## Slide 281: frontscold
the advancing edge of a cold air mass is termed a cold front
the cold air advances towards, and eventually will catch up with, the warm air
vfc©

## Slide 282: frontswarm
the retreating edge of a cold air mass is termed a warm front
the warm front is eventually caught up to by the cold front
or, the cold front eventually will catch up with itself
vfc©

## Slide 283: frontsquasistationary
a quasi-stationary front shows little relative movement of the cold air
with reference to the ground, it is moving at less than 5 kts
vfc©

## Slide 284: frontsupper
cold and warm fronts may also be referred to as upper fronts, meaning their frontal surface does not come in contact with the ground
there is an underlying mass of air with fairly uniform temperature causing the discontinuity of the frontal surface
vfc©

## Slide 285: frontsfrontogenesis
the creation of a front is termed frontogenesis
this occurs when wind increases the temperature contrast within one air mass, creating two areas of differing temperature
vfc©

## Slide 286: frontsfrontolysis
the dissipation of a front is termed frontolysis
this occurs when wind decreases the temperature contrast between two air masses to a point where there is no need for the front to exist
modification of two air masses that remain over the same source region may also cause frontolysis
vfc©

## Slide 287: frontsstructure
remember that a front is in fact a mixing zone of air 50-100 miles across
vfc©

## Slide 288: frontsstructure
it is important to see fronts from all perspectives to fully understand them
vfc©

## Slide 289: frontsinversion
an inversion is encountered during ascent from the surface through a cold front
vfc©

## Slide 290: frontsnorthamerica
vfc©

## Slide 291: frontsmotion
vfc©
frontal motion is dependent on the movement of the cold air perpendicular to it
the motion of the warm air does not affect frontal movement
this is true at both the cold front and the warm front

## Slide 292: frontsmotion
vfc©

## Slide 293: frontsslope
vfc©
the slope a frontal surface makes with earth’s surface is extremely shallow, and in all cases it is in the realm of one degree
the shape of the frontal surface however varies significantly between the various fronts

## Slide 294: frontsslope
vfc©

## Slide 295: frontsgoingup
vfc©
two terms are used to describe the upwards movement that the warm air experiences at the cold and the warm front
at the warm front, the warm air overruns the retreating cold air, and it is lifted aloft
at the cold front, the advancing cold air aggressively lifts the warm air as it undercuts, creating frontal lift

## Slide 296: frontsfrontallift
vfc©

## Slide 297: frontsoverrunning
vfc©

## Slide 298: frontspassage
vfc©
it is important to note the changes with respect to wind, temperature and pressure with both cold and warm front passage
these changes may appear in advance of a front passing, or be evident only during or after its passage

## Slide 299: frontscoldfrontpassage
vfc©
weather | before passage | with passage | after passage
temperature | warm | suddenly cooling | steady cooling
pressure | decreasing | decreasing to lowest point, then sudden increase | steady increase
winds | backing | variable, gusting | veering
visibility | fair to poor | poor but improving | good, except during showers

## Slide 300: frontswarmfrontpassage
vfc©
weather | before passage | with passage | after passage
temperature | cool | sudden warming | warming, then sustaining
pressure | decreasing | sustaining | slight rise then decrease
winds | backing | variable | veering
visibility | poor | improving | fair

## Slide 301: frontswaves
vfc©
wave-like disturbances may form on quasi-stationary fronts that can produce extensive areas of cloud and precipitation
these waves may be stable or unstable

## Slide 302: frontsstablewave
vfc©

## Slide 303: frontsunstablewave
vfc©

## Slide 304: frontstrowal
vfc©
the trough of warm air that is lifted aloft during an unstable wave is termed a trowal

## Slide 305: frontsocclusion
vfc©
the advancing cold front catching up to the warm front is termed an occlusion
it is a like a doing up a zipper with the resultant being a wedge of warm air pushed aloft
remember that in essence this is the cold front catching up to its own tail

## Slide 306: frontsocclusion
vfc©

## Slide 307: frontscoldfrontocclusion
cold air advances on and lifts its retreating cool tail, which in turn lifts warm air aloft
vfc©

## Slide 308: frontswarmfrontocclusion
cool air advances on and overruns its retreating cold tail, which lifts warm air aloft
vfc©

## Slide 309: frontsweather
vfc©
each type of front creates a specific type of weather
this can range from little cloud formation with no precipitation, to aggressive thunderstorms with intense precipitation
the weather seen at the front depends on the characteristics of the warm air mass

## Slide 310: frontscoldfrontweather
vfc©

## Slide 311: frontswarmfrontweather
vfc©

## Slide 312: frontswinterwarmfront
rain falling from cloud in the cold air sector at a warm front has the potential to cause freezing rain and dangerous icing conditions
vfc©

## Slide 313: frontswinterwarmfront
vfc©

## Slide 314: frontstrowalweather
vfc©

## Slide 315: jetstream
vfc©

## Slide 316: jetstreamdefined
vfc©
jet streams are fast moving, narrow corridors of air within the main airflow
they may be thousands of miles long, hundreds of miles wide and a few thousand feet thick
the wind speed must be a minimum of 60 kts to qualify as a jet stream, and speeds in excess of 200 kts may occur

## Slide 317: jetstreamfrontal
vfc©
jet streams may be associated with frontal systems
they flow parallel to the surface position of the front, crossing at the point of occlusion and circling northwards around the low
the jet takes the name of the front causing it - arctic, polar or maritime

## Slide 318: jetstreamfrontal
vfc©

## Slide 319: jetstreamfrontal
vfc©
jet streams flow easterly, below the warm air tropopause of a front, and at approximately the same level of the cold air tropopause
looking down the jet stream, air rotates counter-clockwise, rising to the south and descending to the north
if the ascending air is moist, cirrus clouds may form, with fibrous edges denoting the strong vertical shear

## Slide 320: jetstreamstructure
vfc©

## Slide 321: jetstreamstructure
vfc©

## Slide 322: jetstreamvariation
vfc©
the jet stream position varies with the movement of the front it is associated with
the fronts themselves migrate depending on the season
the tropopause is higher in summer, and lower in winter
jet streams also meander in height along their length

## Slide 323: jetstreamvariation
vfc©
during winter in the mid-latitudes in the northern hemisphere, there is a greater temperature contrast over land areas than in summer
fronts move further to the south in winter with lower tropopause heights
associated frontal jet streams are therefore lower and stronger in intensity (due to the greater temperature contrast) in winter than in summer

## Slide 324: navcanada
vfc©

## Slide 325: navcanadaprovider
Nav Canada is Canada’s civil air navigation service provider of...
air traffic control
flight information
weather briefings
vfc©

## Slide 326: navcanadaprovider
aeronautical information services
airport advisory services
electronic aids to navigation
the aviation weather website - AWWS
vfc©

## Slide 327: navcanadaweatherbriefings
one way aviation weather may be obtained is through a pilot interpretative weather briefing provided by a NavCanada flight information center (FIC)
FICs may be contacted via toll free telephone from anywhere in Canada
1-866-WXBRIEF (1-866-992-7433)
vfc©

## Slide 328: navcanadafic
vfc©

## Slide 329: navcanadaweatherbriefings
when calling for a weather briefing, be prepared to give the following information:
aircraft registration and type
operation type - VFR
route
estimated zulu time of departure
planned altitude
estimated time en route
vfc©

## Slide 330: navcanadainflightweather
there are numerous ways to obtain weather information during flight
air traffic control
FICs via “Pacific Radio”
ATIS
voice generator module
vfc©

## Slide 331: navcanadainflightweather
there are numerous ways to obtain weather information during flight
air traffic control
FICs via “Pacific Radio”
ATIS
voice generator module
vfc©

## Slide 332: information
metar
taf
notam
pirep
fd
bkn
few
sct
ovc
SLP987
A2976
tempo
fm
prob30
becmg
ra
sc3
10018G25KT
speci
awos
rmk
cig
br
+snsh
fu
-dz
pressrr
fldurd
hj
1803Z
VV002
skc
cb
tcu
sf4
blsa
fc
ws
RVRRWY331200V2600
fg
3/4SM
cyyj
fzdz
auto
vis
M01/M05
fcst
ua
rime
nil
blo040
cu2st4acc1
10/03
lwis
FL080
mdt
vfc©

## Slide 333: informationsourcesandreferences
vfc©

## Slide 334: informationclassification
vfc©

## Slide 335: informationMETAR
a METAR is an aviation routine weather report
it observes actual weather conditions, as observed from the ground, within a 5 NM radius of the reporting station
the report is composed of several coded groups, always in the same relative position
vfc©

## Slide 336: informationMETAR
vfc©
METAR CYYJ 250000Z CCA 13015G25KT 3/4SM R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=

## Slide 337: metarreporttype
vfc©
CYYJ 250000Z CCA 13015G25KT 3/4SM R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
METAR
signifies a METAR report
always issued on the top of the zulu hour
issued 24 hours per day at all international airports in Canada

## Slide 338: metarstation
4 letter ICAO identifier of the reporting station
all Canadian stations commence with “C”
vfc©
METAR 250000Z CCA 13015G25KT 3/4SM R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
CYYJ

## Slide 339: metardateandtime
the day of the month is followed by the zulu time of the report issuance
zulu time is exclusively used in aviation weather
vfc©
METAR CYYJ CCA 13015G25KT 3/4SM R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
250000Z

## Slide 340: metarcorrection
this code is used to correct a previous report due to observer or instrumentation error
the first correction uses the designator “A”, the second correction “B” etc.
vfc©
METAR CYYJ 250000Z 13015G25KT 3/4SM R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
CCA

## Slide 341: metarwind
wind is reported as a two minute mean direction and speed, including gusts if observed
gusts are included if in the ten minutes prior to the report, the gust exceeds mean wind by 5 kts or more, and the gust itself is 15 kts or stronger
wind direction in metar is always reported as true
vfc©
METAR CYYJ 250000Z CCA 3/4SM R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
13015G25KT

## Slide 342: metarvisibility
the minimum prevailing ground visibility is reported in statute miles (SM)
an observer can only see point to point, along a statute mile
nautical miles are never used to report visibility
vfc©
METAR CYYJ 250000Z CCA 13015G25KT R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
3/4SM

## Slide 343: metarrunwayvisualrange
runway visual range (RVR) reports ground visibility in feet if below 1 NM for a particular runway
trend is indicated if the visibility changes 300’ or more in the five minutes preceeding observation
/U = upwards trend
/D = downwards trend
/N = no distinct trend
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
    -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
R27/4000FT/D

## Slide 344: metarpresentweather
this code describes one or more forms of precipitation, obscuration or other phenomenon
placed before the code are descriptors of intensity, proximity to the station, or other
present weather is coded by the World Meteorological Organization Code, table 4678
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
    R27/4000FT/D BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
-DZ BR

## Slide 345: metarpresentweather
vfc©

## Slide 346: metarskycondition
cloud bases are reported in hundreds of feet AGL
placed before these altitudes are summative terms that describe, in oktas (eighths), coverage of the sky
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
    R27/4000FT/D -DZ BR 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
    BKN002 OVC005

## Slide 347: metarskycondition
vfc©
FEW (few)
<0/8 - 2/8
SCT (scattered)
<2/8 - 4/8
BKN (broken)
<4/8 - >8/8
OVC
(overcast) 8/8

## Slide 348
2/8
1/8
3/8
2/8
+
FEW
SCT
+
BKN
+
OVC
10 NM

## Slide 349: metarskycondition
the height of the first reported layer of broken (BKN), overcast (OVC) or vertical visbility (VV) is termed a ceiling
a VFR pilot may not fly above the altitude of a summative cloud ceiling
this is true even if there is clear air below and the ground is visible
vfc©

## Slide 350
1/8
FEW
2/8
SCT
3/8
BKN
2/8
OVC
10 NM

## Slide 351: metartemperatureanddewpoint
temperature and dewpoint are rounded to the nearest Celsius degree
the spread between them is an expression of relative humidity
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
    R27/4000FT/D -DZ BR BKN002 OVC005 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
    08/08

## Slide 352: metaraltimetersetting
the altimeter setting is reported to the nearest hundredth of “ Hg
insert the decimal before the 2nd to last number of the group
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
    R27/4000FT/D -DZ BR BKN002 OVC005 08/08 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
    A3026

## Slide 353: metarrecentweather
recent weather of operational significance is reported here
this includes precipitation, blowing snow, storms or volcanic ash
recent implies the weather was seen following the previous report, but not at the issuing time of the current report
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247=
    RERA

## Slide 354: metarwindshear
windshear, if known, is reported when occurring within 1600‘ AGL along an approach or departure path of a specific runway
this knowledge should be combined with the mean wind observance to identify the specific type of performance shear
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA RMK SF5SF3 VIS 3/8 TO NW SLP247=
    WS RWY27

## Slide 355: metarremarks
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 VIS 3/8 TO NW SLP247=
        RMK SF5SF3
the first group of the remarks section indicates the cloud type of each layer, as well as the individual opacity (coverage) of each cloud layer, that was reported by sky condition
sky condition and this section of the remarks should to be used together to gain a complete picture of the observed cloud

## Slide 356: metarremarks
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR 08/08 A3026 RERA WS RWY27 RMK VIS 3/8 TO NW SLP247=
        SF5
        SF3
        BKN002
        OVC005
10 NM

## Slide 357: metarremarks
sector visibility is reported if half or less of the prevailing visibility is observed in a particular sector
the sector visibility, in SM, is followed by which sector is reporting it, as a compass direction referenced from the station
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 SLP247=
        VIS 3/8 TO NW

## Slide 358: metarremarks
sea level pressure is the last part of the remarks code
it is abbreviated, and expressed in millibars
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW
        SLP247 =

## Slide 359: metarremarks
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW
        SLP247 =
9/
mb
247
.
10

## Slide 360: specioffhour
between METAR issuances, weather conditions may change
if conditions change such that a new report is warranted, an off-hour report of similar format to a METAR will be issued
this observance is termed a SPECI
vfc©

## Slide 361: specioffhour
a SPECI may describe the commencement, cessation or change in sky condition, visibility, wind, precipitation, temperature or severe weather phenomena
a SPECI does not report observed changes in dew point, altimeter setting, or sea level pressure
vfc©

## Slide 362: specioffhour
vfc©
      METAR CYYJ 250000Z CCA 13015G25KT 3/4SM
        R27/4000FT/D -DZ BR BKN002 OVC005 08/08 A3026 RERA WS RWY27 RMK SF5SF3 VIS 3/8 TO NW SLP247 =
      SPECI CYYJ 250023Z 18022G37KT 3/8SM R27/1200FT/D FZRA BKN001 OVC003 M01/ RMK SF6ST3=

## Slide 363: awosautomated
at some weather stations it is not feasible to have a human observer
at these stations, automated weather observation system (AWOS) sensors may be installed
vfc©

## Slide 364: awosautomated
AWOS sensors are capable of measuring wind, layer height, sky cover, visibility, temperature, dew point, altimeter setting, precipitation, icing and sea level pressure
to indicate AWOS sensors are being used, the term AUTO is used after the date/time group in a METAR or SPECI code
vfc©

## Slide 365: awosautomated
vfc©
METAR CYHE 072100Z AUTO 14008KT 9SM CLR M04/M19 A3021 RMK SLP233=

## Slide 366: metar/speciaccessing
vfc©

## Slide 367: tafterminalareadromeforecast
vfc©
the terminal areadrome forecast (TAF) is to a local forecast what the METAR is to a local observation
the TAF forecasts within a 5 NM radius of the forecasting station
the TAF is always coded in groups in the same relative position to one another

## Slide 368: tafterminalareadromeforecast
vfc©
at international airports in Canada the TAF is valid for a minimum of 24 hours up to a maximum of 30 under the ICAO format
other stations may issue TAFs for shorter validity periods, depending on operational requirements
TAFs are issued at least every six hours

## Slide 369: tafstations
vfc©

## Slide 370: tafexample
vfc©

## Slide 371: tafexample
vfc©
TAF CYDN 291145Z 2912/3012 24010G25KT WS01127050KT 3SM -SN BKN010 OVC040 TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z

## Slide 372: tafstationidentifier
vfc©
291145Z 2912/3012 24010G25KT WS01127050KT 3SM -SN BKN010 OVC040 TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
TAF CYDN
station identifier, ICAO format
TAF is the international format for an aerodrome forecast, if corrected will be indicated by AMD (amended)

## Slide 373: tafissuance
TAF CYDN 2912/3012 24010G25KT WS01127050KT 3SM -SN BKN010 OVC040 TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
vfc©
the TAF issuing date and time are consistent with the METAR format
291145Z

## Slide 374: tafvalidity
vfc©
validity time is coded as a time bracket, from a specific day and zulu hour, until a specific zulu hour
this start and end bracket is separated by a forward slash
TAF CYDN 291145Z 24010G25KT WS01127050KT 3SM -SN BKN010 OVC040 TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
2912/3012

## Slide 375: tafwind
vfc©
wind is forecast in degrees true and in knots
if it’s written, it’s true
the same gust criteria as METAR applies
TAF CYDN 291145Z 2912/3012 WS01127050KT 3SM -SN BKN010 OVC040 TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
24010G25KT

## Slide 376: tafwindshear
vfc©
wind shear is forecast if the forecaster has strong evidence to believe that significant, non-convective wind shear will occur within 1500‘AGL of the station
often this evidence is based on pilot report
  TAF CYDN 291145Z 2912/3012 24010G25KT
  3SM -SN BKN010 OVC040 TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
WS01127050KT

## Slide 377: tafvisibilityandsigweather
vfc©
prevailing visibility is forecast up to 3 SM in miles or fractions thereof, and then in whole SM up to 6 SM
visibilities forecast to be greater than 6 SM are coded as P6SM
significant weather codes are consistent with METAR
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT BKN010 OVC040 TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
  3SM -SN

## Slide 378: tafskycondition
vfc©
cloud layers are consistent with METAR
forecast layers are summative in feet AGL
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT 3SM -SN TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
  BKN010 OVC040

## Slide 379: taftempo
vfc©
the TEMPO is a temporary change group of certain weather elements
weather groups following the abbreviation TEMPO will differ from those groups before it
TEMPO is in time bracket format
TEMPO states the changing elements will occur for no more than one hour, and if forecast to reoccur, will occur for a sum total of no more than 50% of the time bracket
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT 3SM -SN BKN010 OVC040
  1 1/2SM -SN BLSN BKN008 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
  TEMPO 2918/3001

## Slide 380: taftempo
vfc©
the changing elements are consistently coded
if a weather group is not indicated by TEMPO, it remains unchanged, as previously forecast
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT 3SM -SN BKN010 OVC040
  TEMPO 2918/3001 PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
  1 1/2SM -SN BLSN BKN008

## Slide 381: tafprob
vfc©
PROB describes the forecast probability of a change
it is included if there is the probability of thunderstorms, freezing precipitation or ceilings/visibility which may approach operational minima
PROB only indicates either a 30% or 40% chance of the forecast weather occurring
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT 3SM -SN BKN010 OVC040
        TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008
        PROB30 2920/2922
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
        1/2SM SN VV005

## Slide 382: taffm
vfc©
FM is used to forecast a rapid and permanent change
there is no time bracket associated with FM
it is a new, complete forecast within a TAF
even if elements are forecast to remain unchanged, they will be repeated within the FM change code
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT 3SM -SN BKN010 OVC040
        TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008
        PROB30 2920/2922 1/2SM SN VV005
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
FM300130 28010KT 5SM -SN BKN020

## Slide 383: tafbecmg
vfc©
BECMG is a gradual, permanent change
it is used when up to two elements are forecast to gradually change
the time bracket format is used
if a permanent change is expected in more than two elements, FM will be used
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT 3SM -SN BKN010 OVC040
        TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008
        PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z
BECMG 3006/3008 00000KT SKC

## Slide 384: tafbecmg
vfc©
the remarks code will indicate if the forecast is based on AWOS
it will also indicate the time at which the next TAF will be issued by
TAF issuance commonly precedes its validity period by more than twenty minutes
  TAF CYDN 291145Z 2912/3012 24010G25KT
  WS01127050KT 3SM -SN BKN010 OVC040
        TEMPO 2918/3001 1 1/2SM -SN BLSN BKN008
        PROB30 2920/2922 1/2SM SN VV005
FM300130 28010KT 5SM -SN BKN020
BECMG 3006/3008 00000KT SKC
RMK FCST BASED ON AUTO OBS NXT FCST BY 281800Z

## Slide 385: tafaccessing
vfc©

## Slide 386: fdupperwindandtemp
vfc©
the upper level wind and temperature forecast is know as FD
to generate this forecast, data is collected twice daily (00Z, 12Z) from 32 sites across Canada

## Slide 387: fdupperwindandtemp
vfc©
wind direction (rounded to the nearest 10° true) and speed are forecast for all levels in 3000‘ increments ASL
temperature is forecast for all but the 3000‘ level, due to low level temperature variation

## Slide 388: fdupperwindandtemp
vfc©

## Slide 389: fdaccessing
vfc©

## Slide 390: pireppilotreport
vfc©
PIREP is a report of weather conditions encountered in flight by other pilots
PIREP is invaluable, and pilots are encouraged to file them, especially when significant weather phenomena are observed
PIREP reported as UACN10 are regular
PIREP reported as UACN01 are urgent

## Slide 391: pirepexample
vfc©
UACN01 CYEG 270202 EG UUA /OV YYC 340010 /TM 0200 /FLUNKN /TP UNKN /RM PILOT ON GROUND REPORTS TORNADO MOVING WEST TO EAST
UACN01 CYKA 301613 VR UUA /OV CYVR 145030 /TM 1609 /FLDURD /TP DH8D /IC SEV MXD 090-120 /RM 20-30 NM ON GRIZZ.3 ARR IN CYVR. ACFT HAD NO CHOICE BUT TO DSND

## Slide 392: pirepaccessing
vfc©

## Slide 393: informationclassification
vfc©

## Slide 394: graphicalweathervisual
vfc©
graphical weather uses a combination of symbology and alphanumeric code overlaid on a geographic map to create a weather analysis or forecast
the graphical area forecast (GFA) is one such product

## Slide 395: gfabackground
vfc©
graphical weather uses a combination of symbology and alphanumeric code overlaid on a geographic map to create a weather analysis or forecast
the graphical area forecast (GFA) is one such product

## Slide 396: gfacoverage
vfc©
seven GFA domains provide complete domestic coverage of Canada
it consists of a series of weather charts that provide a 24 hour depiction of the most probable weather conditions forecast to occur over a specific area at a specific time, from the surface to 24000’ ASL

## Slide 397: gfadefined
vfc©
each GFA is in fact a series of weather charts, which are grouped into three sets
each set contains a chart that forecasts clouds and weather, and another chart that forecasts icing, turbulence, and the height of the freezing level

## Slide 398: gfa24hourcoverage
vfc©
the first GFA set is valid at the beginning of the forecast period, for six hours
the second set is valid six hours into the forecast period, for six hours
the third GFA set is valid twelve hours into the forecast period, for twelve hours
this creates a comprehensive 24 hour forecast

## Slide 399: gfaissuanceandvalidity
vfc©
GFA is issued every six hours, with four issuances a day
the issuance, as with any forecast, precedes validity time
GFA is issued before the top of the 0000, 0600, 1200 and 1800 zulu hours, the respective hours when each GFA becomes valid
every time GFA is issued the previous GFA is superseded

## Slide 400: gfaissuanceandvalidity
vfc©
GFA is issued every six hours, with four issuances a day
the issuance, as with any forecast, precedes validity time
GFA is issued before the top of the 0000, 0600, 1200 and 1800 zulu hours, the respective hours when each GFA becomes valid
every time GFA is issued the previous GFA is superseded

## Slide 401: gfaissuance
vfc©
0000Z
0600Z
1200Z
1800Z
1st set
2nd set
3rd set

## Slide 402: gfaIFRoutlook
vfc©
the third clouds and weather chart contains an additional IFR outlook
this will forecast IFR conditions based on the following criteria, for the 12 hour period the 3rd clouds and weather chart represents

## Slide 403
vfc©
gfaexample

## Slide 404: gfaset1
vfc©

## Slide 405: gfaset2
vfc©

## Slide 406: gfaset3
vfc©

## Slide 407: gfaaccessing
vfc©

## Slide 408: gfaamendments
vfc©
one way GFA is amended by SIGMET
SIGMET is a short-term weather advisory to warn pilots of certain potentially hazardous weather phenomena
SIGMET is broadcast on appropriate IFR and VFR ATS frequencies upon receipt

## Slide 409: gfaamendments
vfc©
GFA is also amended by AIRMET
AIRMET is a short-term weather advisory to warn pilots of certain potentially hazardous weather phenomena, not warranting the issuance of SIGMET
SIGMET or AIRMET will be issued for weather occurrence without forecast, or non-occurrence with forecast

## Slide 410: sigmetexample
vfc©
SIGMET
SIGMETS GFACN31
WSCN31 CWEG 131750 SIGMET M4 VALID 131750/132150 CWEG- WTN 25 NM OF LN /4936N12722W/65 S PORT HARDY - /5112N12812W/45 NW PORT HARDY - /5158N12814W/25 SE MCINNES ISLAND. PTCHY SEV MECH/LLWS TURB FCST BLO 040. SOLANDER ISLAND REPD SE60G72KT AT 1700Z. AREA QS. LTL CHG EXPD. END/GFA31/RGH/CMAC-W
WSCN31 CWEG 131633 SIGMET N1 VALID 131635/132035 CWEG- WTN 45 NM OF LN /5206N12448W/25 W PUNTZI MOUNTAIN - /4916N12028W/30 E HOPE. PTCHY SEV LEE WV/MECH TURB FCST BLO 100 DUE STG SWLY WNDS ALF. AREA QS. LTL CHG EXPD. END/1/GFA31/RGH/CMAC-W

## Slide 411: airmet/sigmetaccessing
vfc©

## Slide 412: sigwxmidlevel
vfc©
the significant weather mid-level prognostic chart covers all of Canada
it represents the 700mb to 400mb levels (FL100 to FL240)
they forecast icing, cloud layers of significance, marked mountain waves, FZLVL at 5000’ intervals, surface position and direction of movement of highs, lows, troughs etc.
issued four times per day, 12 hours before validity

## Slide 413: sigwxhighlevel
vfc©
the significant weather high-level prognostic chart is produced by the world area forecast center (WAFC)
it represents from FL250 to FL630
it shows occurring or forecast weather conditions of concern to high level aircraft operations (ie. the jet stream, tropopause height, frontal positions etc.)
issued four times per day, 12 hours before validity

## Slide 414: sigweather
vfc©

## Slide 415: sigweatheraccessing
vfc©

## Slide 416: analyzedchartsanal
vfc©
certain weather parameters in the upper atmosphere are measured on constant pressure level charts
four pressure levels in Canada are recorded: 850mb (5000’), 700mb (10,000’), 500mb (18,000’) and 250mb (34,000’)
they are not forecast charts - they indicate past conditions
issued twice daily at 0000Z and 1200Z

## Slide 417: analyzedchartsanal
vfc©

## Slide 418: analyzedchartsanal
vfc©
analyzed charts represent a common pressure level, not a constant altitude
highs and lows marked on the charts indicate the highest and lowest altitudes of the pressure level in that area
constant pressure level charts are useful as an aircraft flying a constant indicated altitude is flying a constant pressure level
therefore variations in aircraft altitude can de determined based on the contour lines indicated on ANAL charts

## Slide 419: analyzed
vfc©

## Slide 420: analyzedaccessing
vfc©

## Slide 421: notamnoticetoairmen
vfc©
NOTAM are coded messages that describe a change to an aeronautical facility, surface, procedure or hazard
they must be checked before each flight
NOTAM code is standardized in the Canadian Notam Procedures Manual
http://www.navcanada.ca/ContentDefinitionFiles/Publications/NOTAM/NOTAM_Manual_en.pdf

## Slide 422: notamexample
vfc©
110098 CYXX HOPE
CYHE FIRST 1000 FT RWY 07 CLSD, USABLE RWY LEN REMAINING 2960 FT
TIL APRX 1103211900

## Slide 423: notamaccessing
vfc©

## Slide 424: livervrcurrentwind
vfc©
LIVE RVR is a relatively new product created by NAVCANADA which displays current magnetic wind direction and speed at certain airports
this is overlaid on top of an airport diagram so is very intuitive and gives a clear relationship between runway orientation and wind direction
it is updated every 30 seconds

## Slide 425: livervraccessing
vfc©

## Slide 426: awwsexploring
vfc©
the aviation weather website contains much more information than is required to be known for the CPL written test
however it should be explored as much as possible
make sure you are completely versed on the dissemination of any weather product you intend to use for flight planning purposes