Contact Information
- Stephan Heinemann
- SMS: +1 (250) 891-5446
- Email: stephan.heinemann@hotmail.com
- Bookings, Questions

---
Aerodrome Traffic Circuit
- Review Slow Flight and Take-Off
- Definition and Motivation
- Aerodrome Traffic Circuit
- Summary and Questions
- Pre-Flight Briefing

---
Review Slow Flight and Take-Off
- Mentally perform a recovery from slow flight and state all observations and required actions.
- What actions have to be completed before initiating a take-off?
- Describe the take-off phases line-up, run and initial climb.
- What are the criteria for a normal take-off?
- Mentally perform a normal take-off and state all observations and actions.
- What causes wake-turbulence and how does it affect your take-off?
[Speaker Notes: - much shorter review]

---
Definition and Motivation
- Standardized rectangular traffic circuit at aerodromes
- Ordered and organized flow of traffic to avoid conflicts
- Safety and traffic separation, stabilized approaches
- Types: controlled and uncontrolled aerodrome environment
- Applications: portion of a circuit is flown in every single flight

---
Circuit Layout
- Legs: Take-Off, Crosswind, Downwind, Base, Final
- Sides: Upwind and Downwind
- Standard left-hand aerodrome circuit with 1000 ft AAE circuit height
- Standard crosswind and base legs transition between 500 ft and 1000 ft AAE
- Consult Canadian Flight Supplement for specific layout and procedures
- Modifications due to obstacles, noise abatement and operational constraints
[Speaker Notes: - points of interest may not be familiar to the pilot, point out appropriate ATC communication - Upwind (Dead), Downwind (Active) - focus on ground track and wind effect - much more howto, what to do when - downwind checks, airspeed, mixture, carburetor heat, lights, (flaps)]

---
Circuit Procedures
- Climb to 500 ft AAE or as assigned on take-off leg
- Adjust climb airspeed after clearing obstacles as applicable and retract flaps at safe altitude (400 ft AGL)
- Climb to 1000 ft AAE or as assigned on crosswind leg (clear ahead and right)
- Level off (APT) and turn downwind (clear right)
- Perform pre-landing checks and mandatory call on downwind
- Initiate descent (PAT) at 45° or as assigned past abeam threshold (clear right)
- Turn base leg establishing a stabilized appoach at descent airspeed (70 KIAS)
- Set flaps as required on downwind, base and final legs (61-70 KIAS)
- Continue stabilized approach on final leg towards threshold window
- Maintain speed and spot with stable descent rate
- Go around if necessary (traffic, balked landing) and continue in the circuit
- Maintain good lookout for separation: situational awareness
[Speaker Notes: - check positive rate - upwind cockpit checks: climbing one – climbing two - downwind cockpit checks: mags, master, lights, mixture, fuel, seat belts, doors, windows, brakes]

---
Circuit Radio Procedures
- Communication message pattern: Who? Where? What? With?
- Report entry leg as applicable and intentions
- Report downwind leg (standard left or right) and intentions
- Report final leg as applicable and intentions
- Report crossing midfield as applicable and intentions
- Report lost traffic or traffic in sight – advise if unable to follow instructions

---
Controlled Airports
- Control zones with published approach procedures to join circuit
- Standard control zone extends 5 NM radius up to 3000 ft AGL
- Modified circuit procedures and ATC instructions due to traffic situation
- Airspace requirements: weather minima, clearances, equipment

---
Controlled Airports Procedures
8
- Concrete procedures are published in the Candian Flight Supplement
- Instructions are to be followed on towered airports
- Circuit procedures may be modified frequently at busy controlled airports
- Advisories help decision making on non-towered airports
- Maintain constant lookout, traffic separation and sequence
[Speaker Notes: - radio procedures - crossing while joining 500 ft above circuit altitude - actions in the circuit, power, descent, climb... - wind in the circuit and turn anticipation - wind and active runway, PIC final authority - backtracking procedures? runway priority - changing runways]

---
Towered Airports – CYYJ

---
Towered Airports – CYYJ

---
Non-Towered Airports / MF – CYCD
[Speaker Notes: - published night procedures only (used during day time)]

---
Non-Towered Airports / MF – CYCD

---
Uncontrolled Aerodromes / MF or ATF
- Located in uncontrolled airspace (G) and do not necessarily require radio contact, clearances or special equipment
- Mandatory Frequency (MF) versus Aerodrome Traffic Frequency (ATF)
- Own separation and careful lookout required – possible ATF NORDO traffic

---
Uncontrolled Aerodromes Procedures
- Concrete procedures are published in the Canadian Flight Supplement
- Perform standard communications and advise other aircraft of your position and intentions
- Be aware of and lookout for potential ATF NORDO traffic
- Maintain constant lookout, traffic separation and sequence

---
Uncontrolled Aerodromes / ATF – CAM3

---
Circuit Joining Procedures
- Tower Frequency with concrete clearances and instructions
- Mandatory Frequency (MF) with and without advisories (ground station)
- Air Traffic Frequency (ATF) with potential NORDO traffic
- Review Aeronautical Information Manual RAC 4.3-4.5 for unambiguous clarification

---
Transitioning Control Zones
- Crossing requirements depend on airspace structure and ATC entity
- Requirements regarding radio contact, transponder, clearance, routing
- Refer to Terminal Chart and Canadian Flight Supplement procedures
- Control zone versus terminal area recommended transition routes
[Speaker Notes: - circuit transition altitudes (2000 ft AAE)]

---
Special VFR
- Allows to enter a control zone in IMC under day VFR for the purpose of landing at the airport only
- Special VFR has to be requested by the pilot and is not offered by ATC
- Special VFR can be denied due to IFR traffic or operational constraints

---
Summary / Quiz
- Describe the standard circuit with respect to legs, sides, directions and heights.
- What are the three main types of circuit environments and how do they differ?
- Where do you find what particular circuit and procedure applies to an aerodrome?
- Assume you want to join the Nanaimo traffic circuit approaching from Victoria. The ATIS and FSS advisory inform you that the prevailing wind and existing traffic favor runway 34. Mentally perform the procedure and state all observations and required actions.

---
Pre-Flight Briefing
- Exercise
- Training Area
- Departure and Arrival Procedures
- Weather Briefing / NOTAMs
- Aircraft and Documents
- Time and Fuel Requirements
- Safety Considerations and Responsibilities

---
Additional Materials
- Additional materials for the Circuit
- Flight Instructor Guide – Exercise 17, Lesson Plan 2, 8-12

---
VFR Minima

---
NORDO – Visual Signals

---
ATC Circuit Modifications
- ATC may issue instructions to modify the standard circuit pattern at controlled airports
- Use cases include: conflict resolution, traffic separation, wake-turbulence separation, emergencies
- Examples illustrate radio exchanges that lead to circuit pattern modifications

---
Circuit Side Changes after Take-Off
- ATC: “GBMO, (after touch and go) make one right-hand (left-hand) circuit”
- Aircraft: “Make one right-hand (left-hand) circuit, GBMO”
- ATC: “GBMO, (after touch and go), resume left-hand (right-hand) circuits”
- Aircraft: “Resume left-hand (right-hand) circuits, GBMO”

---
Circuit Side Changes from Downwind
- ATC: “GBMO, make a left-turn, cross midfield, join right downwind runway 27”
- Aircraft: “Make a left-turn, cross midfield, join right downwind runway 27, GBMO”
- ATC: “GBMO, make a left turn, cross threshold runway 27, join right downwind runway 27”
- Aircraft: “Make a left turn, cross threshold runway 27, join right downwind runway 27, GBMO”

---
Leg Extensions after Take-Off
- ATC: “GBMO, climb runway heading 1000' before turning crosswind”
- Aircaft: “Climb runway heading 1000' before turning crosswind, GBMO”
- ATC: “GBMO, maintain runway heading, I call your crosswind”
- Aircraft: “Maintain runway heading, you call my crosswind, GBMO”

---
Leg Extensions from Downwind
- ATC: “GBMO, extend downwind, I call your base”
- Aircraft: “Extend downwind, you call my base, GBMO”
- ATC: “GBMO, extend downwind, you are number 4, follow traffic ahead”
- Aircraft: “Extend downwind, number 4, follow traffic ahead – in sight, GBMO”

---
Orbits
- ATC: “GBMO, make one left-hand (right-hand) orbit, re-join downwind”
- Aircraft: “Make one left-hand (right-hand) orbit, re-join downwind, GBMO”
- Aircraft: “GBMO, orbit complete”
- ATC: “GBMO, enter a left-hand (right-hand) orbit”
- Aircraft: “Enter a left-hand (right-hand) orbit, GBMO”

---
Wake-Turbulence Avoidance
- ATC: “GBMO, maintain 1000' and overfly runway”
- Aircraft: “Maintain 1000' and overfly runway, GBMO”
- ATC: “GBMO, due to wake-turbulence, low approach only, not below 500'”
- Aircraft: “Low approach only, not below 500', GBMO”
- ATC: “GBMO, turn early crosswind when safe”
- Aircraft: “Turn early crosswind when safe, GBMO”
- Aircraft: “GBMO, request early crosswind”
- ATC: “GBMO, early crosswind approved”

---
Runway Changes
- ATC: “GBMO, runway change, join downwind runway 21”
- Aircraft: “Join downwind runway 21, GBMO”
- ATC: “GBMO, runway change, continue left turn, cross midfield, join downwind runway 09, GBMO”
- Aircraft: “Continue left-turn, cross midfield, join downwind runway 09, GBMO”
- ATC: “GBMO, runway change, make a right turn, cross threshold 09, join right downwind 27”
- Aircraft: “Make a right turn, threshold 09, join right downwind 27, GBMO”