Contact Information
- Stephan Heinemann
- SMS: +1 (250) 891-5446
- Email: stephan.heinemann@hotmail.com
- Bookings, Questions

---
Forced Landing
- Review Descent, Approach and Landing
- Definition and Motivation
- Forced Landing
- Summary and Questions
- Pre-Flight Briefing

---
Review Descent, Approach and Landing
- Mentally perform a power-off descent and state all observations and required actions.
- What is the best glide airspeed and where do we find it?
- How do we visually determine our glide distance?
- What types of landing can we perform?
- Mentally perform a soft-field landing and state all observations and required actions.
[Speaker Notes: - remove soft-field landing question]

---
Definition and Motivation
- Unplanned landing due to failure or other emergency
- Aviate, Navigate, Communicate, Manage
- Continue to fly the airplane has highest priority
- Situations: engine failure (mechanical, oil supply, fuel supply – contamination, air supply – icing, blockage)

---
Engine Failure During Take-Off
Power Idle
Apply Brakes
Best Glide
Avoid Obstacles
- During Take-Off Run: power idle, apply brakes
- Immediately after Take-Off: best glide airspeed (68 KIAS), avoid obstacles
[Speaker Notes: - V1, TODA, ASDA? - if time permits: Fuel Valve Off, Mixture Off, Ignition Off, Master Off - attitude versus 68 KIAS (focus on attitude)]

---
Engine Failure at Low Altitude
- Establish best glide (68 KIAS) and trim
- Select and head towards suitable field
- Seats, Seatbelts, Cockpit Hazards
- Fuel Valve - Off, Mixture - Off, Ignition - Off
- Mayday, Squawk 7700, ELT On
- Flaps as required
- Master - Off, Doors – Unlatch
- MEMORIZE THIS PROCEDURE!
[Speaker Notes: - focus more on attitude → establish glide speed attitude - key words at the beginning - brace, brace, brace vs. seats, seatbelts, hazards - below 500, above 500, above 1000]

---
Engine Failure at Safe Altitude
- Establish best glide (68 KIAS) and trim
- Select and head towards suitable field
- Cause check (Fuel Valve, Fuel Selector, Mixture, Throttle, Engine Instruments, Fuel Pump, Magnetos, Primer)
- Attempt restart
- If restart not successful, continue with low altitude procedures
- MEMORIZE THIS PROCEDURE!
[Speaker Notes: - Carburettor heat if equipped - Alternate air door automatically opens due to suction - Causes: Mechanical, Fuel, Oil, Icing - Safe Altitude: 2000' AGL? - primer versus fuel injected engine (remove primer) - cause check order POH]

---
Restart Procedure
- Fuel Valve – On
- Fuel Selector – Both
- Mixture – Full Rich
- Fuel Pump – On
- Ignition – Start
- Fuel Pump – Off (Consider On)

---
Engine Failure in Circuit
- Perform power-off landing if at circuit altitude
- Manage energy / airspeed and plan for each leg to final
- Consider altitude, rate of descent and wind
- Inform ATC (request clearance beforehand if practicing)
[Speaker Notes: - focus on key position and where it is - 45° left wing perspective - 1 ½ NM back on final at 1000' AGL - figure of eights, visual estimate - explain radius of action - remove v-speeds]

---
Forced Landing Approach
- Establish key points
- Organize legs
- Consider altitude, rate of descent and wind
- Approach slightly high and attempt to land in first third of the selected field
- Use flaps and slipping to increase rate of descent
[Speaker Notes: - head directly to key point instead of circuit]

---
360° Forced Landing Pattern
- Proceed to selected key point at altitude – high key
- Descend to lower altitude circling – low key
- Initiate final approach from low key point
[Speaker Notes: - remove spiral, try to get original FTM pictures]

---
Distress Communication
- Current frequency or 121.5
- Mayday, Mayday, Mayday
- 3 x Callsign
- Position, Altitude
- Problem
- Intentions
- Callsign
- Squawk 7700, ELT On
[Speaker Notes: - can be abbreviated, more important to make the field]

---
Hills, Mountains, Forest, Water
- Hills / Mountains: land uphill
- Forest: assume tree tops as landing surface
- Roads (traffic, power lines, obstructions)
- Water: ditching and evacuation – swell, wind

---
Safety Considerations
- Remain clear of obstacles
- Clear engine every 1000'
- Go around at 500' AGL (1000' over civilization)
[Speaker Notes: - 500' AGL minimum? - 1000' AGL VFC]

---
Summary / Quiz
- What situations may lead to a forced landing?
- How does altitude affect the type of forced landing?
- Mentally perform a forced landing from a safe altitude within farmland countryside.
- Simulate a Mayday call reporting an engine failure and state your intentions.
- What other means of communication are available in an emergency?
[Speaker Notes: - mentally perform is probably to much - maybe aviate, communicate, … - maybe the first one or two steps...]

---
Pre-Flight Briefing
- Exercise
- Training Area
- Departure and Arrival Procedures
- Weather Briefing / NOTAMs
- Aircraft and Documents
- Time and Fuel Requirements
- Safety Considerations and Responsibilities

---
Forced Landing (Ex. 22, LP. 24)
- Objective
- Review
- Motivation
- Howto
- Summary / Questions
- Preflight Briefing