Contact Information
- Stephan Heinemann
- SMS: +1 (250) 891-5446
- Email: stephan.heinemann@hotmail.com
- Bookings, Questions

---
Flight for Range and Endurance
- Definition and Motivation
- Flight for Range
  - Diagrams
  - Maximum Range (Derived and Experimental)
- Flight for Endurance
  - Diagrams
  - Maximum Endurance (Derived and Experimental)
[Speaker Notes: - gear and carbutettor heat are not applicable]

---
Review Straight and Level Flight
- Attitude plus power equals performance!
- Mentally perform a power reduction from the cruise power setting while maintaining straight and level flight.
- What effect does the power reduction have on the airspeed and the fuel consumption?
- What effect does the power reduction have on the estimated time of arrival?
[Speaker Notes: Until what point can the power be reduced while maintaining straight and level flight?]

---
Definition and Motivation
- Airspeed and fuel flow can be traded off
- Range – achievable distance per fuel unit (air/ground range): destinations, alternates
- Maximum range – best achievable distance
- Endurance – achievable time per fuel unit: holding procedures, cockpit management / decision making, economy
- Maximum endurance – best achievable time
[Speaker Notes: SFC = FF / BHP = FF n / Pa]

---
Flight for Range
Factors: power setting, fuel available, angle of attack, airspeed, weight, centre of gravity, altitude, mixture, wind
[Speaker Notes: - Experimental Method - POH - Wind, Mixture, Altitude (Factors)]

---
    Range Profile
- Consider conditions
- Select pressure altitude
- Select power setting
- Determine range
[Speaker Notes: - Notice almost linear dependency between power setting and airspeed - Linear dependency will eventually change to a much lower airspeed for a lower power setting]

---
        Cruise Performance
- Consider conditions
- Select pressure altitude
- Select temperature
- Select power settting
- Interpolate as required
- Determine airspeed and fuel flow

---
Flight for Maximum Range (Experimental)
- Reduce power in 100 RPM steps until a non-linear decrease in airspeed can be observed
- Maintain level flight, trim and lean mixture as recommended (rich of peak)
[Speaker Notes: - can be increased in 100 RPM steps as well - approximately 2000 RPM for max. range Familarization Demo - 2000 RPM → 5 GPH → 100 KIAS 30 USG → 6 H → 600 NM - 2400 RPM → 10 GPH → 120 KIAS 30 USG → 3 H → 360 NM]

---
Range – Instruments
Performance
Control
Altitude
Attitude
Power
Airspeed
Throttle
Mixture
EGT / FF
- Attitude, Power → Airspeed (about 70-80 KIAS), Altitude
- Mixture → Exaust Gas Temperature, Fuel Flow

---
Flight for Endurance
Factors: power setting, fuel available, angle of attack, airspeed, weight, centre of gravity, altitude, mixture, turbulence
[Speaker Notes: - Experimental Method - POH - Mixture, Flaps, Altitude (Factors → Turbulence) - Reduced Control Response - SL for reciprocating engines (air density)]

---
        Endurance Profile
- Consider conditions
- Select pressure altitude
- Select power
- Determine endurance

---
Flight for Maximum Endurance (Experimental)
- Reduce power in 100 RPM steps maintaining level flight with stable airspeed and trim
- Unstable decreasing airspeed indicates slow flight range – more power required
- Reset cruise power and then decrease power to slightly higher stable setting to compensate for turbulence and required turns
- Lean mixture as recommended
- Notice reduced control responses
[Speaker Notes: www.eaa1000.av.org/technicl/perfspds/perfspds.htm - approximately 1700 RPM for max. endurance Familarization Demo ? - 1700 RPM → 3 GPH → 80 KIAS 30 USG → 10 H → 800 NM]

---
Endurance - Instruments
Performance
Control
Altitude
Attitude
Power
Airspeed
Throttle
EGT / FF
Mixture
- Attitude, Power → Airspeed (about 50-60 KIAS), Altitude
- Mixture → Exaust Gas Temperature, Fuel Flow
[Speaker Notes: www.eaa1000.av.org/technicl/perfspds/perfspds.htm]

---
Summary / Quiz
- Define range, maximum range, endurance and maximum endurance.
- Give examples for when flight for range or endurance is preferrable.
- What are the main factors that influence range and endurance and how do they affect them?
- Mentally configure the airplane for best range and endurance and state all required actions, respectively.

---
Pre-Flight Briefing

---
Flight for Maximum Range (Derived)
- Reduce power to establish best glide airspeed
- Maintain level flight and trim accordingly
- Lean mixture as recommended (rich of peak)
[Speaker Notes: Experimental: ground references during glide]

---
Flight for Maximum Endurance (Derived)
- Reduce power to lowest setting (above slow flight) to maintain altitude (about best glide / 1.3 = 52 KIAS)
- Maintain level flight and trim accordingly
- Lean mixture as recommended (rich of peak)