Contact Information
- Stephan Heinemann
- SMS: +1 (250) 891-5446
- Email: stephan.heinemann@hotmail.com
- Bookings, Questions

---
Aerodrome Traffic Circuit
- Review Slow Flight and Take-Off
- Definition and Motivation
- Aerodrome Traffic Circuit
- Summary and Questions
- Pre-Flight Briefing

---
Review Slow Flight and Take-Off
- Mentally perform a recovery from slow flight and state all observations and required actions.
- What actions have to be completed before initiating a take-off?
- Describe the take-off phases line-up, run and initial climb.
- What are the criteria for a normal take-off?
- Mentally perform a normal take-off and state all observations and actions.
- What causes wake-turbulence and how does it affect your take-off?
[Speaker Notes: - much shorter review]

---
Definition and Motivation
- Standardized rectangular traffic circuit at aerodromes
- Ordered and organized flow of traffic to avoid conflicts
- Safety and traffic separation, stabilized approaches
- Types: controlled and uncontrolled aerodrome circuit
- Applications: portion of a circuit is flown in every single flight

---
Circuit Layout
- Legs: Take-Off, Crosswind, Downwind, Base, Final
- Sides: Upwind and Downwind
- Standard left-hand aerodrome circuit with 1000' AAE circuit height
- Standard crosswind and base legs transition between 500' and 1000' AAE
- Consult Canadian Flight Supplement for specific layout and procedures
- Modifications due to obstacles, noise abatement and points of interest
[Speaker Notes: - points of interest may not be familiar to the pilot, point out appropriate ATC communication - Upwind (Dead), Downwind (Active) - focus on ground track and wind effect - much more howto, what to do when - downwind checks, airspeed, mixture, carburetor heat, lights, (flaps)]

---
Circuit Procedures
- Climb to 500' AAE or as assigned on upwind leg
- Transition to Vy and perform cockpit checks (flaps up)
- Climb to 1000' AAE or as assigned on crosswind leg
- Perform cockpit checks on downwind (switches)
- Turn base leg at 45° or as assigned past threshold
- Configure for landing on downwind and final legs
- Establish stabilized approach on final leg
- Maintain speed and spot with stable descent rate
- Go around if necessary
- Maintain lookout and separation: situational awareness
[Speaker Notes: - check positive rate - upwind cockpit checks: climbing one – climbing two - downwind cockpit checks: master, lights]

---
Circuit Radio Procedures and SOPs
- Report entry leg
- Report downwind leg (standard left or right) and intentions
- Perform downwind leg midfield checks
- Report final leg – check final items
- Assure clearances for landings and deviations or exercises if required in the environment

---
Controlled Airports
- Control zones with traffic patterns to join circuit
- Standard control zone extends 5 NM radius up to 3000' AGL
- Airspace requirements: weather minima, communication, clearances, equipment

---
Controlled Airports Procedures
- Concrete procedures are described in the CFS
- Instructions are to be followed on towered airports
- Advisories help decision making on non-towered airports
- Maintain constant lookout, separation and order
[Speaker Notes: - radio procedures - crossing altitude 500' above circuit altitude - actions in the circuit, power, descent, climb... - wind in the circuit and turn anticipation - wind and active runway, PIC final authority - backtracking procedures? runway priority - changing runways]

---
Towered Airports (CYYJ)

---
Towered Airports (CYYJ)

---
Non-Towered Airports / MF (CYCD)
[Speaker Notes: - published night procedures only (used during day time)]

---
Non-Towered Airports / MF (CYCD)

---
Uncontrolled Aerodromes
- Located in uncontrolled airspace (G)
- Airspace does not require radio contact, clearances or special equipment

---
Uncontrolled Aerodromes Procedures
- Concrete procedures are described in the CFS
- Advise other aircraft of your position and intentions
- Be aware of and lookout for potential NORDO traffic
- Maintain constant lookout, separation and order

---
Uncontrolled Aerodromes / ATF (CAM3)

---
Crossing Control Zones
- Crossing requirements depend on airspace structure
- Radio contact, transponder, clearance, routing
- Refer to Terminal Chart and CFS procedures

---
Special VFR
- Allows to enter a control zone in IMC under VFR
- Special VFR has to be requested by the pilot
- Special VFR can be denied due to IFR traffic

---
Summary / Quiz
- What are the two main types of circuits and how do they differ?
- Describe the standard circuit with respect to legs, sides, directions and heights.
- Where do you find what particular circuit and procedure applies to an aerodrome?
- Assume you want to join the Nanaimo traffic circuit approaching from Victoria. The ATIS informs you that the weather is VFR and the active runway is 34. Mentally perform the procedure and state all observations and required actions.

---
VFR Minima

---
Pre-Flight Briefing
- Exercise
- Training Area
- Departure and Arrival Procedures
- Weather Briefing / NOTAMs
- Aircraft and Documents
- Time and Fuel Requirements
- Safety Considerations and Responsibilities

---
Pre-Flight Briefing
- Exercise
- Training Area
- Departure and Arrival Procedures
- Weather Briefing / NOTAMs
- Aircraft and Documents
- Time and Fuel Requirements
- Safety Considerations and Responsibilities

---
The Circuit (Ex. 17, LP. 3-10, 20)
- Objective
- Review
- Motivation
- Howto
- Summary / Questions
- Preflight Briefing

---
Terminal and Transition Airspace